## Slide 1: Computer Arch. & AI Chip Lecture 15: Flash Attention
Prof. Zeke Wang
Zhejiang University
June 1 2026

## Slide 2: Outline
Zero
FlashAttention

## Slide 3: AI System: Four Components
Networking
Storage
Computing
Model
Training
Compiling

## Slide 4: AI System: Storage

## Slide 5: ZeRO: Zero Redundancy Optimizer
Key Idea:
  Each GPU stores a subset of optimizer states, rather than the whole states like data parallel.

## Slide 6: ZeRO: Zero Redundancy Optimizer
Benefit:
  Training a larger model.

## Slide 7: Overhead of ZeRO: More Communication
Typical PyTorch step:
Forward:
Backward:
Optimizer:
Overhead: more collectives

## Slide 8: Summary
Networks and dataset are getting larger to set new state of art results
Scale-out enables these neural networks to be trained
Success requires many optimized components:
  Hardware:
    Fast accelerators for DL
    High-bandwidth, low-latency interconnects
      Topologies matter (must match communication patterns)
      Network switches with math capabilities free up DL accelerators to do compute
      SmartNIC for offloaded compression/decompression
  Software:
    Math libraries (CUDNN, CUBLAS, MKL, CANN …)
    Collective communication libraries (NCCL, Horovod, …)
    Training frameworks (MindSpore, PyTorch, TensoFlow, HugeCTR, …)
  Proper choice of parallelism (manual, MeshTensorFlow, Gshard, ZeRO)

## Slide 9: Batch Size Limitation of LLM Training
Batch Size Limitation of LLM Training
  Llama: 4M token,
    Seq length: 4K,
    Batch size: 1K
How to choose the parallel training strategy?
  When you have 1K NPU/GPU?
  When you have 10K NPU/GPU?

## Slide 10: Outline
Zero
FlashAttention

## Slide 11: Why FlashAttention？
Why FlashAttention？
  Normal attention is bound by IO
  GPU utilization is low
Notes: 这里只有在第三步是实实在在的计算动作，其余步骤都是在为计算做准备工作。
在性能优化工作中，宏观角度通常是通过更好的算法、数学方法来减少总计算量。
而在微观角度上，则是尽可能的使处理器的计算单元“忙”起来，即增大计算单元的计算时间占总运行时间的比重。

## Slide 12: Naïve Attention
Naïve Attention O = Softmax(QKT) V
  1, A = QKT A: Load Q K from HBM, compute A, write A to HBM
  2, A = Softmax (A) : Load A from HBM, compute A, write A to HBM
  3, O = AV: Load A V from HBM, compute O, write O to HBM
Q
(S x D)
A = softmax(A)
(S x S)
V
(S x D)
O = AV
(S x D)
A = QKT
(S x S)
K
(S x D)

## Slide 13: Two Issues of Naïve Attention
Q
(S x D)
A = softmax(A)
(S x S)
V
(S x D)
O = AV
(S x D)
A = QKT
(S x S)
K
(S x D)
Two Issues of Naïve Attention
  Large intermediate results O(S2) with a long sequence
  Repeated reads/writes from GPU device memory

## Slide 14: Two Challenges of Naïve Attention
Q
(S x D)
A = softmax(A)
(S x S)
V
(S x D)
O = AV
(S x D)
A = QKT
(S x S)
K
(S x D)
Two Challenges of Naïve Attention
                Low precision of the fp16 elements of A easily overflow
     Safe Softmax
  A = softmax(A) is not a streaming algorithm
     Online Softmax

## Slide 15: Softmax  Safe Softmax
{
Given a row of {x1, x2, …, xN}), Softmax({x1, x2, …, xN}) =
{
Softmax
                Issue: can overflow
     fp16: 65536
Safe Softmax
                m = (xj): maxi. value
                Exponential operator is accurate for negative inputs

## Slide 16: Details of Safe Softmax
Goal: Given a row of {x1, x2, …, xN}), Softmax({x1, x2, …, xN}) = ({a1, a2, …, aN})
3-pass Safe Softmax
                1, calculating the maxi. value mN
    for i = 1, ..., N do
    mi = max(mi-1, xi)
                2, calculating the sum sumN
    for i = 1, …, N do
    sumi = sumi-1 +
                3, calculating the final ai
    for i = 1, …, N do
    ai =

## Slide 17: Details of Online Softmax
Goal: Given a row of {x1, x2, …, xN}), Softmax({x1, x2, …, xN}) = ({a1, a2, …, aN})
2-pass Online Softmax
                1, calculating the sum sumN and the maxi. value mN
    for i = 1, ..., N do
    mi = max(mi-1, xi)
                sumi = +
                = ( +
                = sumi-1 * +
                2, calculating the final ai
    for i = 1, …, N do
    ai =

## Slide 18: FlashAttention -1
Two key ideas of FlashAttention-1
                1, Tiling: Compute the attention weights block by block so that we don’t have to load everything into SRAM at once
                2, Recomputation: don’t ever store the full attention matrix, but just recompute the parts of it you need during the backward pass

## Slide 19: FlashAttention -1
Inter-Tile: parallelize over batch size and heads  low parallelism
Intra-Tile:  extra access to HBM from O
  Outer loop: K V
  Inner loop: Q
Outer loop
Inner loop

## Slide 20: FlashAttention -2
Inter-Tile: parallelize over Q and batch size  high parallelism
Intra-Tile:  no extra access to HBM from O
  Outer loop: Q
  Inner loop: K V
Outer loop
Inner loop

## Slide 21: FlashAttention -2
Inter-Tile: parallelize over Q and batch size  high parallelism
Intra-Tile:  no extra access to HBM from O
  Outer loop: Q
  Inner loop: K V
One thread block
for a subset of Q
Iterate over K and V
Accumulate to O

## Slide 22: FlashAttention -3
Two key ideas of FlashAttention-3
  Optimized for Hopper GPU
                1, Warp Specialization: producer consumer model
                2, Intra-warpgroup overlapping: overlap softmax and GEMM
Issues of FlashAttention-2
                Serial Execution of GEMM, softmax, and HBM
                Low GPU utilizaton

## Slide 23: Producer and Consumer Model
One key idea of FlashAttention-3
                1, Warp Specialization: producer consumer model
    Due to async memory access (DMA)

## Slide 24: Intra-warpgroup overlapping
One key idea of FlashAttention-3
                Intra-warpgroup overlapping: overlap softmax and GEMM

## Slide 25: FlashAttention -3
Real Mapping of FlashAttention-3
                Epilogue is softmax

## Slide 26: FlashAttention -4
Two key ideas of FlashAttention-4
  Goal: Optimized for Blackwell GPU
                1, Deeper Warp Specialization
Issues of FlashAttention-2
                Unaware of Blackwell GPU

## Slide 27: 算子融合-PyTorch版Attention
Notes: 这里只有在第三步是实实在在的计算动作，其余步骤都是在为计算做准备工作。
在性能优化工作中，宏观角度通常是通过更好的算法、数学方法来减少总计算量。
而在微观角度上，则是尽可能的使处理器的计算单元“忙”起来，即增大计算单元的计算时间占总运行时间的比重。