## Slide 1: Computer Arch. & AI Chip Lecture 2: Pipeline Hazard + Reorder Buffer
Prof. Zeke Wang
Zhejiang University
09 March 2026

## Slide 2: Recall: Axiom
To achieve the highest energy efficiency and performance:
we must take the expanded view
of LLM system
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Co-design across the hierarchy:
Algorithms to devices
Specialize as much as possible
within the design goals

## Slide 3: Recall: Amdahl’s Law
Amdahl’s Law
  f: Parallelizable fraction of a program
  N: Number of processors
Serial bottleneck of Amdahl’s Law:
  Maximum speedup (1/(1-f)) limited by serial portion (1 - f)
Parallel portion (f) is usually not perfectly parallel
  Synchronization overhead (e.g., updates to shared data)
  Load imbalance overhead (imperfect parallelization)
  Resource sharing overhead (contention among N processors)
Speedup =
1
+
1 - f
f
N
  Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” 1967.

## Slide 4: Recall: Key Term in Roofline Model
Arithmetic intensity (AI)
  Definition: AI = Total Flops / Total Memory Bytes
  Arithmetic intensity describes the characteristics of a compute kernel running on a given processor
    Large AI  Compute-bound
    Small AI  Memory-bound
9
      Williams, Waterman, Patterson, “Roofline: An Insightful Visual Performance Model for Multicore Architectures”, CACM, 2009
Notes: All these works rely on many different methodology's to identify memory bottlenecks in a system. Often, such methodologies are intuitively used as a indication of NDP suitability for a given application
[CLICK] However, as I will show next, none of those models are comprehensive enough to identify memory bottlenecks and NDP suitability. This happens because these models are built targeting to identify specific sources of data movement bottlenecks, and often their definitions of compute and memory bound are not enough to indicate NDP suitability.
[CLICK] For that, we will analyze two commonly used approaches: the roofline model, which correlates the arithmetic intensity of an application with performance,
[CLICK] and identifying application that has high misses-per-kilo instructions or MPKI.
[NEXT]

## Slide 5: Recall: Roofline Model’s 3 Steps
Roofline model’s 3 Steps:
  1, Machine characterization:
    Memory bandwidth,
    Peak compute;
  2, Application Characterization:
    Arithmetic intensity;
  3, Application execution monitoring:
    Real Throughput
9
      Williams, Waterman, Patterson, “Roofline: An Insightful Visual Performance Model for Multicore Architectures”, CACM, 2009
Notes: All these works rely on many different methodology's to identify memory bottlenecks in a system. Often, such methodologies are intuitively used as a indication of NDP suitability for a given application
[CLICK] However, as I will show next, none of those models are comprehensive enough to identify memory bottlenecks and NDP suitability. This happens because these models are built targeting to identify specific sources of data movement bottlenecks, and often their definitions of compute and memory bound are not enough to indicate NDP suitability.
[CLICK] For that, we will analyze two commonly used approaches: the roofline model, which correlates the arithmetic intensity of an application with performance,
[CLICK] and identifying application that has high misses-per-kilo instructions or MPKI.
[NEXT]

## Slide 6: Recall: Little’s Law：Intuition
Image the services provided by counters in the bank.
  Arrival rate: one customer/min;
  Counter’s average serve time: 6 mins;
  Question: how many counters are needed for people who need the service? (Cond: The customer will leave if no counter is available. )
  Answer: 6 counters (one slot for one person, then no customer will leave).
How many Counters?
Arrival rate: one person/min
Average service time: 6 mins
Notes: 这里server不太合理

## Slide 7: Recall: Little’s Law Used in Memory Subsystem
Little’s law is widely used in hardware design whose latency is larger than one cycle, e.g., memory subsystem:
  Throughput: 12GB/s;
  Latency: 100ns;
  Buffer Size (concurrency):
    100ns * 12GB/s = 1200B
Memory
Throughput: 12GB/s
Latency: ~100ns
Buffer
Concurrency = Latency * Throughput

## Slide 8: Recall von Neumann Model: Key Properties
Von Neumann model is also called stored program computer (instructions in memory).
von Neumann Model has two key properties:
  1，Stored program
    Instructions stored in a linear memory array
    Memory is unified between instructions and data
      The interpretation of a stored value depends on the control signals
  2，Sequential instruction processing
    One instruction processed (fetched, executed, completed) at a time
    Program counter (instruction pointer) identifies the current instruction
    Program counter is advanced sequentially except for control transfer instructions
Notes: Every application can be descripted by this complete design von Neumann

## Slide 9: Where Are We?

## Slide 10: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 11: Pipeline hazards
A hazard is a condition that prevents an instruction in the pipeline from executing its next scheduled pipeline stage.
Taxonomy of hazard:
  Structural hazards
    Conflict due to limited hardware resources
  Data hazards
    Instruction depends on result of a prior instruction which is not ready (computed or stored) yet
  Control hazards
    Not able to fetch the next instruction for the next clock due to unsolved branch condition or unavailable branch.

## Slide 12: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 13: Structural hazard
Structural hazard
  Reason: Occurs when two or more instructions try to use the same hardware resource in the same cycle.
  Outcome: Causes bubble (stall) in a pipelined CPU.
  Solution: Can be overcome by replicating hardware resources
    Multiple accesses to the register file
    Multiple accesses to memory
    Fully pipeline the functional unit

## Slide 14: Structural Hazard: Multi Ports of Register File
Condition of Register file to avoid structural hazard?
  Allows concurrently two reads and one write to avoid structural hazard regarding register file.
Notes: 下面，从寄存器文件来说结构冲突：多少个读口，多少个写口才能解决冲突？
答案：两个读口 一个写口
Generalization：硬件设计需要满足最坏的情况

## Slide 15: Instruction and Data Memory Ports Split
Structural hazard regarding memory?
  Solution: Split instruction and data memory
    Fetch the instruction and data using different memory ports, rather than contenting for the same port.
IM
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
Reg
DM
Reg

## Slide 16: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 17: Data Dependences
Three Types of data dependences
  Flow dependence (read after write – true data dependence)
  Output dependence (write after write)
  Anti dependence (write after read)
Which ones cause stalls in a pipelined machine?
  Assumption: we need to ensure semantics of the program is correct.
  Flow dependences always need to be obeyed because they constitute true dependence on a register
  Anti and output dependences exist due to limited number of architectural registers.
    Essentially, insns are dependent on a name, not a value.

## Slide 18: Data Dependence Types
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7

## Slide 19: How to Handle Data Dependences
Anti and output dependences
  They are easier to handle.
  Write to the destination only in last stage and in program order
Handling flow dependences:
  Hardware Pipeline Stall:
    Detect and wait until value is available in register file
  Software Pipeline Stall:
    Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Data Forward/Bypass:
    Detect and forward/bypass data to dependent instruction

## Slide 20: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
    RAW
    WAW
    WAR
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 21: Remember: Data Dependence Types
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7

## Slide 22: RAW Data Dependence: Example
One instruction writes a register ($s0) and next instructions read this register => read after write (RAW) dependence.
  add writes into $s0 in the first half of cycle 5
  and reads $s0 on cycle 3, obtaining the wrong value
  or reads $s0 on cycle 4, again obtaining the wrong value
  sub reads $s0 in 2nd half of cycle 5, getting the correct value
  subsequent instructions read the correct value of $s0
Only if the pipeline handles
data dependences incorrectly!

## Slide 23: How to Handle Data Dependences
Anti and output dependences
  They are easier to handle.
  Write to the destination only in last stage and in program order
Handling flow dependences:
  Hardware Pipeline Stall:
    Detect and wait until value is available in register file
  Software Pipeline Stall:
    Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Data Forward/Bypass:
    Detect and forward/bypass data to dependent instruction

## Slide 24: Hardware Pipeline Stall for Flow Dependency
The simplest way to "fix" flow dependency is to stall the pipeline.
A pipeline stall, called a pipeline bubble or simply bubble.
What does a pipeline stall do to:
  Previous instructions: go on proceeding in the pipeline.
  Following instructions: stalled in the pipeline by one or more clock cycles until the waiting register is ready.
  New instructions: Not fetched during a pipeline stall.

## Slide 25: Hardware Pipeline Stall: An Example
Issue: dependency regarding register ra
Solution: hardware pipeline stalls the second insn until the first insn. writes the latest value of ra back.
MEM
WB
IF
ID
IF
EX
ID
MEM
EX
WB
addi ra r- -
subi r- ra -
MEM
IF
ID
EX
IF
ID
EX
IF
ID
IF
subi r- ra -
subi r- ra -
subi r- ra -
subi r- ra -
?

## Slide 26: Pipeline Stall: Resolving Data Dependence
IF
WB
IF
ID
ALU
MEM
IF
ID
ALU
MEM
IF
ID
ALU
MEM
IF
ID
ALU
t0
t1
t2
t3
t4
t5
IF
ID
MEM
IF
ID
ALU
IF
ID
Insti
Instj
Instk
Instl
WB
WB
i: rx  _
j: _  rx dist(i,j)=1
i
j
Insth
WB
MEM
ALU
i: rx  _
bubble
j: _  rx dist(i,j)=2
WB
IF
ID
ALU
MEM
IF
ID
ALU
MEM
IF
ID
ALU
MEM
IF
ID
ALU
t0
t1
t2
t3
t4
t5
MEM
Insti
Instj
Instk
Instl
WB
WB
i
j
Insth
ID
IF
IF
IF
ID
ALU
IF
ID
i: rx  _
bubble
bubble
j: _  rx dist(i,j)=3
IF
IF
ID
ALU
MEM
IF
ID
ALU
MEM
IF
ID
ALU
IF
ID
t0
t1
t2
t3
t4
t5
IF
MEM
ALU
ID
Insti
Instj
Instk
Instl
WB
WB
i
j
Insth
ID
IF
ID
IF
i: rx  _
bubble
bubble
bubble
j: _  rx dist(i,j)=4
IF
IF
ID
ALU
MEM
IF
ID
ALU
MEM
IF
ID
IF
t0
t1
t2
t3
t4
t5
ALU
ID
Insti
Instj
Instk
Instl
WB
WB
i
j
Insth
ID
IF
ID
IF
ID
IF
Pipeline stall = make the dependent instruction
wait until its source data value is available.
1. stop all up-stream stages,
2. drain all down-stream stages.

## Slide 27: How to Implement Stalling in Pipeline?
Pipeline stalling:
  Disables PC and IF/ID latching; ensure stalled instruction stays in its stage
  Pushs a bubble into next stage: Bubble = 1 and disables control signal Wreg and Wmem; Puch a nop forward into ID/EX.
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 28: Hardware Needed for Stalling
Stalls are supported by the following hardware:
  adding enable inputs (EN) to the Fetch and Decode pipeline registers
  and a synchronous reset/clear (CLR) input to the Execute pipeline register
    or an INV bit associated with each pipeline register, indicating that contents are INValid
When a lw stall occurs
  StallD and StallF are asserted to force the Decode and Fetch stage pipeline registers to hold their old values.
  FlushE is also asserted to clear the contents of the Execute stage pipeline register, introducing a bubble

## Slide 29: Stalling and Dependence Detection Hardware

## Slide 30: How to Handle Data Dependences
Anti and output dependences
  They are easier to handle.
  Write to the destination only in last stage and in program order
Handling flow dependences:
  Hardware Pipeline Stall:
    Detect and wait until value is available in register file
  Software Pipeline Stall:
    Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Data Forward/Bypass:
    Detect and forward/bypass data to dependent instruction

## Slide 31: Compile-Time Detection and Elimination
Insert enough NOPs for the required result to be ready
Or (if you can) move independent useful instructions up
  Reorder/reschedule instructions at the compiler level

## Slide 32
What is the issue of issuing NOPs from the compiler?
Insn’s latency varies, based on the context.
Notes: The majority of you will not work on Systems.
But you should know the key principles that help you understand the system on which your AI task runs.
Our course has to include both computer architecture and AI chip courses.

## Slide 33: More on Software vs. Hardware
Software based scheduling of instructions  static scheduling
  Compiler orders the instructions, hardware executes them in that order
  Contrast this with dynamic scheduling (in which hardware can execute instructions out of the compiler-specified order)
  How does the compiler know the latency of each instruction?
What information does the compiler not know that makes static scheduling difficult?
  Answer: Anything that is determined at run time
    Variable-length operation latency, memory addr, branch direction
How can the compiler alleviate this (i.e., estimate the unknown)?
  Answer: Profiling

## Slide 34: How to Handle Data Dependences
Anti and output dependences
  They are easier to handle.
  Write to the destination only in last stage and in program order
Handling flow dependences:
  Hardware Pipeline Stall:
    Detect and wait until value is available in register file
  Software Pipeline Stall:
    Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Data Forward/Bypass:
    Detect and forward/bypass data to dependent instruction

## Slide 35: Data Forwarding
Data Forwarding (called Data Bypassing)
  Forwards the result value to the dependent instruction as soon as the value is available.
Act like Dataflow?
  Data value supplied to dependent instruction as soon as it is available.
  Instruction executes when all its operands are available.
Data forwarding brings a pipeline closer to dataflow execution principles.

## Slide 36: Data Forwarding
Notes: 关于s0 有依赖。。。第一条写，后面读。。。

## Slide 37: Data Forwarding
Notes: Rse rte 是对应的读寄存器，
regwriteM memory stage
regwriteW write back stage

## Slide 38: Data Forwarding
Forward to Execute stage from either:
  Memory stage or
  Writeback stage
When should we forward from either Memory or Writeback stage?
  Answer：If that stage will write to a destination register and the destination register matches the source register.
If both the Memory and Writeback stages contain matching destination registers?
  Answer： The Memory stage should have priority, because it contains the more recently executed instruction.

## Slide 39: Data Forwarding (in Pseudocode)
Forward to Execute stage from either:
  Memory stage or
  Writeback stage
Forwarding logic for ForwardAE (pseudo code):
if ((rsE != 0) AND (rsE == WriteRegM) AND RegWriteM) then ForwardAE = 10 # forward from Memory stage else if ((rsE != 0) AND (rsE == WriteRegW) AND RegWriteW) then ForwardAE = 01 # forward from Writeback stage else ForwardAE = 00 # no forwarding
Forwarding logic for ForwardBE same, but replace rsE with rtE
Notes: A B是两个不同操作数

## Slide 40: Forwarding Is Not Always Possible
Forwarding is sufficient to resolve RAW data dependences
Unfortunately, there are cases when forwarding is not possible
  Due to pipeline design and instruction latencies
  The lw instruction does not finish reading data until the end of the Memory stage
   its result cannot be forwarded to the Execute stage of the next instruction
Notes: 本质上：把一个周期变成两个部分，第一部分结束 --》第二部分开始。

## Slide 41: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
    RAW
    WAW
    WAR
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 42: Control Dependence
Control dependence
  Data dependence on the Instruction Pointer / Program Counter

## Slide 43: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
    RAW
    WAW
    WAR
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 44: Where Are We?

## Slide 45: Review: Single-Cycle MIPS FSM
Single-cycle machine
AS
Sequential
Logic
(State)
Combinational
Logic
AS’
AS: Architectural State

## Slide 46: Review: Multi-Cycle MIPS FSM
What is the shortcoming of
this design?
What does
this design
assume
about memory?

## Slide 47: Recall: Illustrating Pipeline Operation
I0
I0
I1
I0
I1
I2
I0
I1
I2
I3
I0
I1
I2
I3
I4
I1
I2
I3
I4
I5
I2
I3
I4
I5
I6
I3
I4
I5
I6
I7
I4
I5
I6
I7
I8
I5
I6
I7
I8
I9
I6
I7
I8
I9
I10
 | t0 | t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8 | t9 | t10
IF |  |  |  |  |  |  |  |  |  |  | 
ID |  |  |  |  |  |  |  |  |  |  | 
EX |  |  |  |  |  |  |  |  |  |  | 
MEM |  |  |  |  |  |  |  |  |  |  | 
WB |  |  |  |  |  |  |  |  |  |  | 

## Slide 48: Recall: Pipelined Control
Same control unit as single-cycle processor Control delayed to proper pipeline stage

## Slide 49: Recall: Data Dependence Types
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7

## Slide 50: Recall: How to Handle Data Dependences
Anti and output dependences
  They are easier to handle.
  Write to the destination only in last stage and in program order
Handling flow dependences:
  Hardware Pipeline Stall:
    Detect and wait until value is available in register file
  Software Pipeline Stall:
    Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Data Forward/Bypass:
    Detect and forward/bypass data to dependent instruction

## Slide 51: Pipelined CPU: Ideal vs. Realistic
Ideal pipelined CPU has：
  One pipeline
  Fixed latency
  Dependency is known at compiler time
  no support for exception/interrupt
Realistic Pipelined CPU has:
  Multiple pipelines with different latencies
  Unpredictable latency
  Unknown dependency at compiler time
  Support for exception/interrupt

## Slide 52: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
    RAW
    WAW
    WAR
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 53: Multi-Cycle Execution
Multi-Cycle Execution： Not all instructions take the same amount of time for “execution”.
Question: How to address multi-cycle execution issue?
Answer: Have multiple different functional units that take different number of cycles
  Can let independent instructions start execution on a different functional unit before a previous long-latency instruction finishes execution
F
D
E
?
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store

## Slide 54: Example of Multi-Cycle Execution
Instructions take different number of cycles in EXECUTE stage
  Integer ADD (1 cycle) versus Integer DIVide (8 cycles)
  What is wrong with this picture in a Von Neumann architecture?
    Sequential semantics of the ISA NOT preserved!
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
DIV R4  R1, R2
ADD R3  R1, R2
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
DIV R2  R5, R6
ADD R7  R5, R6
F
D
E
W
E
E
E
E
E
E
E
……

## Slide 55: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
    RAW
    WAW
    WAR
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 56: Exceptions and Interrupts
“Unplanned” changes or interruptions in program execution
  Exceptions: Due to internal problems in execution of the program
  Interrupts: Due to external events that need to be handled by the processor
Both exceptions and interrupts require
  1, stopping of the current program
  2, saving the architectural state
  3, handling the exception/interrupt  switch to handler
  4, return back to program execution (if possible and makes sense)

## Slide 57: Exceptions vs. Interrupts
Cause
  Exceptions: internal to the running thread
  Interrupts: external to the running thread
When to Handle
  Exceptions: when detected (and known to be non-speculative)
  Interrupts: when convenient
    Except for very high priority ones
      Power failure
      Machine check (error)
Notes: Interrupt: machine check

## Slide 58: Precise Exceptions/Interrupts
The architectural state should be consistent (precise) when the exception/interrupt is ready to be handled
1. All previous instructions should be completely retired.
2. No later instruction should be retired.
Retire = commit = finish execution and update arch. state
Notes: 意外、中断处理：之前的指令完成，后面的指令还未更新到寄存器等系统状态内。

## Slide 59: Checking for and Handling Exceptions in Pipelining
When the oldest instruction ready-to-be-retired is detected to have caused an exception, the control logic
  1，Ensures architectural state is precise (register file, PC, memory)
  2，Flushes all younger instructions in the pipeline
  3，Saves PC and registers (as specified by the ISA)
  4，Redirects the fetch engine to the appropriate exception handling routine

## Slide 60: Why Do We Want Precise Exceptions?
Four Goals of Precise Exception:
  1. Keeps the semantics of the von Neumann model
  2. Aids software debugging
  3. Enables (easy) recovery from exceptions
  4. Enables traps into software (e.g., software implemented opcodes)
Notes: Trap: opcode not software emulate the opcode…

## Slide 61: Ensuring Precise Exceptions
Easy to do in single-cycle and multi-cycle machines
Single-cycle
  Instruction boundaries == Cycle boundaries
Multi-cycle
  Add special states in the control FSM that lead to the exception or interrupt handlers
  Switch to the handler only at a precise state  before fetching the next instruction
See H&H Section 7.7 for a treatment of exceptions in multi-cycle uarch

## Slide 62: Precise Exceptions in Multi-Cycle FSM
Notes: S1

## Slide 63: Precise Exceptions in Multi-Cycle Datapath
See H&H Section 7.7 for a treatment of exceptions in multi-cycle uarch

## Slide 64: Ensuring Precise Exceptions in Pipelining
Idea: Make each operation take the same amount of time
Downside:
  Worst-case instruction latency determines all instructions’ latency
    What about memory operations?
    Each functional unit takes worst-case number of cycles?
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
DIV R3  R1, R2
ADD R4  R1, R2
Notes: 第一种：摆烂

## Slide 65: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
    RAW
    WAW
    WAR
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 66: False Dependencies: Lack of registers
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7

## Slide 67: Pipelining and Precise Exceptions: Preserving Sequential Semantics

## Slide 68: Outline
Pipeline Hazard
  Structural Hazard
  Data Hazard (Dependencies)
    RAW
    WAW
    WAR
  Control Hazard
Reorder Buffer
  For Multi-cycle Execution
  For Exception and Interrupt
  For False Dependencies (WAW & WAR)
Definition of Reorder Buffer

## Slide 69: Reorder Buffer
Reorder buffer
  For false dependencies
  For exception and interrupt
  For multi-cycle execute
Suggested reading
  Smith and Plezskun, “Implementing Precise Interrupts in Pipelined Processors,” IEEE Trans on Computers 1988 and ISCA 1985.

## Slide 70: Reorder Buffer (ROB)
Key Idea: Complete instructions out-of-order, but reorder them before writing results to architectural state (Commit).
  1, When instruction is decoded in order, it reserves the next-sequential entry in the ROB, rename the destination register.
  2, When instruction completes out-of-order, it writes result into ROB entry.
  3, When instruction oldest in ROB and it has completed without exceptions, its result writes to reg. file or memory (In order commitment)
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache
Complete out-of-order
Commit
in order
Decoded
in order
Notes: Need the animation here…
Rob index, write, read…

## Slide 71
Reorder buffer类似临时工，没编制。
出问题就怪临时工。
Notes: The majority of you will not work on Systems.
But you should know the key principles that help you understand the system on which your AI task runs.
Our course has to include both computer architecture and AI chip courses.

## Slide 72: What’s in a ROB Entry?
ROBs need to:
  1, correctly reorder instructions back into the program order
  2, update the architectural state with the instruction’s result(s), if instruction can retire without any issues
  3, handle an exception/interrupt precisely, if an exception/interrupt needs to be handled before retiring the instruction
  4, use valid bits to keep track of readiness of the result(s) and find out if the instruction has completed execution
V
DestRegID
DestRegVal
StoreAddr
StoreData
PC
Valid bits for reg/data + control bits
Exception?

## Slide 73: Reorder Buffer: Independent Operations
Indirection:
  1, Result first written to ROB on instruction completion
  2, Result written to register file at commit time
What if a later instruction needs a value in the reorder buffer?
  One option: stall the operation  stall the pipeline
  Better: Read the value from the reorder buffer. How?
F
D
E
W
F
D
E
R
E
E
E
E
E
E
E
F
D
E
W
F
D
E
R
F
D
E
R
F
D
E
R
F
D
E
R
E
E
E
E
E
E
E
W
R
R
W
W
W
W
Notes: Use
bypass

## Slide 74: Reorder Buffer: Where to put?
A register value can be in the register file, reorder buffer.
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache

## Slide 75: Simplifying Reorder Buffer Access
Idea: Use indirection
1, Access register file first (check if the register is valid)
  If register not valid, register file stores the ID of the reorder buffer entry that contains (or will contain) the value of the register
  Mapping of the register to a ROB entry: Register file maps the register to a reorder buffer entry if there is an in-flight instruction writing to the register
2, Access reorder buffer next
Notes: Access ROB first

## Slide 76: Reorder Buffer in Intel Pentium III
Boggs et al., “The Microarchitecture of the Pentium 4 Processor,” Intel Technology Journal, 2001.

## Slide 77: Reorder Buffer: For False Dependencies
Output and anti dependences are not true dependences
  WHY? The same register refers to values that have nothing to do with each other
  They exist due to lack of register ID’s (i.e. names) in the ISA
RB eliminates anti and output dependences
  Gives the illusion that there are a large number of registers
HOW: The register ID is renamed to the reorder buffer entry that will hold the register’s value
  Register ID  ROB entry ID
  Architectural register ID  Physical register ID
  After renaming, ROB entry ID used to refer to the register
Notes: ROB 临时工，临时工多，有编制的少

## Slide 78: Reorder Buffer: For False Dependencies
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7
RB100
RB100
RB101
RB102

## Slide 79
To address false dependency,
number of registers > number of ROB entries?
NO.
Notes: The majority of you will not work on Systems.
But you should know the key principles that help you understand the system on which your AI task runs.
Our course has to include both computer architecture and AI chip courses.

## Slide 80: In-Order Pipeline with Reorder Buffer
In-order dispatch/execution, out-of-order completion, in-order retirement
  Decode (D): Access regfile/ROB, allocate entry in ROB, check if instruction can execute, if so dispatch instruction
  Execute (E): Instructions can complete out-of-order
  Completion (R): Write result to reorder buffer
  Retirement/Commit (W): Check for exceptions; if none, write result to architectural register file or memory; else, flush pipeline and start from exception handler
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
R
Out of Order
In order

## Slide 81: Reorder Buffer Tradeoffs
Advantages
  Conceptually simple for supporting precise exceptions
  Can eliminate false dependences
Disadvantages
  Reorder buffer needs to be accessed to get the results that are yet to be written to the register file
    Indirection  increased latency and complexity

## Slide 82: Can Reorder Buffer Change This Map?
Chart: Throughput (GOPs/s)
One-cycle CPU | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Pipeline CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD CPU | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
GPU | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000
VGG19 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6
GPT-3 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000
Notes: NO