## Slide 1: Computer Arch. & AI Chip Lecture 3: Tomasula
Prof. Zeke Wang
Zhejiang University
22 March 2026

## Slide 2: Recall: Reorder Buffer (ROB)
Key Idea: Complete instructions out-of-order, but reorder them before writing results to architectural state (Commit).
  1, When instruction is decoded in order, it reserves the next-sequential entry in the ROB, rename the destination register.
  2, When instruction completes out-of-order, it writes result into ROB entry.
  3, When instruction oldest in ROB and it has completed without exceptions, its result writes to reg. file or memory (In order commitment)
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache
Complete out-of-order
Commit
in order
Decoded
in order
Notes: Need the animation here…
Rob index, write, read…

## Slide 3: Recall: Reorder Buffer: For False Dependencies
Output and anti dependences are not true dependences
  WHY? The same register refers to values that have nothing to do with each other
  They exist due to lack of register ID’s (i.e. names) in the ISA
This eliminates anti and output dependences
  Gives the illusion that there are a large number of registers
HOW: The register ID is renamed to the reorder buffer entry that will hold the register’s value.
  Register ID  ROB entry ID
  Architectural register ID  Physical register ID
  After renaming, ROB entry ID used to refer to the register

## Slide 4: Reorder Buffer: For False Dependencies
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7
RB100
RB100
RB101
RB102
RB100

## Slide 5: Recall: Reorder Buffer for Multi-cycle Execution and Interrupt
Indirection:
  1, Result first written to ROB on instruction completion
  2, Result written to register file at commit time
F
D
E
W
F
D
E
R
E
E
E
E
E
E
E
F
D
E
W
F
D
E
R
F
D
E
R
F
D
E
R
F
D
E
R
E
E
E
E
E
E
E
W
R
R
W
W
W
W
Notes: Use
bypass

## Slide 6: Out-of-Order Execution (Dynamic Instruction Scheduling)

## Slide 7: Where Are We?

## Slide 8: An In-order Pipeline with only ROB
Dispatch: Act of sending an instruction to a functional unit
Renaming with ROB
  eliminates stalls due to false dependences
Problem: A true data dependence stalls dispatch of younger instructions into functional (execution) units
F
D
E
R
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Cache miss
W
In order dispatch
In order
Out of order
Notes: In-order issue, in-order dispaatch, out-of-order completion, in-order retirement.

## Slide 9: Issue of In-order Dispatch
In order dispatch + precise exceptions:
IO: 16
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
F
D
W
E
E
E
E
R
F
D
E
R
W
STALL
F
D
E
R
W
STALL
F
D
E
R
W
E
E
E
E
F
D
E
R
W
STALL
IMUL: 4 cycles, ADD： 1 cycle
Notes: 假设有forward，IMUL 4 cycles, ADD 1 cycle.

## Slide 10: Can We Do Better?

## Slide 11: How Can We Do Better?
What do the following two pieces of code have in common (with respect to execution in the previous design)?
Answer: First ADD stalls the whole pipeline!
  ADD cannot dispatch because its source register R3 is unavailable
  Later independent instructions cannot get executed
How are the above code portions different?
  Answer: Load latency is variable (unknown until runtime)
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R4  R6, R7
IMUL R5  R6, R8
ADD R7  R9, R9
LD R3  R1 (0)
ADD R3  R3, R1
ADD R4  R6, R7
IMUL R5  R6, R8
ADD R7  R9, R9

## Slide 12: Preventing Dispatch Stalls
Problem: in-order dispatch (scheduling, or execution)
Solution: out-of-order dispatch (scheduling, or execution)
Goal of out-of-order dispatch:
  Like Dataflow, “fire” an instruction only when its inputs are ready
LD R3  R1 (0)
ADD R3  R3, R1
ADD R4  R6, R7
IMUL R5  R6, R8
ADD R7  R9, R9
  The insn “ADD R3…” will not impede insns “ADD R4…, IMUL R5…, ADD R7…”.

## Slide 13: Reservation Station: Out-of-order Execution
Key idea of reservation station: Move the dependent instructions out of the way of independent ones (s.t. independent ones can execute)
  Rest areas for dependent instructions: Reservation Stations
Function of Reservation Station:
  Monitors the source “values” of each instruction in the resting area
  “Fires” (i.e. dispatch) the instruction, when all source “values” of an instruction are available
    Instructions dispatched in dataflow (not control-flow) order
Benefit of Reservation Station:
  Latency tolerance: Allows independent instructions to execute and complete in the presence of a long-latency operation
Notes: One road with multiple ways…
高速路上的

## Slide 14: In-order vs. Out-of-order Dispatch
In order dispatch + precise exceptions:
Out-of-order dispatch + precise exceptions:
IO: 16 vs. OoO:12 cycles
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
F
D
W
E
E
E
E
R
F
D
E
R
W
STALL
F
D
E
R
W
STALL
F
D
E
R
W
E
E
E
E
F
D
E
R
W
STALL
F
D
W
E
E
E
E
R
F
D
E
E
E
E
R
W
F
D
E
R
W
WAIT
F
D
E
R
W
WAIT
F
D
E
R
W
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
IMUL: 4 cycles, ADD： 1 cycle
Notes: 假设有forward，IMUL 4 cycles, ADD 1 cycle.

## Slide 15: Tomasulo’s Algorithm for OoO Execution
OoO with register renaming invented by Robert Tomasulo
  Used in IBM 360/91 Floating Point Units
  Read: Tomasulo, “An Efficient Algorithm for Exploiting Multiple Arithmetic Units,” IBM Journal of R&D, Jan. 1967.
OoO variants are used in most high-performance processors
  Initially in Intel Pentium Pro, AMD K5
  Alpha 21264, MIPS R10000, IBM POWER5, IBM z196, Oracle UltraSPARC T4, ARM Cortex A15, Apple M1, …
Notes: 360 is not commercially suceesful, without precious exception

## Slide 16: Two Humps in a Modern Pipeline
Hump 1: Reservation stations (enabling in-order issue and out-of-order dispatch/execution)
Hump 2: Reorder buffer (enabling OoO completion, in-order commitment)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
Reservation Station
TAG and VALUE Broadcast Bus
In order issue
OoO dispatch
In order commitment
OoO execution

## Slide 17: Two Humps in a Modern Pipeline
Hump 1: Reservation stations (scheduling window)
Hump 2: Reordering (reorder buffer, aka instruction window or active window)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
S
C
H
E
D
U
L
E
TAG and VALUE Broadcast Bus
in order
out of order
in order
Photo credit: http://true-wildlife.blogspot.ch/2010/10/bactrian-camel.html

## Slide 18: Enabling OoO Execution
1. Need to link the consumer of a value to the producer
  Register renaming: Associate a “tag” with each data value
2. Need to buffer instructions until they are ready to execute
  Insert instruction into reservation stations after renaming
3. Instructions need to keep track of readiness of source values
  Broadcast the “tag” when the value is produced
  Instructions compare their “source tags” to the broadcast tag  if match, source value becomes ready
4. When all source values of an instruction are ready, need to dispatch the instruction to its functional unit (FU)
  Instruction wakes up if all sources are ready
  If multiple instructions are awake, need to select one per FU

## Slide 19: General Organization of an OOO Processor
  Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proc. IEEE, Dec. 1995.
Notes: Instruction buffer: reservation station.

## Slide 20: Tomasulo’s Machine: IBM 360/91
FP FU
FP FU
from memory
load
buffers
from instruction unit
FP registers
store buffers
to memory
operation bus
reservation
stations
Common data bus

## Slide 21: Recall Once More: Register Renaming
Output and anti dependences are not true dependences
  WHY? The same register refers to values that have nothing to do with each other
  They exist because not enough register ID’s (i.e. names) in the ISA
The dest. register ID is renamed to the reservation station entry
  Destination register ID  RS entry ID
  After renaming, RS entry ID used to refer to the register for the following instructions before updating the register.
This eliminates anti- and output- dependences
  Approximates the performance effect of a large number of registers even though ISA has a small number.
Notes: Destination id

## Slide 22: Tomasulo’s Algorithm: Three Components
Register Rename Table (register alias table)
R0
R1
R2
R3
tag
value
valid?
R4
R5
R6
R7
R8
R9
1
1
1
1
1
1
1
1
1
1
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a |  |  |  |  |  | 
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
Reservation Station
rs.tag
IF
ID
E
W
RS
Common Data Bus:
  Broadcasts the tag and result to all FUs
  Updates the RF using the tag and result
Notes: RRT:
Tag: reservation station entry ID
Valid: 1 means the register is readable, 0 means the new value exists in a reservation station entry.
Value: value in RF
RS:
V: valid bit of this operand
Tag: RS ID
Value: value of this operand

## Slide 23: Tomasulo’s Algorithm
ID: If reservation station entry available before renaming dest. register
  Occupy a RS entry for the instruction
  For each source register in the RS entry: if the valid bit of source register in RF is 1, RS.source.v = 1 and RS.source.value=source register; else RS.source.v = 0 and RS.source.tag = source register.tag.
  For dest. register in RF: Rename to the tag of the corresponding RS entry, set the valid bit to 0.
Else stall
RS: While in reservation station, each instruction:
  Update: Watches common data bus (CDB) for tag of its sources. When tag seen, grab value for the source and keep it in the reservation station (.v = 1).
  Issue: When both operands available, instruction ready to be dispatched to FU
EXE: Execute the instruction in FU, produce its broadcast tag and value
WB: After instruction finishes in the Functional Unit
  a, Arbitrate for CDB
  b, Put broadcast tag and its broadcast value onto CDB (tag broadcast)
  c, Update register file connected to the CDB
    If the tag in the RF matches the broadcast tag, write broadcast value into register (and set valid bit)
  d, Update reservation station connected to the CDB
    If the broadcast tag matches the tag of any source in a RS entry, write the broadcast value to the source and set the valid bit of the source.
Notes:   d, Reclaim rename tag
    no valid copy of tag in system!

## Slide 24: Our First OoO Machine Simulation
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 3
R4 | 1 |  | 4
R5 | 1 |  | 5
R6 | 1 |  | 6
R7 | 1 |  | 7
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 10
R11 | 1 |  | 11
+
∗
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a |  |  |  |  |  | 
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x |  |  |  |  |  | 
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Tag
Value
Tag
Value
RS for ADD Unit
RS for MUL Unit
Register Rename Table
Program We Will Simulate
ADD and MUL Execution Units
have separate common data buses
Initially:
RS’s are all Invalid (Empty)
All Registers are Valid
MUL: 6 cycles, ADD： 4 cycle

## Slide 25: Cycle 0
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 3
R4 | 1 |  | 4
R5 | 1 |  | 5
R6 | 1 |  | 6
R7 | 1 |  | 7
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 10
R11 | 1 |  | 11
+
∗
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a |  |  |  |  |  | 
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x |  |  |  |  |  | 
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
MUL: 6 cycles, ADD： 4 cycle

## Slide 26: Cycle 1
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 3
R4 | 1 |  | 4
R5 | 1 |  | 5
R6 | 1 |  | 6
R7 | 1 |  | 7
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 10
R11 | 1 |  | 11
+
∗
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a |  |  |  |  |  | 
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x |  |  |  |  |  | 
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
MUL: 6 cycles, ADD： 4 cycle

## Slide 27: Cycle 2
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 3
R4 | 1 |  | 4
R5 | 1 |  | 5
R6 | 1 |  | 6
R7 | 1 |  | 7
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 10
R11 | 1 |  | 11
+
∗
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a |  |  |  |  |  | 
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x |  |  |  |  |  | 
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
D
2
F
F
1
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Cycle
1
2
Step 2: Access the Register Alias Table
Step 3: Put source registers into reservation station x.
1
1
~
~
Step 4: Rename destination register R3  x
0
x
R3 is now renamed to x.
Its new value will produced by the reservation station
that is identified by tag x.
MUL in RS x is ready to execute in the next cycle!
Step 1: Check if reservation station available. Yes: x
MUL gets decoded and allocated into RS x
MUL: 6 cycles, ADD： 4 cycle

## Slide 28: Cycle 3
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 1 |  | 5
R6 | 1 |  | 6
R7 | 1 |  | 7
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 10
R11 | 1 |  | 11
+
∗
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a |  |  |  |  |  | 
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Check readiness (Both sources ready?)  Wakeup
Ready  Dispatch the instruction to the MUL unit
6
Cycles
0
x
4
1
~
0
a
Same Steps 1-4 for ADD… Rename R5  a
ADD in RS a cannot execute in the next cycle: one source is not valid
1. MUL in RS x starts executing
2. ADD gets decoded and allocated into RS a
MUL: 6 cycles, ADD： 4 cycle

## Slide 29: Cycle 4
+
∗
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | a | 
R6 | 1 |  | 6
R7 | 1 |  | 7
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 10
R11 | 1 |  | 11
ADD in RS a waits because one source is not valid.
2
1
~
6
1
~
Rename R7  b
0
b
ADD in RS b is ready to execute in the next cycle!
It will be executed out of order in the next cycle.

## Slide 30: Cycle 5
+
∗
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | a | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 10
R11 | 1 |  | 11
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c |  |  |  |  |  | 
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
8
1
~
9
1
~
4
Cycles
0
c
ADD in RS c is ready to execute in the next cycle!
MUL: 6 cycles, ADD： 4 cycle

## Slide 31: Cycle 6
+
∗
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | a | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 1 |  | 11
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y |  |  |  |  |  | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
0
y
0
b
0
c
MUL: 6 cycles, ADD： 4 cycle

## Slide 32: Cycle 7
+
∗
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | a | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d |  |  |  |  |  | 
0
a
0
y
0
d
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 0 | b |  | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
All 6 instructions are now decoded and renamed
Note what happened to R5!
MUL: 6 cycles, ADD： 4 cycle

## Slide 33: Cycle 8 (First Slide)
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 0 | a |  | 0 | y | 
+
∗
E6
8
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 0 | b |  | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Broadcast MUL’s tag (x)
Check tag
Check for invalidity
2
MUL in RS x is done
x
Broadcast MUL’s result (2)
1
x
1
2
2
2
ADD in RS a is ready to execute in the next cycle!

## Slide 34: Cycle 8 (Second Slide)
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 0 | a |  | 0 | y | 
+
∗
E6
8
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 0 | b |  | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Broadcast ADD’s tag (b)
Check tag
Check for invalidity
ADD in RS b is also done
Broadcast ADD’s result (8)
1
1
8
E4
-
8
b
b
8
8
MUL in RS y is still NOT ready to execute in the next cycle!

## Slide 35: Cycle 8 (Third Slide)
+
∗
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 0 | a |  | 0 | y | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 | b | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
MUL: 6 cycles, ADD： 4 cycle

## Slide 36: Cycle 9
+
∗
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 0 | a |  | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 
17
1
~
c
17
1
17
Broadcast and Update
MUL in RS y is ready to execute in the next cycle!
MUL: 6 cycles, ADD： 4 cycle

## Slide 37: Cycle 10
+
∗
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 0 | a |  | 0 | y | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 0 | y | 
MUL: 6 cycles, ADD： 4 cycle

## Slide 38: Cycle 11
+
∗
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 0 | a |  | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 0 | y | 
MUL: 6 cycles, ADD： 4 cycle

## Slide 39: Cycle 12
+
∗
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 0 | a |  | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
a
6
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 0 | y | 
6
1
~
Broadcast and Update
MUL: 6 cycles, ADD： 4 cycle

## Slide 40: Cycle 13
+
∗
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 0 | y | 
MUL: 6 cycles, ADD： 4 cycle

## Slide 41: Cycle 14
+
∗
14
E5
-
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 0 | y | 
MUL: 6 cycles, ADD： 4 cycle

## Slide 42: Cycle 15
+
∗
15
E6
-
14
E5
-
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 0 | y | 
1
136
136
1
~
y
136
Broadcast and Update
ADD in RS d is ready to execute in the next cycle!
MUL: 6 cycles, ADD： 4 cycle

## Slide 43: Cycle 16
+
∗
16
W
E1
15
E6
-
14
E5
-
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 1 | ~ | 136
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 1 |  | 136
MUL: 6 cycles, ADD： 4 cycle

## Slide 44: Cycle 17
+
∗
17
E2
16
W
E1
15
E6
-
14
E5
-
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 1 |  | 136
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 1 | ~ | 136
MUL: 6 cycles, ADD： 4 cycle

## Slide 45: Cycle 18
+
∗
18
E3
17
E2
16
W
E1
15
E6
-
14
E5
-
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 1 |  | 136
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 1 | ~ | 136
MUL: 6 cycles, ADD： 4 cycle

## Slide 46: Cycle 19
+
∗
19
E4
18
E3
17
E2
16
W
E1
15
E6
-
14
E5
-
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 0 | d | 
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 1 |  | 136
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 1 | ~ | 136
d
142
1
142
Broadcast and Update
MUL: 6 cycles, ADD： 4 cycle

## Slide 47: Cycle 20
+
∗
20
W
19
E4
18
E3
17
E2
16
W
E1
15
E6
-
14
E5
-
13
W
E4
-
12
E4
E3
-
11
E3
E2
-
10
E2
W
E1
-
W
9
E1
W
E4
-
-
E6
8
-
E4
E3
-
-
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 1 | ~ | 8 | 1 | ~ | 17
z |  |  |  |  |  | 
t |  |  |  |  |  | 
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 1 |  | 2
R4 | 1 |  | 4
R5 | 1 |  | 142
R6 | 1 |  | 6
R7 | 1 |  | 8
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 1 |  | 17
R11 | 1 |  | 136
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 1 | ~ | 2 | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d | 1 | ~ | 6 | 1 | ~ | 136
MUL: 6 cycles, ADD： 4 cycle

## Slide 48: Tomasulo’s Algorithm
ID: If reservation station entry available before renaming dest. register
  Occupy a RS entry for the instruction
  For each source register in the RS entry: if the valid bit of source register in RF is 1, RS.source.v = 1 and RS.source.value=source register; else RS.source.v = 0 and RS.source.tag = source register.tag.
  For dest. register in RF: Rename to the tag of the corresponding RS entry, set the valid bit to 0.
Else stall
RS: While in reservation station, each instruction:
  Update: Watches common data bus (CDB) for tag of its sources. When tag seen, grab value for the source and keep it in the reservation station (.v = 1).
  Issue: When both operands available, instruction ready to be dispatched to FU
EXE: Execute the instruction in FU, produce its broadcast tag and value
WB: After instruction finishes in the Functional Unit
  a, Arbitrate for CDB
  b, Put broadcast tag and its broadcast value onto CDB (tag broadcast)
  c, Update register file connected to the CDB
    If the tag in the RF matches the broadcast tag, write broadcast value into register (and set valid bit)
  d, Update reservation station connected to the CDB
    If the broadcast tag matches the tag of any source in a RS entry, write the broadcast value to the source and set the valid bit of the source.
Notes:   d, Reclaim rename tag
    no valid copy of tag in system!

## Slide 49: Some Questions
What can potentially become the critical path?
  Tag broadcast  value capture  instruction wake up
How can you reduce the potential critical paths?
  Break down the critical path

## Slide 50: Dataflow Graph for Our Example
MUL R3  R1, R2
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R7, R10
ADD R5  R5, R11

## Slide 51: State of RAT and RS in Cycle 7
+
∗
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | a | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d |  |  |  |  |  | 
0
a
0
y
0
d
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 0 | b |  | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 

## Slide 52: Corresponding Dataflow Graph (Reverse Engineered)
MUL R3  R1, R2
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R7, R10
ADD R5  R5, R11
*
R1
R2
+
+
R6
R8
R9
+
R4
*
+
R5 (d)
R11 (y)
R10 (c)
R5 (a)
R3 (x)
R7 (b)

## Slide 53: Summary of OOO Execution Concepts
Register renaming eliminates false dependences, enables linking of producer to consumers
Buffering in reservation stations enables the pipeline to move for independent instructions
Tag broadcast enables communication (of readiness of produced value) between instructions
Wakeup and select enables out-of-order dispatch

## Slide 54: For You: An Exercise, wo/ Precise Exceptions
Assume
  ADD (4 cycle execute), MUL (6 cycle execute)
  One adder and one multiplier
How many cycles
  in an in-order-dispatch pipelined machine wo reorder buffer (no forwarding and full forwarding)?
  in an out-of-order dispatch pipelined machine wo reorder buffer (full forwarding)?
MUL R3  R1, R3
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R5, R6
ADD R5  R5, R3
F
D
E
W
Notes: 任务。。。

## Slide 55: Out-of-Order Execution with Precise Exceptions
Hump 1: Reservation stations (scheduling window)
Hump 2: Reordering (reorder buffer, aka instruction window or active window)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
Reservation
Station
TAG and VALUE Broadcast Bus
in order
out of order
in order

## Slide 56: Two Humps in a Modern Pipeline
Hump 1: Reservation stations (scheduling window)
Hump 2: Reordering (reorder buffer, aka instruction window or active window)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
S
C
H
E
D
U
L
E
TAG and VALUE Broadcast Bus
in order
out of order
in order
Photo credit: http://true-wildlife.blogspot.ch/2010/10/bactrian-camel.html

## Slide 57: Modern OoO Execution w/ Precise Exceptions
Most modern processors use the following
Reorder buffer to support in-order retirement of instructions
A single register file to store all registers
  Both speculative and architectural registers
  INT and FP are still separate
Two register maps
  Future/frontend register map  used for renaming
  Architectural register map  used for maintaining precise state

## Slide 58: Out-of-Order Execution with Precise Exceptions
Idea: Use a reorder buffer to reorder instructions before committing them to architectural state
An instruction updates the RAT when it completes execution
  Also called frontend register file
An instruction updates a separate architectural register file when it retires
  i.e., when it is the oldest in the machine and has completed execution
  In other words, the architectural register file is always updated in program order
On an exception: flush pipeline, copy architectural register file into frontend register file

## Slide 59: An Example from Modern Processors
Boggs et al., “The Microarchitecture of the Pentium 4 Processor,” Intel Technology Journal, 2001.

## Slide 60: OOO Execution: Restricted Dataflow
An out-of-order engine dynamically builds the dataflow graph of a piece of the program
  which piece?
The dataflow graph is limited to the instruction window
  Instruction window: all decoded but not yet retired instructions
Can we do it for the whole program?
Why would we like to?
In other words, how can we have a large instruction window?
Can we do it efficiently with Tomasulo’s algorithm?

## Slide 61: Questions to Ponder
Why is OoO execution beneficial?
  What if all operations take a single cycle?
  Latency tolerance: OoO execution tolerates the latency of multi-cycle operations by executing independent operations concurrently
What if an instruction takes 1000 cycles?
  How large of an instruction window do we need to continue decoding?
  How many cycles of latency can OoO tolerate?
  What limits the latency tolerance scalability of Tomasulo’s algorithm?
    Instruction window size: how many decoded but not yet retired instructions you can keep in the machine.

## Slide 62: General Organization of an OOO Processor
  Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proc. IEEE, Dec. 1995.

## Slide 63: A Modern OoO Design: Intel Pentium 4
Boggs et al., “The Microarchitecture of the Pentium 4 Processor,” Intel Technology Journal, 2001.

## Slide 64: Intel Pentium 4 Simplified
Mutlu+, “Runahead Execution,”
HPCA 2003.

## Slide 65: Alpha 21264
Kessler, “The Alpha 21264 Microprocessor,” IEEE Micro, March-April 1999.

## Slide 66: MIPS R10000
Yeager, “The MIPS R10000 Superscalar Microprocessor,” IEEE Micro, April 1996

## Slide 67: IBM POWER4
Tendler et al., “POWER4 system microarchitecture,” IBM J R&D, 2002.

## Slide 68: IBM POWER4
2 cores, out-of-order execution
100-entry instruction window in each core
8-wide instruction fetch, issue, execute
Large, local+global hybrid branch predictor
1.5MB, 8-way L2 cache
Aggressive stream based prefetching

## Slide 69: IBM POWER5
  Kalla et al., “IBM Power5 Chip: A Dual-Core Multithreaded Processor,” IEEE Micro 2004.

## Slide 70: Intel Skylake (3rd Xeon)
Notes: Intel gold CPU…
4rd Xeon Sapphire Rapids

## Slide 71: AMD Zen
Notes: Intel gold CPU…

## Slide 72: Approaches to Dependence Detection (I)
Scoreboarding
  Each register in register file has a Valid bit associated with it
  An instruction that is writing to the register resets the Valid bit
  An instruction in Decode stage checks if all its source and destination registers are Valid
    Yes: No need to stall… No dependence
    No: Stall the instruction
Advantage:
  Simple. 1 bit per register
Disadvantage:
  Need to stall for all types of dependences, not only flow dep.