## Slide 1: Computer Arch. & AI Chip Lecture 4: Superscalar + SIMD + Multi-core
Prof. Zeke Wang
Zhejiang University
26 March 2026

## Slide 2: Recall: Reorder Buffer (ROB)
Key Idea: Complete instructions out-of-order, but reorder them before writing results to architectural state (Commit).
  1, When instruction is decoded in order, it reserves the next-sequential entry in the ROB, rename the destination register.
  2, When instruction completes out-of-order, it writes result into ROB entry.
  3, When instruction oldest in ROB and it has completed without exceptions, its result writes to reg. file or memory (In order commitment)
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache
Complete out-of-order
Commit
in order
Decoded
in order
Notes: Need the animation here…
Rob index, write, read…

## Slide 3: Recall: Effect of Out-of-order Dispatch
In order dispatch + precise exceptions:
Out-of-order dispatch + precise exceptions:
IO: 16 vs. OoO:12 cycles
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
F
D
W
E
E
E
E
R
F
D
E
R
W
STALL
F
D
E
R
W
STALL
F
D
E
R
W
E
E
E
E
F
D
E
R
W
STALL
F
D
W
E
E
E
E
R
F
D
E
E
E
E
R
W
F
D
E
R
W
WAIT
F
D
E
R
W
WAIT
F
D
E
R
W
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
IMUL: 4 cycles, ADD： 1 cycle
Notes: 假设有forward，IMUL 4 cycles, ADD 1 cycle.

## Slide 4: Recall: Two Humps in a Modern Pipeline
Hump 1: Reservation stations (enabling in-order issue and out-of-order dispatch/execution)
Hump 2: Reorder buffer (enabling OoO completion, in-order commitment)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
Reservation Station
TAG and VALUE Broadcast Bus
In order issue
OoO dispatch
In order commitment
OoO execution

## Slide 5: Recall: Tomasulo’s Algorithm: Components
Register rename table (register alias table)
R0
R1
R2
R3
tag
value
valid?
R4
R5
R6
R7
R8
R9
1
1
1
1
1
1
1
1
1
1
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a |  |  |  |  |  | 
b |  |  |  |  |  | 
c |  |  |  |  |  | 
d |  |  |  |  |  | 
Reservation station
rs.tag
IF
ID
E
W
RS
Common Data Bus:
  Broadcasts the tag and result to all RSs
  Updates the RF using the tag and result
Notes: Tag: reservation station entry ID
Valid: 1 means the register is readable, 0 means the new value exists in a reservation station entry.

## Slide 6: Recall: Tomasulo’s Algorithm
ID: If reservation station entry available before renaming dest. register
  Occupy a RS entry for the instruction
  For each source register in the RS entry: if the valid bit of source register in RF is 1, RS.source.v = 1 and RS.source.value=source register; else RS.source.v = 0 and RS.source.tag = source register.tag.
  For dest. register in RF: Rename to the tag of the corresponding RS entry, set the valid bit to 0.
Else stall
RS: While in reservation station, each instruction:
  Update: Watches common data bus (CDB) for tag of its sources. When tag seen, grab value for the source and keep it in the reservation station.
  Issue: When both operands available, instruction ready to be dispatched to FU
EXE: Execute the instruction in FU, produce its broadcast tag and value
WB: After instruction finishes in the Functional Unit
  a, Arbitrate for CDB
  b, Put broadcast tag and its broadcast value onto CDB (tag broadcast)
  c, Update register file connected to the CDB
    If the tag in the register file matches the broadcast tag, write broadcast value into register (and set valid bit)
  d, Update reservation station connected to the CDB
    If the broadcast tag matches the tag of any source in a RS entry, write the broadcast value to the source and set the valid bit of the source.
Notes:   d, Reclaim rename tag
    no valid copy of tag in system!

## Slide 7: Outline
Superscalar
Vector Insn
Multithreading
Multi-core

## Slide 8: Superscalar Execution

## Slide 9: Where Are We?

## Slide 10: Superscalar Execution
Idea: Fetch, decode, execute, retire multiple instructions per cycle
  N-wide superscalar  N instructions per cycle
Issues:
  Need to add the hardware resources for doing so
  Hardware performs the dependence checking between concurrently-fetched instructions
Superscalar execution and out-of-order execution are orthogonal concepts
  Can have all four combinations of processors:
    [in-order, out-of-order] x [scalar, superscalar]

## Slide 11: In-Order Superscalar Processor Example
Idea: Multiple copies of data-path: Can fetch/decode/execute multiple instructions per cycle.
Issue: Dependences make it tricky to dispatch multiple instructions in the same cycle.
  Need dependence detection between concurrently-fetched instructions.
Here: Ideal IPC = 2

## Slide 12: In-Order Superscalar: Ideal
lw $t0, 40($s0)
add $t1, $s1, $s2
sub $t2, $s1, $s3 and $t3, $s3, $s4 or $t4, $s1, $s5
sw $s5, 80($s0)
Ideal IPC = 2
Actual IPC = 2 (6 instructions issued in 3 cycles)

## Slide 13: In-Order Superscalar: Dependences
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 and $t2, $s4, $t0 or $t3, $s5, $s6
sw $s7, 80($t3)
Ideal IPC = 2
Actual IPC = 1.2
(6 instructions issued in 5 cycles)
Notes: Pointer chasing

## Slide 14: Superscalar Execution Tradeoffs
Advantages
  Higher instruction throughput
    Higher IPC: instructions per cycle (i.e., lower CPI)
Disadvantages
  Higher complexity for dependence checking
    Require checking within a pipeline stage
    Register renaming becomes more complex in an OoO processor
    Potentially lengthens critical path delay  clock cycle time
  More hardware resources needed

## Slide 15
Can superscalar tech affect the result in Roofline model?
Notes: 不太行

## Slide 16: Outline
Superscalar
Vector Insn
Multithreading
Multi-core

## Slide 17: Where Are We?

## Slide 18: Flynn’s Taxonomy of Computers
SISD: Single instruction operates on single data element
SIMD: Single instruction operates on multiple data elements
  Array processor
  Vector processor
MISD: Multiple instructions operate on single data element
  Closest form: systolic array processor, streaming processor
MIMD: Multiple instructions operate on multiple data elements (multiple instruction streams)
  Multiprocessor
  Multithreaded processor
Mike Flynn, “Very High-Speed Computing Systems,” Proc. of IEEE, 1966
Notes: Flynn:弗林

## Slide 19: Single-Instruction/Single-Data Stream (SISD)
SISD computer that exploits no parallelism in either the instruction or data streams.
Examples of SISD：
  traditional uniprocessor machines, e.g. our trusted RISC-V pipeline
Instruction Pool
PU
Data Pool

## Slide 20: Single-Instruction/Multiple-Data (SIMD or “sim-dee”)
SIMD computer exploits multiple data streams against a single instruction stream to operations that are naturally parallelized.
Examples of SIMD:
  Intel SIMD instruction extensions
  AMD, PowerPC
Instruction Pool
PU
PU
PU
PU
Data Pool

## Slide 21: Multi-Instruction/Multiple-Data (MIMD or “mim-dee”)
MIMD computer exploits a number of processors that function asynchronously and independently for parallelism. At any time, different processors may be executing different instructions on different pieces of data.
Example of MIMD:
  Intel Xeon Phi
Instruction Pool
PU
PU
PU
PU
Data Pool

## Slide 22: Multiple-Instruction/Single-Data Stream (MISD)
MISD computer exploits multiple instruction streams against a single data stream.
Example of MISD:
  Historical significance,
  Systolic array processor,
  Streaming processor
Instruction Pool
PU
PU
Data Pool

## Slide 23: SIMD Applications & Implementations
Applications:
  Scientific computing
    Matlab, NumPy
  Graphics and video processing
    Photoshop, …
  Big Data
    Deep learning
  Gaming
  …
Implementations:
  x86
  ARM
  RISC-V vector extensions

## Slide 24: Intuition of SIMD Capability
Computing task (A[6:0] + B[6:0])
  Scalar: one addition per cycle
  SIMD : Multiple additions per cycle
+
t0
A[0]
B[0]
t1
A[1]
B[1]
t2
A[2]
B[2]
t3
A[3]
B[3]
t4
A[4]
B[4]
t5
A[5]
B[5]
t6
A[6]
B[6]
t1
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
+
+
+
+
t0
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[3]
B[3]
Scalar
SIMD

## Slide 25
1, 256-bit AVX2 (8个32-bit float)
2, 512-bit AVX512 (16个32-bit float)
SIMD in Intel CPU：
Linus Torvalds: “I hope AVX512 dies a painful death, and that Intel starts fixing real problems instead of trying to create magic instructions to then create benchmarks that they can look good on…”
Notes: 现在的计算世界往三个方向发展

## Slide 26: Recall: Amdahl’s Law
Amdahl’s Law
  f: Parallelizable fraction of a program
  N: Number of processors
Maximum speedup limited by serial portion: Serial bottleneck
All parallel machines “suffer from” the serial bottleneck
Speedup =
1
+
1 - f
f
N
  Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” AFIPS 1967.

## Slide 27: Vector Processor Limitations
-- Memory (bandwidth) can easily become a bottleneck, especially if
1. compute/memory operation balance is not maintained
2. data is not mapped appropriately to memory banks

## Slide 28
What needs us to do to support SIMD instructions?
Notes: 现在的计算世界往三个方向发展

## Slide 29: Recall: MIPS State Elements
  Program counter:
    32-bit register
  Instruction memory:
    Takes input 32-bit address A and reads the 32-bit data (i.e., instruction) from that address to the read data output RD.
  Register file:
    The 32-element, 32-bit register file has 2 read ports and 1 write port
  Data memory:
    If the write enable, WE, is 1, it writes 32-bit data WD into memory location at 32-bit address A on the rising edge of the clock.
    If the write enable is 0, it reads 32-bit data from address A onto RD.
This notation is used in H&H single-cycle MIPS implementation (H&H Chapter 7.3)

## Slide 30: Recall: The Full MIPS Datapath
**Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]
JAL, JR, JALR omitted

## Slide 31: MIPS State Elements When Enabling SIMD
  Program counter:
    32-bit register
  Instruction memory:
    Takes input 32-bit address A and reads the 32-bit data (i.e., instruction) from that address to the read data output RD.
  Register file (s):
    The 32-element, 32-bit register file has 2 read ports and 1 write port
    The 32-element, 128-bit register file has 2 read ports and 1 write port
  Data memory:
    If WE is 1, it writes 32-bit data WD into memory location at 32-bit address A. If WE1 = 1, writes 128-bit data WD1 to A1 address.
This notation is used in H&H single-cycle MIPS implementation (H&H Chapter 7.3)
What else parts needs to add?
Notes: EXE

## Slide 32: What will This Graph Be to Support Vector Insns?
VRF VALU VMemory

## Slide 33: Programmer Visible (Architectural) States
M[0]
M[1]
M[2]
M[3]
M[4]
M[N-1]
Memory:
1, array of storage locations
indexed by an address;
2, Multiple bank design.
Program Counter
Registers:
General purpose register file
Vector register file
Program Counter:
memory address
of the current (or next) instruction

## Slide 34: Roofline Model for SIMD CPU
Chart: Throughput (GOPs/s)
One-cycle CPU | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Pipeline CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD CPU | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
GPU | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000
VGG19 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6
GPT-3 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000
Notes: KB MB GB TB
K M B T
1B=10亿

## Slide 35: Outline
Superscalar
Vector Insn
Multithreading
Multi-core

## Slide 36: Fine-Grained Multithreading

## Slide 37: Where Are We?

## Slide 38: Fine-Grained Multithreading
Idea: Hardware has multiple thread contexts (PC+registers). Each cycle, fetch engine fetches from a different thread.
  By the time the fetched branch/instruction resolves, no instruction is fetched from the same thread
  Branch/instruction resolution latency overlapped with execution of other threads’ instructions
+ No logic needed for handling control and
data dependences within a thread
-- Single thread performance suffers
-- Extra logic for keeping thread contexts
-- Does not overlap latency if not enough
threads to cover the whole pipeline
Notes: Latency overlap/hiding

## Slide 39: Fine-Grained Multithreading (II)
Idea: Switch to another thread every cycle such that no two instructions from a thread are in the pipeline concurrently
Advantages：
  Tolerates the control and data dependency latencies by overlapping the latency with useful work from other threads
  Improves pipeline utilization by taking advantage of multiple threads
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.

## Slide 40: Fine-Grained Multithreading: History
CDC 6600’s peripheral processing unit is fine-grained multithreaded
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Processor executes a different I/O thread every cycle
  An operation from the same thread is executed every 10 cycles
Denelcor HEP (Heterogeneous Element Processor)
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.
  120 threads/processor
  Available queue vs. unavailable (waiting) queue for threads
  Each thread can have only 1 instruction in the processor pipeline; each thread independent
  For each thread, processor looks like a non-pipelined machine
  System throughput vs. single thread performance tradeoff

## Slide 41: Fine-Grained Multithreading in HEP
Cycle time: 100ns
8 stages  800 ns to complete an instruction
  assuming no memory access
No control and data dependency checking
Burton Smith
(1941-2018)

## Slide 42: Multithreaded Pipeline Example
Slide credit: Joel Emer

## Slide 43: Sun Niagara Multithreaded Pipeline
Kongetira et al., “Niagara: A 32-Way Multithreaded Sparc Processor,” IEEE Micro 2005.

## Slide 44: Fine-grained Multithreading
Advantages
  + No need for dependency checking between instructions
  (only one instruction in pipeline from a single thread)
  + No need for branch prediction logic
  + Otherwise-bubble cycles used for executing useful instructions from different threads
  + Improved system throughput, latency tolerance, utilization
Disadvantages
  - Extra hardware complexity: multiple hardware contexts (PCs, register files, …), thread selection logic
  - Reduced single thread performance (one instruction fetched every N cycles from the same thread)
  - Resource contention between threads in caches and memory
  - Some dependency checking logic between threads remains (load/store)

## Slide 45
Can multithreading tech affect the result in Roofline model?
Notes: 现在的计算世界往三个方向发展

## Slide 46: Outline
Superscalar
Vector Insn
Multithreading
Multi-core

## Slide 47: Where Are We?

## Slide 48: Multi-Core Processors

## Slide 49: Moore’s Law
Notes: 晶体管数量两年翻倍

## Slide 51: Gordon E. Moore Dies at 94
Intel and the Gordon and Betty Moore Foundation announce that company co-founder Gordon Moore died on March 24, 2023, at the age of 94.

## Slide 52: Multi-Core
Idea: Put multiple cores on the same die.
Technology scaling (Moore’s Law) enables more transistors to be placed on the same die area
What else could you do with the die area you dedicate to multiple processors?
  Have a bigger, more powerful core
  Have larger caches in the memory hierarchy
  Simultaneous multithreading
  Integrate platform components on chip (e.g., network interface, memory controllers)

## Slide 53: Why Multi-Core?
Alternative: Bigger, more powerful single core
  Larger superscalar issue width, larger instruction window, more execution units, large trace caches, large branch predictors, etc
  + Improves single-thread performance transparently to programmer, compiler;
  - Very difficult to design (Scalable algorithms for improving single-thread performance elusive);
  - Power hungry – many out-of-order execution structures consume significant power/area when scaled. Why?
  - Diminishing returns on performance;
  - Does not significantly help memory-bound application performance (Scalable algorithms for this elusive).

## Slide 54: Large Superscalar vs. Multi-Core
Olukotun et al., “The Case for a Single-Chip Multiprocessor,” ASPLOS 1996.
Vs.
Large Superscalar
Multi-Core

## Slide 55: Multi-Core vs. Large Superscalar
Multi-core advantages
  + Simpler cores  more power efficient, lower complexity, easier to design and replicate, higher frequency (shorter wires, smaller structures)
  + Higher system throughput on multiprogrammed workloads  reduced context switches
  + Higher system throughput in parallel applications
Multi-core disadvantages
  - Requires parallel tasks/threads to improve performance (parallel programming)
  - Resource sharing can reduce single-thread performance
  - Shared hardware resources need to be managed
  - Number of pins limits data supply for increased demand

## Slide 56: Why Multi-Core over Large Superscalar
Technology push
  Instruction issue queue size limits the cycle time of the superscalar, OoO processor  diminishing performance
    Quadratic increase in complexity with issue width
  Large, multi-ported register files to support large instruction windows and issue widths  more resources, reduced frequency or longer RF access, diminishing performance
Application pull
  Multiple applications run on your CPU
Olukotun et al., “The Case for a Single-Chip Multiprocessor,” ASPLOS 1996.
Notes: What does application pull mean?
Cell phone use multiple cores…

## Slide 57: Comparison Points…

## Slide 58
Can multi-core tech affect the result in Roofline model?
Notes: 现在的计算世界往三个方向发展

## Slide 59: Can Multi-core CPU Increase Throughput?
Chart: Throughput (GOPs/s)
One-cycle CPU | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Pipeline CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD CPU | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Multi-core CPU | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16
Notes: KB MB GB TB
K M B T
1B=10亿

## Slide 60: Multi-Core Evolution (An Early History)

## Slide 61: Piranha Chip Multiprocessor
  Barroso et al., “Piranha: A Scalable Architecture Based on Single-Chip Multiprocessing,” ISCA 2000.
An early example of a symmetric multi-core processor
Large-scale server based on CMP nodes
Designed for commercial workloads
Read:
  Barroso et al., “Memory System Characterization of Commercial Workloads,” ISCA 1998.
  Ranganathan et al., “Performance of Database Workloads on Shared-Memory Systems with Out-of-Order Processors,” ASPLOS 1998.

## Slide 62: Commercial Workload Characteristics
Memory system is the main bottleneck
  Very high CPI
  Execution time dominated by memory stall times
  Instruction stalls as important as data stalls
  Fast/large L2 caches are critical
Very poor Instruction Level Parallelism (ILP) with existing techniques
  Frequent hard-to-predict branches
  Large L1 miss ratios
  Small gains from wide-issue out-of-order techniques
No need for floating point and multimedia units

## Slide 63: Piranha Processing Node
Alpha core:
1-issue, in-order,
500MHz
CPU
Next few slides from
Luiz Barroso’s ISCA 2000 presentation of
Piranha: A Scalable Architecture Based on Single-Chip Multiprocessing

## Slide 64: Piranha Processing Node
CPU
Alpha core:
1-issue, in-order,
500MHz
L1 caches:
I&D, 64KB, 2-way
D$
I$

## Slide 65: Piranha Processing Node
CPU
Alpha core:
1-issue, in-order,
500MHz
L1 caches:
I&D, 64KB, 2-way
Intra-chip switch (ICS)
32GB/sec, 1-cycle delay
D$
I$
ICS
CPU
D$
I$
CPU
D$
I$
CPU
D$
I$
CPU
D$
I$
CPU
D$
I$
CPU
D$
I$
CPU
D$
I$

## Slide 66: Piranha Processing Node
CPU
Alpha core:
1-issue, in-order,
500MHz
L1 caches:
I&D, 64KB, 2-way
Intra-chip switch (ICS)
32GB/sec, 1-cycle delay
L2 cache:
shared, 1MB, 8-way
D$
I$
L2$
ICS
CPU
D$
I$
L2$
L2$
CPU
D$
I$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
L2$
CPU
D$
I$
L2$
CPU
D$
I$

## Slide 67: Piranha Processing Node
CPU
Alpha core:
1-issue, in-order,
500MHz
L1 caches:
I&D, 64KB, 2-way
Intra-chip switch (ICS)
32GB/sec, 1-cycle delay
L2 cache:
shared, 1MB, 8-way
Memory Controller (MC)
RDRAM, 12.8GB/sec
D$
I$
L2$
ICS
CPU
D$
I$
L2$
L2$
CPU
D$
I$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
8 banks
@1.6GB/sec

## Slide 68: Piranha Processing Node
CPU
Alpha core:
1-issue, in-order,
500MHz
L1 caches:
I&D, 64KB, 2-way
Intra-chip switch (ICS)
32GB/sec, 1-cycle delay
L2 cache:
shared, 1MB, 8-way
Memory Controller (MC)
RDRAM, 12.8GB/sec
Protocol Engines (HE & RE)
prog., 1K instr.,
even/odd interleaving
D$
I$
L2$
ICS
CPU
D$
I$
L2$
L2$
CPU
D$
I$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
RE
HE

## Slide 69: Piranha Processing Node
CPU
Alpha core:
1-issue, in-order,
500MHz
L1 caches:
I&D, 64KB, 2-way
Intra-chip switch (ICS)
32GB/sec, 1-cycle delay
L2 cache:
shared, 1MB, 8-way
Memory Controller (MC)
RDRAM, 12.8GB/sec
Protocol Engines (HE & RE):
prog., 1K instr.,
even/odd interleaving
System Interconnect:
4-port Xbar router
topology independent
32GB/sec total bandwidth
D$
I$
L2$
ICS
CPU
D$
I$
L2$
L2$
CPU
D$
I$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
RE
HE
Router
4 Links
@ 8GB/s

## Slide 70: Piranha Processing Node
CPU
Alpha core:
1-issue, in-order,
500MHz
L1 caches:
I&D, 64KB, 2-way
Intra-chip switch (ICS)
32GB/sec, 1-cycle delay
L2 cache:
shared, 1MB, 8-way
Memory Controller (MC)
RDRAM, 12.8GB/sec
Protocol Engines (HE & RE):
prog., 1K instr.,
even/odd interleaving
System Interconnect:
4-port Xbar router
topology independent
32GB/sec total bandwidth
D$
I$
L2$
ICS
CPU
D$
I$
L2$
L2$
CPU
D$
I$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
L2$
L2$
CPU
D$
I$
L2$
CPU
D$
I$
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
MEM-CTL
RE
HE
Router
Single Chip

## Slide 71: Piranha Processing Node

## Slide 72: Inter-Node Coherence Protocol Engine

## Slide 73: Piranha System

## Slide 74: Piranha I/O Node

## Slide 75: Sun Niagara (UltraSPARC T1)
Kongetira et al., “Niagara: A 32-Way Multithreaded SPARC Processor,” IEEE Micro 2005.

## Slide 76: Niagara Core
4-way fine-grain multithreaded, 6-stage, dual-issue in-order
Round robin thread selection (unless cache miss)
Shared FP unit among cores

## Slide 77: Niagara Design Point
Also designed for commercial applications

## Slide 78: Sun Niagara II (UltraSPARC T2)
8 SPARC cores, 8 threads/core. 8 stages. 16 KB I$ per Core. 8 KB D$ per Core. FP, Graphics, Crypto, units per Core.
4 MB Shared L2, 8 banks, 16-way set associative.
4 dual-channel FBDIMM memory controllers.
X8 PCI-Express @ 2.5 Gb/s.
Two 10G Ethernet ports @ 3.125 Gb/s.

## Slide 79: Chip Multithreading (CMT)
Spracklen and Abraham, “Chip Multithreading: Opportunities and Challenges,” HPCA Industrial Session, 2005.
Idea: Chip multiprocessor where each core is multithreaded
  Niagara 1/2: fine grained multithreading
  IBM POWER5: simultaneous multithreading
Motivation: Tolerate memory latency better
  A simple core stays idle on a cache miss
  Multithreading enables tolerating cache miss latency when there is TLP

## Slide 80: CMT (CMP + MT) vs. CMP
Advantages of adding multithreading to each core
  + Better memory latency tolerance when there are enough threads
  + Fine grained multithreading can simplify core design (no need for branch prediction, dependency checking)
  + Potentially better utilization of core, cache, memory resources
  + Shared instructions and data among threads not replicated
  + When one thread is not using a resource, another can
Disadvantages
  - Reduced single-thread performance (a thread does not have the core and L1 caches to itself)
  - More pressure on the shared resources (cache, off-chip bandwidth)  more resource contention
  - Applications with limited TLP do not benefit

## Slide 81: Sun ROCK
Chaudhry et al., “Rock: A High-Performance Sparc CMT Processor,” IEEE Micro, 2009.
Chaudhry et al., “Simultaneous Speculative Threading: A Novel Pipeline Architecture Implemented in Sun's ROCK Processor,” ISCA 2009
Goals:
  Maximize throughput when threads are available
  Boost single-thread performance when threads are not available and on cache misses
Ideas:
  Runahead on a cache miss  ahead thread executes miss-independent instructions, behind thread executes dependent instructions
  Branch prediction (gshare)

## Slide 82: Sun ROCK
16 cores, 2 threads per core (fewer threads than Niagara 2)
4 cores share a 32KB instruction cache
2 cores share a 32KB data cache
2MB L2 cache (smaller than Niagara 2)

## Slide 83: Sun ROCK Cores
Load miss in L1 cache starts parallelization using 2 HW threads
Ahead thread
  Checkpoints state and executes speculatively
  Instructions independent of load miss are speculatively executed
  Load miss(es) and dependent instructions are deferred to behind thread
Behind thread
  Executes deferred instructions and re-defers them if necessary
Memory-Level Parallelism (MLP)
  Run ahead on load miss and generate additional load misses
Instruction-Level Parallelism (ILP)
  Ahead and behind threads execute independent instructions from different points in program in parallel

## Slide 84: ROCK Pipeline

## Slide 85: More Powerful Cores in Sun ROCK
Advantages
  + Higher single-thread performance (MLP + ILP)
  + Better cache miss tolerance  Can reduce on-chip cache sizes
Disadvantages
  - Bigger cores  Fewer cores  Lower parallel throughput (in terms of threads).
  How about each thread’s response time?
  - More complex than Niagara cores (but simpler than conventional out-of-order execution)  Longer design time?

## Slide 86: More Powerful Cores in Sun ROCK
Chaudhry talk, Aug 2008.

## Slide 87: More Powerful Cores in Sun ROCK
Chaudhry et al., “Simultaneous Speculative Threading: A Novel Pipeline Architecture Implemented in Sun's ROCK Processor,” ISCA 2009

## Slide 88: IBM POWER4
Tendler et al., “POWER4 system microarchitecture,” IBM J R&D, 2002.
Another symmetric multi-core chip…
But, fewer and more powerful cores

## Slide 89: IBM POWER4
2 cores, out-of-order execution
100-entry instruction window in each core
8-wide instruction fetch, issue, execute
Large, local+global hybrid branch predictor
1.5MB, 8-way L2 cache
Aggressive stream based prefetching

## Slide 90: IBM POWER5
  Kalla et al., “IBM Power5 Chip: A Dual-Core Multithreaded Processor,” IEEE Micro 2004.

## Slide 91: IBM POWER6
Le et al., “IBM POWER6 microarchitecture,” IBM J R&D, 2007.
2 cores, in order, high frequency (4.7 GHz)
8 wide fetch
Simultaneous multithreading in each core
Runahead execution in each core
  Similar to Sun ROCK

## Slide 92: IBM POWER7
Kalla et al., “Power7: IBM’s Next-Generation Server Processor,” IEEE Micro 2010.
8 out-of-order cores, 4-way SMT in each core
TurboCore mode
  Can turn off cores so that other cores can be run at higher frequency

## Slide 93: Large vs. Small Cores
Out-of-order
Wide fetch e.g. 4-wide
Deeper pipeline
Aggressive branch predictor (e.g. hybrid)
Multiple functional units
Trace cache
Memory dependence speculation
In-order
Narrow Fetch e.g. 2-wide
Shallow pipeline
Simple branch predictor (e.g. Gshare)
Few functional units
Large Core
Small Core
Large Cores are power inefficient: e.g., 2x performance for 4x area (power)

## Slide 94: Large vs. Small Cores
Grochowski et al., “Best of both Latency and Throughput,” ICCD 2004.

## Slide 95: Tile-Large Approach
Tile a few large cores
IBM Power 5, AMD Barcelona, Intel Core2Quad, Intel Nehalem
+ High performance on single thread, serial code sections (2 units)
- Low throughput on parallel program portions (8 units)
Large core
Large core
Large
core
Large core
“Tile-Large”

## Slide 96: Tile-Small Approach
Tile many small cores
Sun Niagara, Intel Larrabee, Tilera TILE (tile ultra-small)
+ High throughput on the parallel part (16 units)
- Low performance on the serial part, single thread (1 unit)
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
“Tile-Small”

## Slide 97: Can We Get the Best of Both worlds?
Tile Large
+ High performance on single thread, serial code sections (2 units)
- Low throughput on parallel program portions (8 units)
Tile Small
+ High throughput on the parallel part (16 units)
- Low performance on the serial part, single thread (1 unit), reduced single-thread performance compared to existing single thread processors
Idea: Have both large and small on the same chip  Performance asymmetry

## Slide 98: Asymmetric Chip Multiprocessor (ACMP)
Provide one large core and many small cores
+ Accelerate serial part using the large core (2 units)
+ Execute parallel part on all cores for high throughput (14 units)
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Large
core
ACMP
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
“Tile-Small”
Large core
Large core
Large
core
Large core
“Tile-Large”