## Slide 1: AI Chip & Systems. Lecture 6: Graphics Processing Units
Prof. Zeke Wang
Zhejiang University
April 9 2026

## Slide 2: Recall: Comparison of Memories
SRAM
HBM
DDR
SSD
DISK
Capacity
SRAM
HBM
DDR
SSD
DISK
Latency
Bandwidth
~10MB
~10GB
~100GB
~1TB
~10TB
~1ns
~100ns
~100ns
~1us
~1ms
~100GB/s
DISK
SSD
DDR
HBM
SRAM
~10MB/s
~1GB/s
~10GB/s
~1TB/s

## Slide 3: Recall: FF vs. SRAM vs. DRAM vs. SSD
Flip-Flops (~K)
  Very fast, parallel access
  Very expensive (one bit costs tens of transistors)
Static RAM (~M)
  Relatively fast, only one data word at a time
  Expensive (one bit costs 6+ transistors)
Dynamic RAM (~G)
  Slower, one data word at a time, reading destroys content (refresh), needs special process for manufacturing
  Cheap (one bit costs only one transistor plus one capacitor)
Flash Memory (~T)
  Much slower, access takes a long time, non-volatile
  Very cheap (one transistor stores 16 bits or no transistors involved)

## Slide 4: Recall: SRAM Summary
SRAM
  Goal: buffering data on chip to reduce external memory traffic
  Advantage: random access still keeps high performance
  Disadvantage: low capacity (multiple MBs)
Where to Use SRAM?
  Cache in CPU
  Shared memory in GPU
  On-chip buffer in AI accelerator
How to Use SRAM?
  Multiple small separate SRAMs: low latency and high throughput
  Banked design: wide access ports

## Slide 5: Recall: A Large Fraction of CPU is SRAM
SRAM (Cache) in a CPU
  Half chip area is occupied by cache
  10MB (2.5MB/core * 4 cores)

## Slide 6: Recall: DRAM Capacity, Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x

## Slide 7: Recall: Key Messages behind Memory
Memory Optimizations aim at size, bandwidth, not latency.
A memory read/write may need a few DDR operations, e.g., ACTIVATE, Column, Prechange, within a memory chip…
Different access sequence leads to different throughput, sequential (mainly row buffer hit) > random (mainly row buffer miss).
Random access is slow due to low row buffer miss rate.

## Slide 8: Recall: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 9: Recall: HBM
HBM stack:
  It is used in conjunction with high-end GPUs, AI ASICs and FPGAs.
  Each stack has 4/8 DRAM dies and a logic die.
Notes: Substrate: 底座
Interposer: 插入式选样

## Slide 10: Recall: HBM in Nvidia A100
A100 GPU: 6 HBM2 stacks at the left/right side.

## Slide 11: Recall: Advantage and Disadvantage of HBM
Advantage of HBM:
  High bandwidth: ~500GB/s per stack.
  Low power consumption: due to running without termination.
Disadvantage of HBM:
  Less flexibility: fixed, in the same package with compute chip.
  Low capacity: really close to compute chip.
  High cost: strict condition.
Notes: Termination is needed when CPU is long away from memory. However, HBM is close to accelerator, so termination is not needed.

## Slide 12: Recall: NVME SSD
Advantage: Large memory size, e.g., 16TB per SSD
Disadvantage: Low throughput, high latency, hard to use
Samsung PM853T 960GB Enterprise SSD (from https://www.tweaktown.com/reviews/6695/samsung-pm853t-960gb-enterprise-ssd-review/index.html)
Core
Core
Core
HW
Flash Ctrl.
HW
Flash Ctrl.
HW
Flash Ctrl.
HW
Flash Ctrl.
Request Handler
ECC/Randomizer
Encryption Engine
SSD Controller
NAND Packages
8×128 GB = 1 TB
LPDDR DRAM
0.001×1,024 = 1 GB

## Slide 13: Recall: Comparison of Memories
SRAM
HBM
DDR
SSD
DISK
Capacity
SRAM
HBM
DDR
SSD
DISK
Latency
Bandwidth
~10MB
~10GB
~100GB
~1TB
~10TB
~1ns
~100ns
~100ns
~1us
~1ms
~100GB/s
DISK
SSD
DDR
HBM
SRAM
~10MB/s
~1GB/s
~10GB/s
~1TB/s

## Slide 14: Where Are We?

## Slide 15: Agenda for Today
Why GPU?
Hardware Execution Model
Programming Model
  SISD vs. SIMD vs. SPMD
  GPU Programming Example
Advance
  SIMT (Hardware) & Warp (Software)

## Slide 16
Motivation of In-network Computing
Why GPU?
Need More Computing Power.

## Slide 17: OpenAI: Compute Power Needed by NN Model
Model | Model Size | Compute/iteration (OPs)
VGG 19 | 114M | ~19.6 B
“GPT-3” | 175B | ~250 T
One Forward Pass of Model:
Chart: Throughput (GOPs/s)
One-cycle CPU | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01
Pipeline CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD CPU | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
GPU | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000 | 20000
VGG19 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6 | 19.6
GPT-3 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000 | 250000
Notes: KB MB GB TB
K M B T
1B=10亿

## Slide 18: CPU vs GPU： Compute Perspective
CPU:
  Few complex cores
  Larger cache for low memory latency
  Large and slow memory
GPU:
  Lots of simple cores
  Small cache for low memory latency
  Small and fast memory

## Slide 19: State-of-the-art CPU GPU and FPGA
 | Cores (Threads) | TFLOPS | Memory Size (Bandwidth) | PCIe | Network
CPU (AMD Threadripper 3995WX) | 64 (128) | 2.8 (FP32), 1.4 (FP64) | 512GB (80GB/s) | 32.0GB/s (PCIe 4.0 X16) | No
GPU (Nvidia H100) | 18432 (128K) | 67 (FP32), 34 (FP64), 989 (FP32, Tensor), 1979 (FP16, Tensor) | 80GB (3350GB/s) | 64.0GB/s (PCIe 5.0 X16) | No
FPGA (U280) | 9,024 (25x18 MULs) | 1.8 (FP32) | 40GB (460GB/s) | 16.0GB/s (PCIe 4.0 X8) | Yes
Notes: KB MB GB TB
K M B T E P
1B=10亿

## Slide 20: Relationship between CPU and GPU
PCI Bus
CPU
GPU

## Slide 21
Motivation of In-network Computing
More cores  More trouble
Challenge: How to manipulate them?
Notes: 之前千核项目 很多，只活了英伟达。

## Slide 22: GPU Computing
Key Idea:
  Computation is offloaded to the GPU
Three steps:
  CPU-GPU data transfer (1)
  GPU kernel execution (2)
  GPU-CPU data transfer (3)

## Slide 23: Programming Model: CPU and GPU
CPU-GPU Co-processing:
  CPU: Sequential or modestly parallel sections
  GPU: Massively parallel sections
Serial Code (CPU):
. . .
. . .
Parallel Kernel (GPU):
KernelA<<<nBlk, nThr>>>(args);
Serial Code (CPU):
Parallel Kernel (GPU):
KernelB<<<nBlk, nThr>>>(args);

## Slide 24: Recall: Amdahl’s Law
Amdahl’s Law
  f: Parallelizable fraction of a program
  N: Number of processors
Serial bottleneck of Amdahl’s Law:
  Maximum speedup (1/(1-f)) limited by serial portion (1 - f)
Parallel portion (f) is usually not perfectly parallel
  Synchronization overhead (e.g., updates to shared data)
  Load imbalance overhead (imperfect parallelization)
  Resource sharing overhead (contention among N processors)
Speedup =
1
+
1 - f
f
N
  Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” 1967.

## Slide 25: GPUs are SIMD Engines Underneath
The instruction pipeline operates like a SIMD pipeline (e.g., an array processor)
However, the programming is done using threads, NOT SIMD instructions
To understand this, let’s go back to our parallelizable code example
But, before that, let’s distinguish between
  Programming Model (Software)
  vs.
  Execution Model (Hardware)

## Slide 26: Programming Model vs. Hardware Execution Model
Programming Model： how the programmer expresses the code
  E.g., Sequential (von Neumann), Data Parallel (SIMD), Dataflow, Multi-threaded (MIMD, SPMD), …
Hardware Execution Model： how the hardware executes the code underneath
  E.g., Out-of-order execution, Vector processor, Array processor, Dataflow processor, Multiprocessor, Multithreaded processor, …
Discussion: Execution Model can be very different from Programming Model
  E.g., von Neumann model implemented by an OoO processor
  E.g., SPMD model implemented by a SIMD processor (a GPU)

## Slide 27: GPU: Programming Model vs. Hardware Execution Model
Hardware Execution Model
CUDA Programming Model
Streaming
Multi-processor
GPU
CUDA core
Thread
Thread block
Grid
...

## Slide 28: Agenda for Today
Where is GPU? & Key Message
Hardware Execution Model
Programming Model
  SISD vs. SIMD vs. SPMD
  GPU Programming Example
Advance
  SIMT (Hardware) & Warp (Software)

## Slide 29: A Many-core GPU (Hardware Execution Model)

## Slide 30: NVIDIA GeForce GTX 285
NVIDIA-speak:
  240 stream processors (CUDA cores)
  “SIMT execution”
Generic speak:
  30 cores
  8 SIMD functional units per core
NVIDIA, “NVIDIA GeForce GTX 200 GPU. Architectural Overview. White Paper,” 2008.
Slide credit: Kayvon Fatahalian
Notes: Link to the GTX 200 series white paper:
https://www.nvidia.com/docs/IO/55506/GeForce_GTX_200_GPU_Technical_Brief.pdf
The NVIDIA GeForce GTX 285 was launched on January 2009.

## Slide 31: NVIDIA GeForce GTX 285 “core”(SM)
…
= instruction stream decode
= SIMD functional unit, control
shared across 8 units
= execution context storage
= multiply-add
= multiply
64 KB of storage
for thread contexts (registers)
Slide credit: Kayvon Fatahalian
Notes: 30 * 32 * 32 = 30 * 1024 = 30K fragments
64KB register file = 16 32-bit registers per thread = 64B (1/32 that of LRB)
16KB of shared scratch
80KB / core available to software

## Slide 32: NVIDIA GeForce GTX 285
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
30 cores on the GTX 285: 30K threads
Slide credit: Kayvon Fatahalian
Notes: If you’re running a CUDA program, and your not launching 30K threads, you are certainly not getting full latency hiding, and you might not be using the GPU well

## Slide 33: Evolution of NVIDIA GPUs: Compute

## Slide 34: NVIDIA V100
NVIDIA-speak:
  5120 stream processors (CUDA cores)
  “SIMT execution”
Generic speak:
  80 cores
  64 SIMD functional units per core
  Tensor cores for Machine Learning
NVIDIA, “NVIDIA Tesla V100 GPU Architecture. White Paper,” 2017.
Notes: CUDA core： stream processor

## Slide 35: NVIDIA V100 Block Diagram
80 cores on the V100
https://devblogs.nvidia.com/inside-volta/

## Slide 36: NVIDIA A100
NVIDIA-speak:
  6912 stream processors (CUDA cores)
  “SIMT execution”
Generic speak:
  108 cores
  64 SIMD functional units per core
  Tensor cores for Machine Learning
    Support for sparsity
    New floating point data type (TF32)
https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/
Notes: 5 HBM2 stacks, 10 512-bit memory controllers
Sparsity is possible in deep learning because the importance of individual weights evolves during the learning process, and by the end of network training, only a subset of weights have acquired a meaningful purpose in determining the learned output. The remaining weights are no longer needed (see https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/).
TensorFloat-32 (TF32) uses 8 bit for exponent and 10 bits for mantissa. This way, TF32 provides the range of FP32 with the precision of FP16 (see https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/).

## Slide 37: NVIDIA A100 Block Diagram
108 cores on the A100
(Up to 128 cores in the full-blown chip)
40MB L2 cache
https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/
Notes: The A100 GPU includes 40 MB of L2 cache, which is 6.7x larger than V100 L2 cache.The L2 cache is divided into two partitions to enable higher bandwidth and lower latency memory access. Each L2 partition localizes and caches data for memory accesses from SMs in the GPCs directly connected to the partition. This structure enables A100 to deliver a 2.3x L2 bandwidth increase over V100 (see https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/).

## Slide 38: NVIDIA H100
NVIDIA-speak:
  8448 stream processors (CUDA cores)
  “SIMT execution”
Generic speak:
  132 cores
  64 SIMD functional units per core
  Tensor cores for Machine Learning
    Support for sparsity
    Support for transformer
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/
Notes: 5 HBM2 stacks, 10 512-bit memory controllers
Sparsity is possible in deep learning because the importance of individual weights evolves during the learning process, and by the end of network training, only a subset of weights have acquired a meaningful purpose in determining the learned output. The remaining weights are no longer needed (see https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/).
TensorFloat-32 (TF32) uses 8 bit for exponent and 10 bits for mantissa. This way, TF32 provides the range of FP32 with the precision of FP16 (see https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/).

## Slide 39: NVIDIA H100 Block Diagram
https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/
Notes: The A100 GPU includes 40 MB of L2 cache, which is 6.7x larger than V100 L2 cache.The L2 cache is divided into two partitions to enable higher bandwidth and lower latency memory access. Each L2 partition localizes and caches data for memory accesses from SMs in the GPCs directly connected to the partition. This structure enables A100 to deliver a 2.3x L2 bandwidth increase over V100 (see https://developer.nvidia.com/blog/nvidia-ampere-architecture-in-depth/).

## Slide 40: GPU Trend: H100 vs. A100
 | FP8 | FP16 | FP32 | FP64 | Memory bandwidth | Memory capacity
H100 | 4000T | 2000T | 1000T | 60T | 3TB/s | 80GB
A100 | 666T | 666T | 333T | 20T | 2TB/s | 80GB
Compute power scales well.
GPU memory capacity does not scale well.
Notes: 军迷：
算力：武器 坦克等
内存：后勤

## Slide 41: Agenda for Today
Where is GPU? & Key Message
Hardware Execution Model
Programming Model
  SISD vs. SIMD vs. SPMD
  GPU Programming Example
Advance
  SIMT (Hardware) & Warp (Software)

## Slide 42: How Can You Exploit Parallelism Here?
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Let’s examine three programming options to exploit instruction-level parallelism present in this sequential code:
1. Sequential (SISD)
2. Data-Parallel (SIMD)
3. Multithreaded (SPMD)

## Slide 43: Prog. Model 1: Sequential (SISD)
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Can be executed on thee processors:
1, Pipelined processor
2, Out-of-order execution processor
  Independent instructions executed when ready
  Different iterations are present in the instruction window and can execute in parallel in multiple functional units
3, Superscalar or VLIW processor
  Can fetch and execute multiple instructions per cycle
for (i=0; i < N; i++)
C[i] = A[i] + B[i];

## Slide 44: Prog. Model 2: Data Parallel (SIMD)
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Motivation: Each iteration is independent
Idea: Programmer or compiler generates a SIMD instruction to execute the same instruction from all iterations across different data
VLD A  V1
VLD B  V2
VADD V1 + V2  V3
VST V3  C

## Slide 45: Prog. Model 3: Multithreaded
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Motivation: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)

## Slide 46: Prog. Model 3: Multithreaded
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Realization: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)
This programming model (software) is called:
SPMD: Single Program Multiple Data

## Slide 47: SPMD
SPMD: Single procedure/program, multiple data
  This is a programming model rather than computer organization
Each processing element executes the same procedure, except on different data elements
  Procedures can synchronize at certain points in program, e.g. barriers
Key Idea of SPMD: multiple instruction streams execute the same program
  Each program/procedure 1) works on different data, 2) can execute a different control-flow path, at run-time
  Many scientific applications are programmed this way and run on MIMD hardware (multiprocessors)
  Modern GPUs programmed in a similar way on a SIMD hardware

## Slide 48: Agenda for Today
Where is GPU? & Key Message
Hardware Execution Model
Programming Model
  SISD vs. SIMD vs. SPMD
  GPU Programming Example
Advance
  SIMT (Hardware) & Warp (Software)

## Slide 49: CUDA/OpenCL Programming Model
Single Program Multiple Data (SPMD), e.g., CUDA
  Bulk synchronous programming: Global (coarse-grain) synchronization between kernels
The device (typically GPU) executes CUDA kernels
  Grid
  Thread Block
    CUDA runtime schedules at granularity of thread block.
    A thread block is a programming abstraction that represents a group of threads that can be executed in parallel.
    Within a block, shared memory, and synchronization.
  Thread
    A thread corresponds to an iteration.

## Slide 50: GPU: Programming Model vs. Hardware Execution Model
Hardware Execution Model
CUDA Programming Model
Streaming
Multi-processor
GPU
CUDA core
Thread
Thread block
Grid
...
Notes: Wrap

## Slide 51: CUDA: Memory Hierarchy

## Slide 52: Traditional Program Structure in CUDA
Function prototypes
  float serialFunction(…);
  __global__ void kernel(…);
main()
  1) Allocate memory space on the device – cudaMalloc(&d_in, bytes);
  2) Transfer data from host to device – cudaMemCpy(d_in, h_in, …);
  3) Execution configuration setup: #blocks and #threads
  4) Kernel call – kernel<<<execution configuration>>>(args…);
  5) Transfer results from device to host – cudaMemCpy(h_out, d_out, …);
Kernel – __global__ void kernel(type args,…)
      Automatic variables transparently assigned to registers
      Shared memory: __shared__
      Intra-block synchronization: __syncthreads();
Repeat as needed
Slide credit: Hwu & Kirk

## Slide 53: CUDA Programming Language
Memory allocation
  cudaMalloc((void**)&d_in, #bytes);
Memory copy
  cudaMemcpy(d_in, h_in, #bytes, cudaMemcpyHostToDevice);
Kernel launch
  kernel<<< #blocks, #threads >>>(args);
Memory deallocation
  cudaFree(d_in);
Explicit synchronization
  cudaDeviceSynchronize();

## Slide 54: First GPU Example: Vector Addition (I)
Key Idea: one GPU thread to each element-wise addition

## Slide 55: First GPU Example: Vector Addition (II)
A grid: the whole set of threads
We need a way to assign threads to GPU cores

## Slide 56: First GPU Example: Vector Addition (III)
We group threads into blocks
Block 0
Block 1
Block 2
Block 3
blockIdx = 0
blockIdx = 1
blockIdx = 2
blockIdx = 3
threadIdx = 0
threadIdx = 1
threadIdx = 2
threadIdx = 2
blockDim = 4
Notes: 每个block有四个threads。
blockIdx = 0

## Slide 57: GPU: Programming Model vs. Hardware Execution Model
Hardware Execution Model
CUDA Programming Model
Streaming
Multi-processor
GPU
CUDA core
Thread
Thread block
Grid
...
Notes: Wrap

## Slide 58: Host Code Example: Vector Addition
void vecadd(float* A, float* B, float* C, int N) {
//1, Allocate GPU memory
float *A_d, *B_d, *C_d;
cudaMalloc((void**) &A_d, N*sizeof(float));
cudaMalloc((void**) &B_d, N*sizeof(float));
cudaMalloc((void**) &C_d, N*sizeof(float));
//2, Copy data to GPU memory
cudaMemcpy(A_d, A, N*sizeof(float), cudaMemcpyHostToDevice);
cudaMemcpy(B_d, B, N*sizeof(float), cudaMemcpyHostToDevice);
//3, Perform computation on GPU
...
//4, Copy data from GPU memory
cudaMemcpy(C, C_d, N*sizeof(float), cudaMemcpyDeviceToHost);
//5, Deallocate GPU memory
cudaFree(A_d);
cudaFree(B_d);
cudaFree(C_d);
}
Slide credit: Izzat El Hajj
const unsigned int numThreadsPerBlock = 512;
const unsigned int numBlocks = N/numThreadsPerBlock;
vecadd_kernel<<<numBlocks, numThreadsPerBlock>>>(A_d, B_d, C_d, N);

## Slide 59: Kernel Code Example: Vector Addition
Slide credit: Izzat El Hajj
__global__ void vecadd_kernel(float* A, float* B, float* C, int N) {
int i = blockDim.x*blockIdx.x + threadIdx.x;
C[i] = A[i] + B[i];
}
blockDim: block dimension
blockIdx: block index within a grid
threadIdx: thread index within a block

## Slide 60: Boundary Conditions
Question: What if the size of the input is not a multiple of the number of threads per block?
  Solution: use the ceiling to launch extra threads then omit the threads after the boundary
Host code:
Kernel code:
const unsigned int numBlocks = (N +numThreadsPerBlock – 1)/numThreadsPerBlock;
__global__ void vecadd_kernel(float* A, float* B, float* C, int N) {
int i = blockDim.x*blockIdx.x + threadIdx.x;
if(i < N) {
C[i] = A[i] + B[i]; }
}
vecadd_kernel<<<numBlocks, numThreadsPerBlock>>>(A_d, B_d, C_d, N);

## Slide 61: Sample GPU Program: Matrix Multiplication
Slide credit: Hyesoon Kim

## Slide 62: Indexing and Memory Access
Images are 2D data structures
  height x width
  Image[j][i], where 0 ≤ j < height, and 0 ≤ i < width
Image[0][1]
Image[1][2]
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 63: Image Layout in Memory
Row-major layout
  Image[j][i] = Image[j x width + i]
Image[0][1] = Image[0 x 8 + 1]
Image[1][2] = Image[1 x 8 + 2]
Stride = width

## Slide 64: Indexing and Memory Access: 1D Grid
One GPU thread per pixel
Grid of Blocks of Threads
  gridDim.x, blockDim.x
  blockIdx.x, threadIdx.x
Block 0
Block 0
Thread 0
Thread 1
Thread 2
Thread 3
blockIdx.x
threadIdx.x
blockIdx.x * blockDim.x + threadIdx.x
6 * 4 + 1 = 25

## Slide 65: Agenda for Today
Where is GPU? & Key Message
Hardware Execution Model
Programming Model
  SISD vs. SIMD vs. SPMD
  GPU Programming Example
Advance
  SIMT (Hardware) & Warp (Software)

## Slide 66: GPU: Programming Model vs. Hardware Execution Model
Hardware Execution Model
CUDA Programming Model
Streaming
Multi-processor
GPU
CUDA core
Thread
Thread block
Grid
...
Wrap
SIMT
Notes: SIMD Wrap

## Slide 67: SIMT (Hardware) & Warp (Software)
SIMT: Single Instruction Multiple Thread
  Key Feature: 16 CUDA cores in a SM are executed in a lock step.
Warp:
  A warp, a basic execution unit, consists of 32 consecutive threads
  A thread block is divided into warps for SIMT execution.
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0’s warps
Block 1’s warps
…
t0 t1 t2 … t31
…
Block 2’s warps

## Slide 68
Motivation of In-network Computing
Why SIMT and Warp?
Reduce GPU scheduling overhead

## Slide 69: How to Form Warps?
Warp 0 at PC X+3
Warp 0 at PC X+2
Warp 0 at PC X+1
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Warp 0 at PC X
Warp: A set of threads that execute
the same instruction (i.e., at the same PC)
Iter. 32

## Slide 70: Mapping Warps on a SIMT Hardware
Warp:
  A thread block is divided into warps.
  A warp executes the same instruction on different data elements
SIMT Pipeline:
  16 CUDA cores are executed in a lock step to serve each warp.
Thread Warp 0
Thread Warp 8
Thread Warp 7
Thread Warp
Scalar
Thread
0
Scalar
Thread
1
Scalar
Thread
2
Scalar
Thread
31
Common PC
SIMT Pipeline
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.
Notes: In SIMD, you need to specify the data array + an instruction (on which to operate the data on) + THE INSTRUCTION WIDTH. Eg: You might want to add 2 integer arrays of length 16, then a SIMD instruction would look like (the instruction has been cooked-up by me for demo) add.16 arr1 arr2 However, SIMT doesn't bother about the instruction width. So, essentially, you could write the above example as: arr1[i] + arr2[i] and then launch as many threads as the length of the array, as you want. Note that, if the array size was, let us say, 32, then SIMD EXPECTS you to explicitly call two such 'add.16' instructions! Whereas, this is not the case with SIMT.

## Slide 71: GPU Execution with Warps
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Warp 0 at PC X
Assume: a warp consists of 32 threads
If you have 32K iterations, and 1 iteration/thread  1K warps
Warps can be interleaved on the same pipeline  Fine grained multithreading of warps.
Warp 1 at PC X
Iter. 33
Iter. 34
Warp 20 at PC X+2
Iter.
20*32 + 1
Iter.
20*32 + 2

## Slide 72: Warp Instruction Level Parallelism
Can overlap execution of multiple instructions
  Example machine has 32 threads per warp and 8 lanes
  Completes 24 operations/cycle while issuing 1 warp/cycle
W3
W0
W1
W4
W2
W5
Load Unit
Multiply Unit
Add Unit
time
Warp issue
Slide credit: Krste Asanovic

## Slide 73
Motivation of In-network Computing
SIMT is not SIMD!

## Slide 74: SIMD vs. SIMT Execution Model
SIMD: A single sequential instruction stream of SIMD instructions  each instruction specifies multiple data inputs
  [VLD, VLD, VADD, VST], VLEN
SIMT: Multiple instruction streams of scalar instructions  threads grouped dynamically into warps
  [LD, LD, ADD, ST], NumThreads
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently on any type of scalar pipeline  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing

## Slide 75: SPMD: Genius Abstraction
Slide credit: Hyesoon Kim
GPUs were invented and gpus are a kind vector computer which is really wild because while gpus have big vectors they essentially run scalar programs on each element and you can think of them as running a vector of scalar programs which by the way was a genius abstraction because everybody can write a scalar program almost nobody can write a vector program but suddenly we had all kinds of people doing vector programs on GPUs”
--- Jim Keller @DAC’24

## Slide 76: SIMT Code vs. SIMD Code
for (ii = 0; ii < 100000; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100000 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU scalar code
CUDA code
Slide credit: Hyesoon Kim
// there are 25000 loops with SIMD=4
…
v_A = vec_load (A);
v_B = vec_load (B);
v_C = vec_add(v_A, v_B);
Vec_store(v_C, C)
…
}
CPU vector code

## Slide 77: Warp-based SIMD vs. Traditional SIMD
Traditional SIMD contains a single thread
  Sequential instruction execution; lock-step operations in a SIMD instruction
  Programming model is SIMD (no extra threads)  SW needs to know vector length
  ISA contains vector/SIMD instructions
Warp-based SIMD consists of multiple scalar threads executing in a SIMD manner (i.e., same instruction executed by all threads)
  Does not have to be lock step
  Each thread can be treated individually (i.e., placed in a different warp)  programming model not SIMD
    SW does not need to know vector length
    Enables multithreading and flexible dynamic grouping of threads
  ISA is scalar  SIMD operations can be formed dynamically
  Essentially, it is SPMD programming model implemented on SIMD hardware

## Slide 78: Threads Can Take Different Paths in Warp-based SIMD
Each thread can have conditional control flow instructions
Threads can execute different control flow paths
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B
C
D
E
F
A
G
Slide credit: Tor Aamodt

## Slide 79: Control Flow Problem in GPUs/SIMT
A GPU uses a SIMD pipeline to save area on control logic
  Groups scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths
Branch
Path A
Path B
Branch
Path A
Path B
Slide credit: Tor Aamodt

## Slide 80: SIMD Utilization
Intra-warp divergence
Compute(threadIdx.x);
if (threadIdx.x % 2 == 0){
Do_this(threadIdx.x);
}
else{
Do_that(threadIdx.x);
}

## Slide 81: Increasing SIMD Utilization
Divergence-free execution
Compute(threadIdx.x);
if (threadIdx.x < 32){
Do_this(threadIdx.x * 2);
}
else{
Do_that((threadIdx.x%32)*2+1);
}

## Slide 82: Vector Reduction: Naïve Mapping (I)
0
1
2
3
4
5
7
6
10
9
8
11
0+1
2+3
4+5
6+7
10+11
8+9
0...3
4..7
8..11
0..7
8..15
1
2
3
iterations
Thread 0
Thread 8
Thread 2
Thread 4
Thread 6
Thread 10
Slide credit: Hwu & Kirk
…

## Slide 83: Vector Reduction: Naïve Mapping (II)
Program with low SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for (int stride = 1; stride < blockDim.x; stride *= 2) {
  __syncthreads();
  if (t % (2*stride) == 0)
  partialSum[t] += partialSum[t + stride];
  }

## Slide 84: Divergence-Free Mapping (I)
All active threads belong to the same warp
Thread 0
0
1
2
3
…
13
15
14
18
17
16
19
0+16
15+31
1
2
3
Thread 1
Thread 2
Thread 14
Thread 15
iterations
Slide credit: Hwu & Kirk
…

## Slide 85: Divergence-Free Mapping (II)
Program with high SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for (int stride = blockDim.x; stride > 0; stride >> 1){
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t + stride];
  }

## Slide 86: Programming Model vs. Hardware Execution Model
Hardware Programming Model
Programming Model
Core
Streaming
Multi-processor
GPU
CUDA core:
Thread
Thread block (s)
Wrap
Thread blocks

## Slide 87: NVIDIA H100 Block Diagram
144 cores on the full GH100
60MB L2 cache
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/

## Slide 88: NVIDIA H100 Core
48 TFLOPS Single Precision*
24 TFLOPS Double Precision*
800 TFLOPS (FP16, Tensor Cores)*
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/
* Preliminary performance estimates

## Slide 89: NVIDIA H100 Tensor Memory Accelerator
Asynchronous memory copy with LDGSTS instruction vs. TMA
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/
TMA unit reduces addressing overhead
A single thread per warp issues the TMA operation
Support for different tensor layouts (1D-5D)
Notes: New asynchronous execution features include a new Tensor Memory Accelerator (TMA) unit that can transfer large blocks of data efficiently between global memory and shared memory. TMA also supports asynchronous copies between thread blocks in a cluster. There is also a new asynchronous transaction barrier for doing atomic data movement and synchronization.
  New asynchronous execution features include a new Tensor Memory Accelerator (TMA) unit that can efficiently transfer large blocks of data between global memory and shared memory. TMA also supports asynchronous copies between thread blocks in a cluster. There is also a new asynchronous transaction barrier for doing atomic data movement and synchronization.

## Slide 90: NVIDIA H100 Distributed Shared Memory
Shared memory virtual address space distributed across the blocks of a cluster
Load, store, and atomic operations to other SM’s shared memory
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/
Thread block clusters and distributed shared memory (DSMEM) are leveraged via cooperative_groups API
TMA unit supports copies across thread blocks in a cluster
Asynchronous transaction barriers
Notes: Distributed shared memory allows direct SM-to-SM communications for loads, stores, and atomics across multiple SM shared memory blocks.
  Distributed shared memory enables direct SM-to-SM communications for loads, stores, and atomics across multiple SM shared memory blocks

## Slide 91: NVIDIA GeForce GTX 285 “core”
…
64 KB of storage
for thread contexts (registers)
Groups of 32 threads share instruction stream (each group is a Warp)
Up to 32 warps are simultaneously interleaved
Up to 1024 thread contexts can be stored
Slide credit: Kayvon Fatahalian
Notes: To get maximal latency hiding:
Run 1/32 of the time
16 words per thread = 64B