## Slide 1: AI Chip & Systems. Lecture 7: GPU Optimization
Prof. Zeke Wang
Zhejiang University
April 20 2026

## Slide 2: Recall: CPU vs GPU： Compute Perspective
CPU:
  Few complex cores
  Larger cache for low memory latency
  Large and slow memory
GPU:
  Lots of simple cores
  Small cache for low memory latency
  Small and fast memory

## Slide 3: Recall: Relationship between CPU and GPU
PCI Bus
CPU
GPU

## Slide 4: Recall: SPMD
SPMD: Single procedure/program, multiple data
  This is a programming model rather than computer organization
Each processing element executes the same procedure, except on different data elements
  Procedures can synchronize at certain points in program, e.g. barriers
Key Idea of SPMD: multiple instruction streams execute the same program
  Each program/procedure 1) works on different data, 2) can execute a different control-flow path, at run-time
  Many scientific applications are programmed this way and run on MIMD hardware (multiprocessors)
  Modern GPUs programmed in a similar way on a SIMD hardware

## Slide 5: Recall Programming Model vs. Hardware Execution Model
Hardware Execution Model
CUDA Programming Model
Streaming
Multi-processor
GPU
CUDA core
Thread
Thread block
Grid
...
Warp
SIMT
Notes: SIMD Wrap

## Slide 6: Recall: SIMT (Hardware) & Warp (Software)
SIMT: Single Instruction Multiple Thread
  More precisely, SIMD (Single Instruction Multiple Data)
  Key Feature: 16 CUDA cores in a SM are executed in a lock step.
Warp:
  A warp, a basic execution unit, consists of 32 consecutive threads
  A thread block is divided into warps for SIMT execution.
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0’s warps
Block 1’s warps
…
t0 t1 t2 … t31
…
Block 2’s warps

## Slide 7
Motivation of In-network Computing
Why SIMT and Warp?
Reduce GPU scheduling overhead

## Slide 8: Recall: Mapping Warps on a SIMT Hardware
Warp:
  A thread block is divided into warps.
  A warp executes the same instruction on different data elements
SIMT Pipeline:
  16 CUDA cores are executed in a lock step to serve each warp.
Thread Warp 0
Thread Warp 8
Thread Warp 7
Thread Warp
Scalar
Thread
0
Scalar
Thread
1
Scalar
Thread
2
Scalar
Thread
31
Common PC
SIMT Pipeline
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.
Notes: In SIMD, you need to specify the data array + an instruction (on which to operate the data on) + THE INSTRUCTION WIDTH. Eg: You might want to add 2 integer arrays of length 16, then a SIMD instruction would look like (the instruction has been cooked-up by me for demo) add.16 arr1 arr2 However, SIMT doesn't bother about the instruction width. So, essentially, you could write the above example as: arr1[i] + arr2[i] and then launch as many threads as the length of the array, as you want. Note that, if the array size was, let us say, 32, then SIMD EXPECTS you to explicitly call two such 'add.16' instructions! Whereas, this is not the case with SIMT.

## Slide 9: Recall: GPU Execution with Warps
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Warp 0 at PC X
Assume: a warp consists of 32 threads
If you have 32K iterations, and 1 iteration/thread  1K warps
Warps can be interleaved on the same pipeline  Fine grained multithreading of warps.
Warp 1 at PC X
Iter. 33
Iter. 34
Warp 20 at PC X+2
Iter.
20*32 + 1
Iter.
20*32 + 2

## Slide 10: Recall: Warp Instruction Level Parallelism
Can overlap execution of multiple instructions
  Example machine has 32 threads per warp and 8 lanes
  Completes 24 operations/cycle while issuing 1 warp/cycle
W3
W0
W1
W4
W2
W5
Load Unit
Multiply Unit
Add Unit
time
Warp issue
Slide credit: Krste Asanovic

## Slide 11
Motivation of In-network Computing
SIMT is not SIMD!

## Slide 12: Recall: SIMT Code vs. SIMD Code
for (ii = 0; ii < 100000; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100000 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU scalar code
CUDA code
Slide credit: Hyesoon Kim
// there are 25000 loops with SIMD=4
…
v_A = vec_load (A);
v_B = vec_load (B);
v_C = vec_add(v_A, v_B);
Vec_store(v_C, C)
…
}
CPU vector code

## Slide 13: Agenda for Today
SIMT (Hardware) & Warp (Software)
Optimization of Memory System
  Multi-threading
  Memory Coalescing
  Shared Memory
SIMT Efficiency
  Divergency
  Atomic
  CPU-GPU Transfer

## Slide 14: GPU Memories

## Slide 15: Memory in the GPU Architecture
…
SM
Core
Control
Core
Core
Core
Core
Core
Core
Core
SM
Core
Control
Core
Core
Core
Core
Core
Core
Core
SM
Core
Control
Core
Core
Core
Core
Core
Core
Core
L2 Cache
Global Memory
Registers
Shared Memory
L1 Cache
Constant Cache
Registers
Shared Memory
L1 Cache
Constant Cache
Registers
Shared Memory
L1 Cache
Constant Cache
≈1 cycle
≈5 cycles
≈5 cycles
≈500 cycles
Slide credit: Izzat El Hajj

## Slide 16: Memory in the GPU Architecture
…
SM
Core
Control
Core
Core
Core
Core
Core
Core
Core
SM
Core
Control
Core
Core
Core
Core
Core
Core
Core
SM
Core
Control
Core
Core
Core
Core
Core
Core
Core
L2 Cache
Global Memory
Registers
Shared Memory
L1 Cache
Constant Cache
Registers
Shared Memory
L1 Cache
Constant Cache
Registers
Shared Memory
L1 Cache
Constant Cache
≈1 cycle
≈5 cycles
≈5 cycles
≈500 cycles
Slide credit: Izzat El Hajj
50 MB
80 GB
Direct copy
3 TB/s
Notes: HBM3 memory subsystem provides nearly a 2x bandwidth increase over the previous generation. The H100 SXM5 GPU is the world’s first GPU with HBM3 memory delivering a class-leading 3 TB/sec of memory bandwidth.
50 MB L2 cache architecture caches large portions of models and datasets for repeated access, reducing trips to HBM3.
SM： streaming multiprocessor

## Slide 17: NVIDIA V100 & A100 Memory Hierarchy
Example of data movement between GPU global memory (DRAM) and GPU cores.
A100 feature:
Direct copy from L2 to scratchpad, bypassing L1 and register file.
https://images.nvidia.com/aem-dam/en-zz/Solutions/data-center/nvidia-ampere-architecture-whitepaper.pdf
Notes: A100: New load instruction that copies from global memory (DRAM) to shared memory (scratchpad) directly, without having to use registers (i.e., no need to copy from global memory to register and then from register to shared memory).

## Slide 18: CUDA Variable Type Qualifiers
__device__ is optional when used with __shared__, or __constant__
Recall cudaMalloc(…) allocates memory from the host
  Constant memory can also be allocated and initialized from the host
Automatic variables without any qualifier reside in a register
  Except arrays that reside in global memory
Variable declaration | Memory | Scope | Lifetime
int LocalVar; | register | thread | thread
int localArr[N]; | global | thread | thread
__device__ __shared__ int SharedVar; | shared | block | block
__device__ int GlobalVar; | global | grid | application
__device__ __constant__ int ConstantVar; | constant | grid | application

## Slide 19: Memory Hierarchy in CUDA Programs

## Slide 20: Recall: Comparison of Memories
SRAM
HBM
DDR
SSD
DISK
Capacity
SRAM
HBM
DDR
SSD
DISK
Latency
Bandwidth
~10MB
~10GB
~100GB
~1TB
~10TB
~1ns
~100ns
~100ns
~1us
~1ms
~100GB/s
DISK
SSD
DDR
HBM
SRAM
~10MB/s
~1GB/s
~10GB/s
~1TB/s

## Slide 21: The DRAM Subsystem The Top-Down View

## Slide 22: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 23: The DRAM Subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 24: Breaking down a DIMM (module)
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 25: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 26: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 27: Inside a DRAM Chip
Access
Transistor
Storage
Capacitor
Bitline
Wordline
Wordline
Bitline
Subarray
(2D Array of DRAM Cells)
Sense Amplifiers
DRAM Module
DRAM Chips
DRAM Bank
DRAM Cells
8
Row Buffer

## Slide 28: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 29: Long Global Memory Access Latency

## Slide 30
Motivation of In-network Computing
How to optimize global memory access?
Multithreading
Shared Memory
Memory Coalescing

## Slide 31: Agenda for Today
SIMT (Hardware) & Warp (Software)
Optimization of Memory System
  Multi-threading
  Memory Coalescing
  Shared Memory
SIMT Efficiency
  Divergency
  Atomic
  CPU-GPU Transfer

## Slide 32: Latency Hiding via Warp-Level FGMT
Warp: A set of threads that execute the same instruction (on different data elements)
Fine-grained multithreading
  One instruction per thread in pipeline at a time (No interlocking)
  Interleaving warp execution to hide latencies
Register values of all threads stay in register file
FGMT enables long latency tolerance
  Millions of pixels
Decode
R
F
R
F
R
F
A
L
U
A
L
U
A
L
U
D-Cache
Thread Warp 6
Thread Warp 1
Thread Warp 2
Data
All Hit?
Miss?
Warps accessing
memory hierarchy
Thread Warp 3
Thread Warp 8
Writeback
Warps available
for scheduling
Thread Warp 7
I-Fetch
SIMD Pipeline
Slide credit: Tor Aamodt
Notes: With a large number of shader threads multiplexed on the same execution re- sources, our architecture employs fine-grained multithreading where individual threads are interleaved by the fetch unit to proactively hide the potential latency of stalls before they occur. As illustrated by Figure, warps are issued fairly in a round-robin queue. When a thread is blocked by a memory request, shader core simply removes that thread’s warp from the pool of “ready” warps and thereby allows other threads to proceed while the memory system processes its request.
With a large number of threads (1024 per shader core) interleaved on the same pipeline, FGMT effectively hides the latency of most memory operations since the pipeline is occupied with instructions from other threads while memory operations complete. also hides the pipeline latency so that data bypassing logic can potentially be omitted to save area with minimal impact on performance. simplify the dependency check logic design by restricting each thread to have at most one instruction running in the pipeline at any time.

## Slide 33: Latency Hiding and Occupancy
FGMT can hide long latency operations (e.g., memory accesses)
Occupancy: ratio of active warps to the maximum number of warps per GPU core
4 active warps
2 active warps

## Slide 34: Agenda for Today
SIMT (Hardware) & Warp (Software)
Optimization of Memory System
  Multi-threading
  Memory Coalescing
  Shared Memory
SIMT Efficiency
  Divergency
  Atomic
  CPU-GPU Transfer

## Slide 35: Memory Coalescing (I)
Memory Coalescing：
  When threads in the same warp access consecutive memory locations in the same burst, the accesses can be combined and served by one burst
  Only one DRAM transaction is needed.
Memory Divergence：
  If threads in the same warp access locations not in the same burst, accesses cannot be combined
  Multiple memory transactions are needed
  Takes longer to service data to the warp
Slide credit: Izzat El Hajj

## Slide 36: Memory Coalescing (II)
Memory Coalescing:
  When accessing global memory, memory coalescing makes sure that concurrent threads access nearby memory locations
  Peak bandwidth utilization occurs when all threads in a warp access one cache line (or several consecutive cache lines)
Md
Nd
W
I
D
T
H
WIDTH
Thread 1
Thread 2
Not coalesced
Coalesced
Slide credit: Hwu & Kirk

## Slide 37: Uncoalesced Memory Accesses
M2,0
M1,1
M1,0
M0,0
M0,1
M3,0
M2,1
M3,1
M2,0
M1,0
M0,0
M3,0
M1,1
M0,1
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M1,3
M0,3
M2,3
M3,3
M
T1
T2
T3
T4
Warp 1
T1
T2
T3
T4
Warp 2
Access direction of each thread
…
Slide credit: Hwu & Kirk

## Slide 38: Coalesced Memory Accesses
M2,0
M1,1
M1,0
M0,0
M0,1
M3,0
M2,1
M3,1
M2,0
M1,0
M0,0
M3,0
M1,1
M0,1
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M1,3
M0,3
M2,3
M3,3
M
T1
T2
T3
T4
Warp 1
T1
T2
T3
T4
Warp 2
…
Slide credit: Hwu & Kirk
Access direction of each thread

## Slide 39: SIMT Memory Access
Same instruction in different threads uses thread id to index and access different data elements
Let’s assume N=16, 4 threads per warp  4 warps
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
+
+
+
+
+
Slide credit: Hyesoon Kim
Threads
Data elements
Warp 0
Warp 1
Warp 2
Warp 3

## Slide 40: Agenda for Today
SIMT (Hardware) & Warp (Software)
Optimization of Memory System
  Multi-threading
  Memory Coalescing
  Shared Memory
SIMT Efficiency
  Divergency
  Atomic
  CPU-GPU Transfer

## Slide 41: Shared Memory
Shared memory is an interleaved (banked) memory
  Each bank can service one address per cycle
Typically, 32 banks in NVIDIA GPUs
  Successive 32-bit words are assigned to successive banks
    Bank = Address % 32
Bank conflicts are only possible within a warp
  No bank conflicts between different warps

## Slide 42: Shared Memory Bank Conflicts (I)
Bank conflict free
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Linear addressing: stride = 1
Random addressing 1:1
Slide credit: Hwu & Kirk

## Slide 43: Shared Memory Bank Conflicts (II)
N-way bank conflicts
2-way bank conflict: stride = 2
8-way bank conflict: stride = 8
Thread 11
Thread 10
Thread 9
Thread 8
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 9
Bank 8
Bank 15
Bank 7
Bank 2
Bank 1
Bank 0
x8
x8
Slide credit: Hwu & Kirk

## Slide 44: Use Shared Memory to Improve Coalescing
Md
Nd
W
I
D
T
H
WIDTH
Md
Nd
Original
Access
Pattern
Tiled
Access
Pattern
Copy into
scratchpad
memory
Perform
multiplication
with scratchpad
values
Slide credit: Hwu & Kirk

## Slide 45: Reducing Shared Memory Bank Conflicts
Bank conflicts are only possible within a warp
  No bank conflicts between different warps
If strided accesses are needed, some optimization techniques can help
  Padding
  Randomized mapping
    Rau, “Pseudo-randomly interleaved memory,” ISCA 1991
  Hash functions
    V.d.Braak+, “Configurable XOR Hash Functions for Banked Scratchpad Memories in GPUs,” IEEE TC, 2016

## Slide 46: No Data Reuse
No Data reuse:
  Each thread reads its only elements.
for (int i = 0; i < 3; i++){
for (int j = 0; j < 3; j++){
sum += gauss[i][j] * Image[(i+row-1)*width + (j+col-1)];
}
}
Loading Amount:
9 elements per thread
Notes: 对每一个row，col,计算一个sum。

## Slide 47: Data Reuse: Tiling
For data reuse, we divide the input into tiles, each of which loads L_SIZE chunks together into shared memory, then compute together
__shared__ int l_data[(L_SIZE+2)*(L_SIZE+2)];
…
Load tile into shared memory l_data
__syncthreads();
for (int i = 0; i < 3; i++){
for (int j = 0; j < 3; j++){
sum += gauss[i][j] * l_data[(i+l_row-1)*(L_SIZE+2)+j+l_col-1];
}
}
Loading Amount:
(L_SIZE+2)2/L_SIZE2
elements per thread
Compute Amount:
The same
Notes: L_SIZE: number of points together…

## Slide 48: Synchronization Function
void __syncthreads();
  Synchronizes all threads in a block
  Once all threads in a block have reached this point, execution resumes normally
  Used to avoid RAW / WAR / WAW hazards when accessing shared or global memory

## Slide 49: Tiling/Blocking in On-chip Memories
Tiling or Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the on-chip RAM (or other on-chip memory, e.g., scratchpad)
  Avoids on-chip RAM conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the on-chip RAMs

## Slide 50: CPU: Naïve Matrix Multiplication (I)
Matrix multiplication: C = A x B
Consider two input matrices A and B in row-major layout
  A size is M x P
  B size is P x N
  C size is M x N
A
B
C
P
M
P
N
i
j
k
k

## Slide 51: CPU: Naïve Matrix Multiplication (II)
Naïve implementation of matrix multiplication
  Poor access locality
#define A(i,j) matrix_A[i * P + j]
#define B(i,j) matrix_B[i * N + j]
#define C(i,j) matrix_C[i * N + j]
for (i = 0; i < M; i++){ // i = row index
for (j = 0; j < N; j++){ // j = column index
C(i, j) = 0; // Set to zero
for (k = 0; k < P; k++) // Row x Col
C(i, j) += A(i, k) * B(k, j);
}
}
A
B
C
P
M
P
N
i
j
k
k
Consecutive accesses to B are far from each other, in different memory lines.
Every access to B is likely to cause a row buffer miss

## Slide 52: CPU: Tiled Matrix Multiplication (I)
Tiled Matrix Multiplication:
  Achieve better on-chip RAM locality by computing on smaller tiles or blocks that fit in the RAMs
A
B
C
P
M
P
N
k
k
tile_dim
tile_dim
i
j
Lam+, "The cache performance and optimizations of blocked algorithms," ASPLOS 1991. https://doi.org/10.1145/106972.106981
Bansal+, "Chapter 15 - Fast Matrix Computations on Heterogeneous Streams," in "High Performance Parallelism Pearls", 2015. https://doi.org/10.1016/B978-0-12-803819-2.00011-2
Kirk & Hwu, "Chapter 5 - Performance considerations," in "Programming Massively Parallel Processors (Third Edition)", 2017. https://doi.org/10.1016/B978-0-12-811986-0.00005-4

## Slide 53: CPU: Tiled Matrix Multiplication (II)
Tiled implementation operates on submatrices (tiles or blocks) that fit fast RAMs (cache, scratchpad, RF)
#define A(i,j) matrix_A[i * P + j]
#define B(i,j) matrix_B[i * N + j]
#define C(i,j) matrix_C[i * N + j]
for (I = 0; I < M; I += tile_dim){
for (J = 0; J < N; J += tile_dim){
Set_to_zero(&C(I, J)); // Set to zero
for (K = 0; K < P; K += tile_dim)
Multiply_tiles(&C(I, J), &A(I, K), &B(K, J));
}
}
Multiply small submatrices (tiles or blocks) of size tile_dim x tile_dim
A
B
C
P
M
P
N
k
k
tile_dim
tile_dim
i
j
Lam+, "The cache performance and optimizations of blocked algorithms," ASPLOS 1991. https://doi.org/10.1145/106972.106981
Bansal+, "Chapter 15 - Fast Matrix Computations on Heterogeneous Streams," in "High Performance Parallelism Pearls", 2015. https://doi.org/10.1016/B978-0-12-803819-2.00011-2
Kirk & Hwu, "Chapter 5 - Performance considerations," in "Programming Massively Parallel Processors (Third Edition)", 2017. https://doi.org/10.1016/B978-0-12-811986-0.00005-4

## Slide 54: GPU: Matrix-Matrix Multiplication (I)
N
N
C = A x B
A
B
C
N
N
N
N
Slide credit: Izzat El Hajj

## Slide 55: GPU: Matrix-Matrix Multiplication (II)
N
N
A
B
C
N
N
N
N
Parallelization approach: assign one thread to each element in the output matrix (C)
Slide credit: Izzat El Hajj
C = A x B

## Slide 56: GPU: Matrix-Matrix Multiplication (III)
__global__ void mm_kernel(float* A, float* B, float* C, unsigned int N) {
unsigned int row = blockIdx.y*blockDim.y + threadIdx.y;
unsigned int col = blockIdx.x*blockDim.x + threadIdx.x;
float sum = 0.0f;
for(unsigned int i = 0; i < N; ++i) {
sum += A[row*N + i]*B[i*N + col];
}
C[row*N + col] = sum;
}
Slide credit: Izzat El Hajj

## Slide 57: GPU: Reuse in Matrix-Matrix Multiplication (I)
N
N
A
B
C
N
N
N
N
Some of the threads in the same thread block use the same input data
Slide credit: Izzat El Hajj
C = A x B

## Slide 58: GPU: Reuse in Matrix-Matrix Multiplication (II)
N
N
A
B
C
N
N
N
N
Some of the threads in the same thread block use the same input data
Slide credit: Izzat El Hajj
C = A x B

## Slide 59: GPU: Tiled Matrix-Matrix Multiplication (I)
N
N
A
B
C
N
N
N
N
Step 1: Load the first tile of each input matrix to shared memory (each thread loads one element)
Slide credit: Izzat El Hajj
Ctile = Atile1 x Btile1

## Slide 60: GPU: Tiled Matrix-Matrix Multiplication (II)
Ctile += Atile2 x Btile2
Atile2
Btile2
Ctile
Step 2: Each thread computes its partial sum from the tiles in shared memory (threads wait for each other to finish)
Slide credit: Izzat El Hajj

## Slide 61: GPU: Tiled Matrix-Matrix Multiplication (III)
N
N
A
B
C
N
N
N
N
…accumulate the second tile
Slide credit: Izzat El Hajj
Ctile += Atile2 x Btile2

## Slide 62: GPU: Tiled Matrix-Matrix Multiplication (IV)
N
N
A
B
C
N
N
N
N
…and accumulate the third tile
Slide credit: Izzat El Hajj
Ctile += Atile3 x Btile3

## Slide 63: GPU: Tiled Matrix-Matrix Multiplication (V)
__shared__ float A_s[TILE_DIM][TILE_DIM];
__shared__ float B_s[TILE_DIM][TILE_DIM];
unsigned int row = blockIdx.y*blockDim.y + threadIdx.y;
unsigned int col = blockIdx.x*blockDim.x + threadIdx.x;
float sum = 0.0f;
for(unsigned int tile = 0; tile < N/TILE_DIM; ++tile) {
// Load tile to shared memory
A_s[threadIdx.y][threadIdx.x] = A[row*N + tile*TILE_DIM + threadIdx.x];
B_s[threadIdx.y][threadIdx.x] = B[(tile*TILE_DIM + threadIdx.y)*N + col];
__syncthreads();
// Compute with tile
for(unsigned int i = 0; i < TILE_DIM; ++i) {
sum += A_s[threadIdx.y][i]*B_s[i][threadIdx.x];
}
__syncthreads();
}
C[row*N + col] = sum;
Declare arrays in shared memory
Threads wait for each other to finish loading before computing
Threads wait for each other to finish computing before loading
Slide credit: Izzat El Hajj

## Slide 64: Agenda for Today
SIMT (Hardware) & Warp (Software)
Optimization of Memory System
  Multi-threading
  Memory Coalescing
  Shared Memory
SIMT Efficiency
  Divergency
  Atomic
  CPU-GPU Transfer

## Slide 65: Threads Can Take Different Paths in Warp-based SIMT
Each thread can have conditional control flow instructions
Threads can execute different control flow paths
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B
C
D
E
F
A
G
Slide credit: Tor Aamodt

## Slide 66: Control Flow Problem in GPUs/SIMT
A GPU uses a SIMT pipeline to save area on control logic
  Groups scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths
Branch
Path A
Path B
Branch
Path A
Path B
Slide credit: Tor Aamodt

## Slide 67: SIMT Utilization
Intra-warp divergence
Compute(threadIdx.x);
if (threadIdx.x % 2 == 0){
Do_this(threadIdx.x);
}
else{
Do_that(threadIdx.x);
}

## Slide 68: Increasing SIMT Utilization
Divergence-free execution
Compute(threadIdx.x);
if (threadIdx.x < 32){
Do_this(threadIdx.x * 2);
}
else{
Do_that((threadIdx.x%32)*2+1);
}

## Slide 69: Vector Reduction: Naïve Mapping (I)
0
1
2
3
4
5
7
6
10
9
8
11
0+1
2+3
4+5
6+7
10+11
8+9
0...3
4..7
8..11
0..7
8..15
1
2
3
iterations
Thread 0
Thread 8
Thread 2
Thread 4
Thread 6
Thread 10
Slide credit: Hwu & Kirk
…

## Slide 70: Vector Reduction: Naïve Mapping (II)
Program with low SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for (int stride = 1; stride < blockDim.x; stride *= 2) {
  __syncthreads();
  if (t % (2*stride) == 0)
  partialSum[t] += partialSum[t + stride];
  }

## Slide 71: Divergence-Free Mapping (I)
All active threads belong to the same warp
Thread 0
0
1
2
3
…
13
15
14
18
17
16
19
0+16
15+31
1
2
3
Thread 1
Thread 2
Thread 14
Thread 15
iterations
Slide credit: Hwu & Kirk
…

## Slide 72: Divergence-Free Mapping (II)
Program with high SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for (int stride = blockDim.x; stride > 0; stride >> 1){
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t + stride];
  }

## Slide 73: Agenda for Today
SIMT (Hardware) & Warp (Software)
Optimization of Memory System
  Multi-threading
  Memory Coalescing
  Shared Memory
SIMT Efficiency
  Divergency
  Atomic
  CPU-GPU Transfer

## Slide 74: Atomic Operations

## Slide 75: Atomic Operations (I)
CUDA provides atomic instructions on shared memory and global memory
  They perform read-modify-write operations atomically
Arithmetic functions
  Add, sub, max, min, exch, inc, dec, CAS
  int atomicAdd(int*, int);
Bitwise functions
  And, or, xor
Datatypes: int, uint, ull, float (half, single, double)*
Pointer to shared memory or global memory
Value to add
Return value (old value)
* Datatypes for different atomic operations in https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#atomic-functions

## Slide 76: Atomic Operations (II)
Atomic operations serialize the execution if there are atomic conflicts
tbase
tconflict
Shared memory
Shared memory
tbase
No atomic conflict = concurrent updates
Atomic conflict = serialized updates

## Slide 77: Uses of Atomic Operations
Use atomic operations to prevent data races when more than one thread need to update the same memory location
Computation
  Atomics on an array that will be the output of the kernel
  Example
    Histogram, reduction
Synchronization
  Atomics on memory locations that are used for synchronization or coordination
  Example
    Counters, locks, flags…

## Slide 78: Image Histogram
  Histograms are widely used in image processing
  Some computation before voting in the histogram may be needed
  Parallel threads frequently incur atomic conflicts in image histogram computation
For (each pixel i in image I){
  Pixel = I[i] // Read pixel
  Pixel’ = Computation(Pixel) // Optional computation
  Histogram[Pixel’]++ // Vote in histogram bin
}

## Slide 79: Agenda for Today
SIMT (Hardware) & Warp (Software)
Optimization of Memory System
  Multi-threading
  Memory Coalescing
  Shared Memory
SIMT Efficiency
  Divergency
  Atomic
  CPU-GPU Transfer

## Slide 80: Asynchronous Data Transfers between CPU and GPU

## Slide 81: CUDA Streams
CUDA streams (command queues in OpenCL)
Sequence of operations that are performed in order
  1. Data transfer CPU-GPU
  2. Kernel execution
    D input data instances, B blocks
    #Streams: (D / #Streams) data instances, (B / #Streams) blocks
  3. Data transfer GPU-CPU
Notes: Computation is divided such that if D data instances need B blocks to be processed… The kernel is therefore #Streams times launched.
CUDA literature gives only two rough estimates, but does not give any hint of the optimal number of streams in which a given data set should be preferably divided.

## Slide 82: Asynchronous Transfers between CPU & GPU
Computation divided into #Streams
  D input data instances, B blocks
  #Streams
    D/#Streams data instances
    B/#Streams blocks
  Estimates
tE >= tT (dominant kernel)
tT > tE (dominant transfers)
Default stream
Several streams
Notes: Computation is divided such that if D data instances need B blocks to be processed… The kernel is therefore #Streams times launched.
CUDA literature gives only two rough estimates, but does not give any hint of the optimal number of streams in which a given data set should be preferably divided.

## Slide 83
Overlap of Data Transfers and Kernel Execution
// Create streams
int number_of_streams = 32;
cudaStream_t stream[number_of_streams]; // Stream declaration
for(int i = 0; i < number_of_streams; ++i)
cudaStreamCreate(&stream[i]); // Stream creation
// CPU-GPU data transfers
for (int i = 0; i < number_of_streams; ++i)
cudaMemcpyAsync(inputDevPtr + i * size, hostPtr + i * size, size,
cudaMemcpyHostToDevice, stream[i]);
// Kernel launches
for (int i = 0; i < number_of_streams; ++i)
MyKernel<<<num_blocks / number_of_streams, num_threads, 0, stream[i]>>>
(outputDevPtr + i * size, inputDevPtr + i * size, size);
// GPU-CPU data transfers
for (int i = 0; i < number_of_streams; ++i)
cudaMemcpyAsync(hostPtr + i * size, outputDevPtr + i * size, size,
cudaMemcpyDeviceToHost, stream[i]);
cudaDeviceSynchronize(); // Explicit synchronization
// Destroy streams
for (int i = 0; i < number_of_streams; ++i)
cudaStreamDestroy(stream[i]); // Stream destruction
Code for devices that do not support concurrent data transfers
Gomez-Luna+, “Performance Models for Asynchronous Data Transfers on Consumer Graphics Processing Units,”
JPDC, 2012
Check CUDA programming guide
https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#streams

## Slide 84: Use Case: Video Processing
Applications with independent computation on different data instances can benefit from asynchronous transfers
For instance, video processing
Gomez-Luna+, “Performance Models for Asynchronous Data Transfers on Consumer Graphics Processing Units,”
JPDC, 2012
Notes: A number b of blocks per frame executes.
Data transfers are overlapped with computation. Thus, some time can be saved.

## Slide 85: NVIDIA H100 Tensor Memory Accelerator
Asynchronous memory copy with LDGSTS instruction vs. TMA
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/
TMA unit reduces addressing overhead
A single thread per warp issues the TMA operation
Support for different tensor layouts (1D-5D)
Notes: New asynchronous execution features include a new Tensor Memory Accelerator (TMA) unit that can transfer large blocks of data efficiently between global memory and shared memory. TMA also supports asynchronous copies between thread blocks in a cluster. There is also a new asynchronous transaction barrier for doing atomic data movement and synchronization.
  New asynchronous execution features include a new Tensor Memory Accelerator (TMA) unit that can efficiently transfer large blocks of data between global memory and shared memory. TMA also supports asynchronous copies between thread blocks in a cluster. There is also a new asynchronous transaction barrier for doing atomic data movement and synchronization.

## Slide 86: State-of-the-art CPU GPU and FPGA
 | Cores (Threads) | TFLOPS | Memory Size (Bandwidth) | PCIe | Network
CPU (AMD Threadripper 3995WX) | 64 (128) | 2.8 (FP32), 1.4 (FP64) | 512GB (80GB/s) | 32.0GB/s (PCIe 4.0 X16) | No
GPU (Nvidia A100) | 8192 (128K) | 19.5 (FP32), 9.7 (FP64), 156 (FP32, Tensor), 312 (FP16, Tensor) | 40/80GB (1935GB/s) | 32.0GB/s (PCIe 4.0 X16) | No
FPGA (U280) | 9,024 (25x18 MULs) | 1.8 (FP32) | 40GB (460GB/s) | 16.0GB/s (PCIe 4.0 X8) | Yes
Notes: KB MB GB TB
K M B T E P
1B=10亿

## Slide 87: Limitation of GPU
CPU
GPU
PCIe
32.0GB/s
1935GB/s

## Slide 88: Limitation of GPU
Serial Code of Prefix sum:
GPU Code of Prefix sum:
Multi-pass (ISSUE)
// Fills prefix sum array
void fillPrefixSum(int arr[], int n, int prefixSum[])
{ prefixSum[0] = arr[0];
// Adding present element
for (int i = 1; i < n; i++)
prefixSum[i] = prefixSum[i-1] + arr[i]; }

## Slide 89: Nvidia’s Success: Transparent Scalability
Hardware is free to schedule thread blocks
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Kernel grid
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Each block can execute in any order relative to other blocks.
time
Slide credit: Hwu & Kirk
time
Gen 1
Gen 2
The CUDA code stays the same and enjoys performance improvement while GPU hardware evolves.
Notes: Thread block is the key innovation to scale-up GPU architecture. The software code stays the same and enjoys performance speedup while GPU hardware evolves.

## Slide 90: Key Messages:
Programming model is the key success of Nvidia, rather than the GPU itself.
GPU has an order of magnitude higher memory bandwidth and compute power than CPU.
Offloading a task to GPU pays off only when the task has enough compute intensity.
AI task needs compute-intensive accelerators, e.g., GPU and AI processor.

## Slide 91: Prog. Model 3: Multithreaded
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Realization: Each iteration is independent
Idea: Programmer or compiler generates a thread to execute each iteration. Each thread does the same thing (but on different data)
This programming model (software) is called:
SPMD: Single Program Multiple Data
Executed on a SIMT machine (hardware)
Single Instruction Multiple Thread

## Slide 92: A GPU is a SIMD (SIMT) Machine
Except it is not programmed using SIMD instructions
It is programmed using threads (SPMD programming model)
  Each thread executes the same code but operates a different piece of data
  Each thread has its own context (i.e., can be treated/restarted/executed independently)
A set of threads executing the same instruction are dynamically grouped into a warp (wavefront) by the hardware
  A warp is essentially a SIMD operation formed by hardware!

## Slide 93: SIMD vs. SIMT Execution Model
SIMD: A single sequential instruction stream of SIMD instructions  each instruction specifies multiple data inputs
  [VLD, VLD, VADD, VST], VLEN
SIMT: Multiple instruction streams of scalar instructions  threads grouped dynamically into warps
  [LD, LD, ADD, ST], NumThreads
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently on any type of scalar pipeline
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing

## Slide 94: Brief Review of GPU Architecture (I)
Streaming Processor Array
  Tesla architecture (G80/GT200)

## Slide 95: Brief Review of GPU Architecture (II)
Streaming Multiprocessors (SM)
  Streaming Processors (SP)
Blocks are divided into warps
  SIMD unit (32 threads)
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0’s warps
Block 1’s warps
…
t0 t1 t2 … t31
…
Block 2’s warps
NVIDIA Fermi architecture

## Slide 96: Brief Review of GPU Architecture (III)
Streaming Multiprocessors (SM) or Compute Units (CU)
  SIMD pipelines
Streaming Processors (SP) or CUDA ”cores”
  Vector lanes
Number of SMs x SPs across generations
  Tesla (2007): 30 x 8
  Fermi (2010): 16 x 32
  Kepler (2012): 15 x 192
  Maxwell (2014): 24 x 128
  Pascal (2016): 56 x 64
  Volta (2017): 80 x 64

## Slide 97: Graphics Processing Units SIMD not Exposed to Programmer (SIMT)

## Slide 98: SIMD vs. SIMT Execution Model
SIMD: A single sequential instruction stream of SIMD instructions  each instruction specifies multiple data inputs
  [VLD, VLD, VADD, VST], VLEN
SIMT: Multiple instruction streams of scalar instructions  threads grouped dynamically into warps
  [LD, LD, ADD, ST], NumThreads
Two Major SIMT Advantages:
  Can treat each thread separately  i.e., can execute each thread independently (on any type of scalar pipeline)  MIMD processing
  Can group threads into warps flexibly  i.e., can group threads that are supposed to truly execute the same instruction  dynamically obtain and maximize benefits of SIMD processing

## Slide 99: High-Level View of a GPU
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.

## Slide 100: Latency Hiding via Warp-Level FGMT
Warp: A set of threads that execute the same instruction (on different data elements)
Fine-grained multithreading
  No interlocking: One instruction per thread in pipeline at a time.
  Interleave warp execution to hide latencies
Register values of all threads stay in register file
FGMT enables long latency tolerance
  Millions of pixels
Decode
R
F
R
F
R
F
A
L
U
A
L
U
A
L
U
D-Cache
Thread Warp 6
Thread Warp 1
Thread Warp 2
Data
All Hit?
Miss?
Warps accessing
memory hierarchy
Thread Warp 3
Thread Warp 8
Writeback
Warps available
for scheduling
Thread Warp 7
I-Fetch
SIMD Pipeline
Slide credit: Tor Aamodt
Notes: With a large number of shader threads multiplexed on the same execution re- sources, our architecture employs fine-grained multithreading where individual threads are interleaved by the fetch unit to proactively hide the potential latency of stalls before they occur. As illustrated by Figure, warps are issued fairly in a round-robin queue. When a thread is blocked by a memory request, shader core simply removes that thread’s warp from the pool of “ready” warps and thereby allows other threads to proceed while the memory system processes its request.
With a large number of threads (1024 per shader core) interleaved on the same pipeline, FGMT effectively hides the latency of most memory operations since the pipeline is occupied with instructions from other threads while memory operations complete. also hides the pipeline latency so that data bypassing logic can potentially be omitted to save area with minimal impact on performance. simplify the dependency check logic design by restricting each thread to have at most one instruction running in the pipeline at any time.

## Slide 101: Warp Execution (Recall the Slide)
32-thread warp executing ADD A[tid],B[tid]  C[tid]
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units
Slide credit: Krste Asanovic
Time
Space
Time

## Slide 102
Lane
Functional Unit
Registers
for each
Thread
Memory Subsystem
Registers for thread IDs
0, 4, 8, …
Registers for thread IDs
1, 5, 9, …
Registers for thread IDs
2, 6, 10, …
Registers for thread IDs
3, 7, 11, …
Slide credit: Krste Asanovic
SIMD Execution Unit Structure

## Slide 103: Warps not Exposed to GPU Programmers
CPU threads and GPU kernels
  Sequential or modestly parallel sections on CPU
  Massively parallel sections on GPU: Blocks of threads
Serial Code (host)
. . .
. . .
Parallel Kernel (device)
KernelA<<<nBlk, nThr>>>(args);
Serial Code (host)
Parallel Kernel (device)
KernelB<<<nBlk, nThr>>>(args);
Slide credit: Hwu & Kirk

## Slide 104: From Blocks to Warps
GPU cores: SIMD pipelines
  Streaming Multiprocessors (SM)
  Streaming Processors (SP)
Blocks are divided into warps
  SIMD unit (32 threads)
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0’s warps
Block 1’s warps
…
t0 t1 t2 … t31
…
Block 2’s warps
NVIDIA Fermi architecture

## Slide 105: SPMD
Single procedure/program, multiple data
  This is a programming model rather than computer organization
Each processing element executes the same procedure, except on different data elements
  Procedures can synchronize at certain points in program, e.g. barriers
Essentially, multiple instruction streams execute the same program
  Each program/procedure 1) works on different data, 2) can execute a different control-flow path, at run-time
  Many scientific applications are programmed this way and run on MIMD hardware (multiprocessors)
  Modern GPUs programmed in a similar way on a SIMD hardware

## Slide 106: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction (after branch divergence)
Form new warps from warps that are waiting
  Enough threads branching to each path enables the creation of full new warps
Warp X
Warp Y
Warp Z

## Slide 107: Dynamic Warp Formation/Merging
Idea: Dynamically merge threads executing the same instruction (after branch divergence)
  Fung et al., “Dynamic Warp Formation and Scheduling for Efficient GPU Control Flow,” MICRO 2007.
Branch
Path A
Path B
Branch
Path A

## Slide 108: Dynamic Warp Formation Example
A
A
B
B
G
G
A
A
C
C
D
D
E
E
F
F
Time
A
A
B
B
G
G
A
A
C
D
E
E
F
Time
A
x/1111
y/1111
B
x/1110
y/0011
C
x/1000
y/0010
D
x/0110
y/0001
F
x/0001
y/1100
E
x/1110
y/0011
G
x/1111
y/1111
A new warp created from scalar threads of both Warp x and y executing at Basic Block D
D
Execution of Warp x
at Basic Block A
Execution of Warp y
at Basic Block A
Legend
A
A
Baseline
Dynamic
Warp
Formation
Slide credit: Tor Aamodt

## Slide 109: Hardware Constraints Limit Flexibility of Warp Grouping
Lane
Functional Unit
Registers
for each
Thread
Memory Subsystem
Registers for thread IDs
0, 4, 8, …
Registers for thread IDs
1, 5, 9, …
Registers for thread IDs
2, 6, 10, …
Registers for thread IDs
3, 7, 11, …
Slide credit: Krste Asanovic

## Slide 110: Clarification of Some GPU Terms
Generic Term | NVIDIA Term | AMD Term | Comments
Vector length | Warp size | Wavefront size | Number of threads that run in parallel (lock-step) on a SIMD functional unit
Pipelined functional unit / Scalar pipeline | Streaming processor / CUDA core | - | Functional unit that executes instructions for one GPU thread
SIMD functional unit / SIMD pipeline | Group of N streaming processors (e.g., N=8 in GTX 285, N=16 in Fermi) | Vector ALU | SIMD functional unit that executes instructions for an entire warp
GPU core | Streaming multiprocessor | Compute unit | It contains one or more warp schedulers and one or several SIMD pipelines

## Slide 111: Programming Model vs. Hardware Execution Model
Hardware Programming Model
Programming Model
Core
Streaming
Multi-processor
GPU
CUDA core:
Thread
Thread block (s)
Wrap
Thread blocks

## Slide 112: NVIDIA H100 Block Diagram
144 cores on the full GH100
60MB L2 cache
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/

## Slide 113: NVIDIA H100 Core
48 TFLOPS Single Precision*
24 TFLOPS Double Precision*
800 TFLOPS (FP16, Tensor Cores)*
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/
* Preliminary performance estimates

## Slide 114: NVIDIA H100 Distributed Shared Memory
Shared memory virtual address space distributed across the blocks of a cluster
Load, store, and atomic operations to other SM’s shared memory
https://developer.nvidia.com/blog/nvidia-hopper-architecture-in-depth/
Thread block clusters and distributed shared memory (DSMEM) are leveraged via cooperative_groups API
TMA unit supports copies across thread blocks in a cluster
Asynchronous transaction barriers
Notes: Distributed shared memory allows direct SM-to-SM communications for loads, stores, and atomics across multiple SM shared memory blocks.
  Distributed shared memory enables direct SM-to-SM communications for loads, stores, and atomics across multiple SM shared memory blocks

## Slide 115: Optimized Parallel Reduction
7 versions in CUDA samples: Tree-based reduction in shared memory
  Version 0: No whole warps active
  Version 1: Contiguous threads, but many bank conflicts
  Version 2: No bank conflicts
  Version 3: First level of reduction when reading from global memory
  Version 4: Warp shuffle or unrolling of final warp
  Version 5: Warp shuffle or complete unrolling
  Version 6: Multiple elements per thread sequentially
https://docs.nvidia.com/cuda/cuda-samples/index.html#cuda-parallel-reduction
Harris, “Optimizing Parallel Reduction in CUDA,” https://developer.download.nvidia.com/assets/cuda/files/reduction.pdf

## Slide 116: Reduction with Atomic Operations
3 new versions of reduction based on 3 previous versions
  Version 0: No whole warps active
  Version 3: First level of reduction when reading from global memory
  Version 6: Multiple elements per thread sequentially
New versions 7, 8, and 9
  Replace the for loop (tree-based reduction) with one shared memory atomic operation per thread

## Slide 117: Video Processing: Performance Results (I)
256-bin histogram calculation
Gomez-Luna+, “Performance Models for Asynchronous Data Transfers on Consumer Graphics Processing Units,”
JPDC, 2012
44%
21%

## Slide 118: Video Processing: Performance Results (II)
RGB-to-grayscale conversion
Gomez-Luna+, “Performance Models for Asynchronous Data Transfers on Consumer Graphics Processing Units,”
JPDC, 2012
63%
18%

## Slide 119: Performance Considerations
Main bottlenecks
  CPU-GPU data transfers
  Global memory access
Memory access
  Latency hiding
    Occupancy
  Memory coalescing
  Data reuse
    Shared memory usage
SIMD (Warp) Utilization: Divergence
Other considerations
  Atomic operations: Serialization
  Data transfers between CPU and GPU
    Overlap of communication and computation

## Slide 120: Recommended Readings
Hwu and Kirk, “Programming Massively Parallel Processors,” Third Edition, 2017
  Chapter 5: Performance considerations
  Chapter 18 - Programming
  a heterogeneous computing cluster,
  Section 18.5