## Slide 1: Computer Arch. & AI Chip Lecture 8: Memory Hierarchy and Caches
Prof. Zeke Wang
Zhejiang University
23 April 2026

## Slide 2: Recall: GPU Programming Model vs. Hardware Execution Model
Hardware Execution Model
CUDA Programming Model
Streaming
Multi-processor
GPU
CUDA core
Thread
Thread block
Grid
...
Warp
SIMT
Notes: SIMD Wrap

## Slide 3
Motivation of In-network Computing
How to deal with long-latency global memory access?
Multithreading
Shared Memory
Memory Coalescing

## Slide 4: Recall: Latency Hiding and Occupancy
FGMT can hide long latency operations (e.g., memory accesses)
Occupancy: ratio of active warps to the maximum number of warps per GPU core
4 active warps
2 active warps

## Slide 5: Recall: SIMT Memory Access
Same instruction in different threads uses thread id to index and access different data elements
Let’s assume N=16, 4 threads per warp  4 warps
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
+
+
+
+
+
Slide credit: Hyesoon Kim
Threads
Data elements
Warp 0
Warp 1
Warp 2
Warp 3

## Slide 6: Recall: Naïve Matrix-Matrix Multiplication
N
N
C = A x B
A
B
C
N
N
N
N
Slide credit: Izzat El Hajj

## Slide 7: Recall: GPU Tiled Matrix-Matrix Multiplication
N
N
A
B
C
N
N
N
N
Slide credit: Izzat El Hajj
C += Atile x Btile

## Slide 8: Recall: Tiled Matrix-Matrix Multiplication with Shared Memory
__shared__ float A_s[TILE_DIM][TILE_DIM];
__shared__ float B_s[TILE_DIM][TILE_DIM];
unsigned int row = blockIdx.y*blockDim.y + threadIdx.y;
unsigned int col = blockIdx.x*blockDim.x + threadIdx.x;
float sum = 0.0f;
for(unsigned int tile = 0; tile < N/TILE_DIM; ++tile) {
// Load tile to shared memory
A_s[threadIdx.y][threadIdx.x] = A[row*N + tile*TILE_DIM + threadIdx.x];
B_s[threadIdx.y][threadIdx.x] = B[(tile*TILE_DIM + threadIdx.y)*N + col];
__syncthreads();
// Compute with tile
for(unsigned int i = 0; i < TILE_DIM; ++i) {
sum += A_s[threadIdx.y][i]*B_s[i][threadIdx.x];
}
__syncthreads();
}
C[row*N + col] = sum;
Declare arrays in shared memory
Threads wait for each other to finish loading before computing
Threads wait for each other to finish computing before loading
Slide credit: Izzat El Hajj

## Slide 9: Issue of Shared Memory Mechanism
Issue of Shared Memory:
  Manual: Programmer manages data movement across levels
  -- too painful for programmers on substantial programs
  Done in on-chip scratchpad SRAM: GPUs (called “shared memory”), ML accelerators, …
Cache: Hardware manages data movement across levels, Automatic: transparently to the programmer
  ++ programmer’s life is easier
  The average programmer doesn’t need to know about caches
    You don’t need to know how big the cache is and how it works to write a “correct” program! (What if you want a “fast” program?)

## Slide 10: Recall: Data Movement vs. Computation
32-bit Operation | Energy (pJ) | ADD (int) Relative Cost
ADD (int) | 0.1 | 1
ADD (float) | 0.9 | 9
Register File | 1 | 10
MULT (int) | 3.1 | 31
MULT (float) | 3.7 | 37
SRAM Cache | 5 | 50
DRAM | 640 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.
A memory access consumes ~6400X
the energy of an integer addition

## Slide 11: Recall: Idealism
Instruction
Supply
Pipeline
(Instruction
execution)
Data
Supply
- Zero latency access
- Infinite capacity
- Zero cost
- Perfect control flow
No pipeline stalls
Perfect data flow
(reg/memory dependencies)
Zero-cycle interconnect
(operand communication)
Enough functional units
Zero latency compute
Zero latency access
Infinite capacity
- Infinite bandwidth
Zero cost

## Slide 12: Recall: DRAM Capacity, Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x

## Slide 13: Recall: FF vs. SRAM vs. DRAM vs. Flash
Flip-Flops
  Very fast, parallel access
  Very expensive (one bit costs tens of transistors)
Static RAM
  Relatively fast, only one data word at a time
  Expensive (one bit costs 6+ transistors)
Dynamic RAM
  Slower, one data word at a time, reading destroys content (refresh), needs special process for manufacturing
  Cheap (one bit costs only one transistor plus one capacitor)
Flash Memory
  Much slower, access takes a long time, non-volatile
  Very cheap (one transistor stores 16 bits or no transistors involved)

## Slide 14: Recall: Memory Address Mapping
row 0
row 32k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>
App address to memory address: channel, DIMM, rank, row, column
  Sequential: column, column
  Random: pre-charge previous row, activate new row, column
Sequential > Random:
  Row buffer hit vs. Row buffer miss.

## Slide 15: Where Are We?

## Slide 16: The Memory Hierarchy

## Slide 17: Memory Hierarchy in a Modern System (I)
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER
AMD Barcelona, circa 2006

## Slide 18: Memory Hierarchy in a Modern System (II)
https://wccftech.com/amd-ryzen-5000-zen-3-vermeer-undressed-high-res-die-shots-close-ups-pictured-detailed/
AMD Ryzen 5000, 2020
Core Count:
8 cores/16 threads
L1 Caches:
32 KB per core
L2 Caches:
512 KB per core
L3 Cache:
32 MB shared

## Slide 19: Memory Hierarchy in a Modern System (III)
https://www.it-techblog.de/ibm-power10-prozessor-mehr-speicher-mehr-tempo-mehr-sicherheit/09/2020/
IBM POWER10,
2020
Cores:
15-16 cores,
8 threads/core
L2 Caches:
2 MB per core
L3 Cache:
120 MB shared

## Slide 20: Memory Hierarchy in a Modern System (IV)
https://www.tomshardware.com/news/infrared-photographer-photos-nvidia-ga102-ampere-silicon
Nvidia Ampere, 2020
Cores:
108 Streaming Multiprocessors
L1 Cache or Scratchpad:
192KB per SM
Can be used as L1 Cache and/or Scratchpad
L2 Cache:
40 MB shared

## Slide 21: Ideal Memory
Properties of ideal memory:
  Zero access time (latency)
  Infinite capacity
  Infinite bandwidth (to support multiple accesses in parallel)
  Zero cost

## Slide 22: The Problem of Ideal Memory
Ideal memory’s requirements oppose each other
  Bigger is slower
    Bigger  Takes longer to determine the location
  Faster is more expensive
    Memory technology: SRAM vs. DRAM vs. SSD vs. Disk vs. Tape
  Higher bandwidth is more expensive
    Need more banks, more ports, more channels, higher frequency or faster technology

## Slide 23: The Problem of Ideal Memory
Bigger is slower
  SRAM, 512 Bytes, sub-nanosec
  SRAM, KByte~MByte, ~nanosec
  DRAM, Gigabyte, ~50 nanosec
  PCM-DIMM (Intel Optane DC DIMM), Gigabyte, ~200 nanosec
  PCM-SSD (Intel Optane SSD), Gigabyte, ~10 µs
  Flash memory, Gigabyte~Terabyte, ~100 µs
  Hard Disk, Terabyte, ~10 millisec
Faster is more expensive (dollars and chip area)
  SRAM, < 0.3$ per Megabyte
  DRAM, < 0.03$ per Megabyte
  PCM-DIMM (Intel Optane DC DIMM), < 0.004$ per Megabyte
  PCM-SSD, < 0.001$ per Megabyte
  Flash memory, < 0.00008$ per Megabyte
  Hard Disk, < 0.00003$ per Megabyte
  These sample values (circa ~2021) scale with time
Other technologies have their place as well
  MRAM, RRAM, STT-MRAM, … (not mature yet)

## Slide 24: The Problem (Table View)
Memory Device | Capacity | Latency | Cost per Megabyte
SRAM | 512 Bytes | sub-nanosec | 
SRAM | KByte~MByte | ~nanosec | < 0.3$
DRAM | Gigabyte | ~50 nanosec | < 0.03$
PCM-DIMM (Intel Optane DC DIMM) | Gigabyte | ~200 nanosec | < 0.004$
PCM-SSD (Intel Optane SSD) | Gigabyte ~Terabyte | ~10 µs | < 0.001$
Flash memory | Gigabyte ~Terabyte | ~100 µs | < 0.00008$
Hard Disk | Terabyte | ~10 millisec | < 0.00003$
  These sample values (circa ~2021) scale with time
Bigger is slower
Faster is more expensive
(dollars and chip area)

## Slide 25: Aside: The Problem (2011 Version)
Bigger is slower
  SRAM, 512 Bytes, sub-nanosec
  SRAM, KByte~MByte, ~nanosec
  DRAM, Gigabyte, ~50 nanosec
  Hard Disk, Terabyte, ~10 millisec
Faster is more expensive (dollars and chip area)
  SRAM, < 10$ per Megabyte
  DRAM, < 1$ per Megabyte
  Hard Disk < 1$ per Gigabyte
  These sample values (circa ~2011) scale with time
Other technologies have their place as well
  Flash memory (mature), PC-RAM, MRAM, RRAM (not mature yet)

## Slide 26: Why Cache?
Challenge: DRAM latency is ~100ns, slightly decreasing over time.
Our Goal: CPU wants both fast (~1ns) and large memory (GB) without modifying user code.
Notes: 九品芝麻官电影

## Slide 27: DRAM Capacity, Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Notes: Latency issue is still there…

## Slide 28: Why Cache?
Observation: we cannot achieve both with a single level of memory
Idea:
  Have multiple levels of storage (progressively bigger and slower as the levels are farther from the processor) and
  Ensure most of the data the processor needed is kept in the fast(er) level(s).

## Slide 29: Memory Hierarchy
Fundamental tradeoff
  Fast memory: small
  Large memory: slow
Idea: Memory hierarchy.
Latency, cost, size,
bandwidth
CPU
Main
Memory
(DRAM)
RF
Cache
Hard Disk

## Slide 30: The Memory Hierarchy
fast
small
large but slow
move what you use here
backup
everything
here
With good locality of reference, memory appears as fast as
and as large as
faster per byte
cheaper per byte

## Slide 31: Memory Hierarchy Example
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014
  https://people.inf.ethz.ch/omutlu/pub/memory-systems-introduction_computing-handbook14.pdf

## Slide 32: Why Cache Works? Locality
Locality: One’s recent past is a very good predictor of his/her near future.
  Temporal Locality: If you just did something, it is very likely that you will do the same thing again soon
    since you are here today, there is a good chance you will be here again and again regularly
  Spatial Locality: If you did something, it is very likely you will do something similar/related (in space)
    every time I find you in this room, you are probably sitting close to the same people

## Slide 33: Why Cache Works? Memory Locality
A “typical” program has a lot of locality in memory references
  typical programs are composed of “loops”
Temporal Locality: A program tends to reference the same memory location many times and all within a small window of time
Spatial Locality: A program tends to reference nearby memory locations within a window of time
  most notable examples:
    1. instruction memory references  most sequential/streaming
    2. references to arrays/vectors  often streaming/strided

## Slide 34: Caching Basics: Exploit Temporal Locality
Idea: Store recently accessed data in automatically-managed fast memory (called cache)
Anticipation: same mem. location will be accessed again soon
Temporal locality principle
  Recently accessed data will be again accessed in the near future
  This is what Maurice Wilkes had in mind:
    “The use is discussed of a fast core memory of, say 32000 words as a slave to a slower core memory of, say, one million words in such a way that in practical cases the effective access time is nearer that of the fast memory than that of the slow memory.”
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.

## Slide 35: Caching Basics: Exploit Spatial Locality
Idea: Store data in addresses adjacent to the recently accessed one in automatically-managed fast memory
  Logically divide memory into equal-size blocks
  Fetch to cache the accessed block in its entirety
Anticipation: nearby memory locations will be accessed soon
Spatial locality principle
  Nearby data in memory will be accessed in the near future
    E.g., sequential instruction access, array traversal
  This is what IBM 360/85 implemented
    16 Kbyte cache with 64 byte blocks
    Liptay, “Structural aspects of the System/360 Model 85 II: the cache,” IBM Systems Journal, 1968.

## Slide 36: The Bookshelf Analogy
Book in your hand
Desk
Bookshelf
Boxes at home
Boxes in storage
Recently-used books tend to stay on desk
  Comp Arch books, books for classes you are currently taking
  Until the desk gets full
Adjacent books in the shelf needed around the same time
  If I have organized/categorized my books well in the shelf

## Slide 37: Caching in a Pipelined Design
The cache needs to be tightly integrated into the pipeline
  Ideally, access in 1-cycle so that load-dependent operations do not stall
High frequency pipeline  Cannot make the cache large
  But, we want a large cache AND a pipelined design
Idea: Cache hierarchy
CPU
Main
Memory
(DRAM)
RF
Level1
Cache
Level 2
Cache

## Slide 38: A Note on Manual vs. Automatic Management
Manual: Programmer manages data movement across levels
  -- too painful for programmers on substantial programs
  “core” vs “drum” memory in the 1950s
  done in embedded processors (on-chip scratchpad SRAM in lieu of a cache), GPUs (called “shared memory”), ML accelerators, …
Automatic: Hardware manages data movement across levels, transparently to the programmer
  ++ programmer’s life is easier
  the average programmer doesn’t need to know about caches
    You don’t need to know how big the cache is and how it works to write a “correct” program! (What if you want a “fast” program?)

## Slide 39: Automatic Management in Memory Hierarchy
Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
“By a slave memory I mean one which automatically accumulates to itself words that come from a slower main memory, and keeps them available for subsequent use without it being necessary for the penalty of main memory access to be incurred again.”

## Slide 40: Cache in 1962 (Bloom, Cohen, Porter)

## Slide 41: A Modern Memory Hierarchy
Register File
32 words, sub-nsec
L1 cache
~10s of KB, ~nsec
L2 cache
100s of KB ~ few MB, many nsec
L3 cache,
many MBs, even more nsec
Main memory (DRAM),
Many GBs, ~100 nsec
Swap Disk
~100 GB or few TB, ~10s of usec-msec
manual/compiler
register spilling
automatic
demand
paging
automatic
HW cache
management
Memory
Abstraction

## Slide 42: Hierarchical Latency Analysis
For a given memory hierarchy level i it has a technology-intrinsic access time of ti, The perceived access time Ti is longer than ti
Except for the outer-most hierarchy, when looking for a given address there is
  a chance (hit-rate hri) you “hit” and access time is ti
  a chance (miss-rate mri) you “miss” and access time ti + Ti+1
  hri + mri = 1
Thus
Ti = hri·ti + mri·(ti + Ti+1)
Ti = ti + mri ·Ti+1
hri and mri are defined to be the hit-rate and miss-rate of just the references that missed at Li-1

## Slide 43: Hierarchy Design Considerations
Recursive latency equation
Ti = ti + mri ·Ti+1
The goal: achieve desired Ti within allowed cost
Ti  ti is desirable, when we
  Keep mri low
    increasing capacity Ci lowers mri, but beware of increasing ti
    lower mri by smarter cache management (replacement::anticipate what you don’t need, prefetching::anticipate what you will need)
  Keep Ti+1 low
    faster lower hierarchies, but beware of increasing cost
    introduce intermediate hierarchies as a compromise

## Slide 44: Memory Bottleneck
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 45: Comparison of Latency: L1 of Intel CPU
Addr
Data
Memory
L2
L1
L1: 1 cycle
Really fast

## Slide 46: Comparison of Latency: L2 of Intel CPU
Addr
Data
Memory
L2
L1
L1: 1 cycle
Really fast
Memory
L2
L1
Addr
Data
Moderate
L2: 14 cycles

## Slide 47: Comparison of Latency: Memory of Intel CPU
Addr
Data
Memory
L2
L1
L1: 1 cycle
Really fast
Memory
L2
L1
Addr
Data
Moderate
L2: 14 cycles
Addr
Data
Memory
L2
L1
Extremely slow
Memory: 200 cycles

## Slide 48: Cache Basics and Operation
Notes: ISCA: international Symposium of cache architecture

## Slide 49: Cache
Any structure that “memorizes” frequently used results/data
  to avoid repeating the long-latency operations required to reproduce/fetch the results/data from scratch
  e.g., a web cache
Most commonly in the processor design context: an automatically-managed memory structure
  e.g., memorize in fast SRAM the most frequently or recently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency

## Slide 50: Blocks
Main memory logically divided into fixed-size chunks (blocks)
Cache can house only a limited number of blocks
Each block address maps to a potential location in the cache, determined by the index bits in the address
  used to index into the tag and data stores
8-bit address
tag
index
byte in block
3 bits
3 bits
2b

## Slide 51: Conceptual Picture of a Cache
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014
  https://people.inf.ethz.ch/omutlu/pub/memory-systems-introduction_computing-handbook14.pdf

## Slide 52: Cache Abstraction and Metrics
Cache hit rate = (# hits) / (# hits + # misses) = (# hits) / (# accesses)
Average memory access time (AMAT)
= ( hit-rate * hit-latency ) + ( miss-rate * miss-latency )
Important Aside: Is reducing AMAT always beneficial for performance?
Address
Tag Store
(Valid bit +
Address tag +
Replacement policy bits)
Data Store
(stores
memory
blocks)
Hit/miss?
Data
Notes: Reducing AMAT is not always beneficial for performance. The direct metric is instruction throughput, which might be orthogonal to latency.

## Slide 53: Addressing the Cache
Cache access:
  1) index into the tag and data stores with index bits in address;
  2) checks valid bit in tag store;
  3) compares tag bits in address with the stored tag in tag store;
  4) If a block is in the cache (cache hit), the stored tag should be valid and match the tag of the block, and read out data.

## Slide 54: A Toy Example for Cache
Toy example:
  256-byte memory,
     8-bit address
  64-byte cache, 8-byte blocks
     least significant 3 bits within a line
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014

## Slide 55: Caching Basics
Cache Block (line): Unit of storage in the cache
  Memory is logically divided into blocks that map to potential locations in the cache.
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    May have to evict some other block
For high cache hit rate, important cache design decisions:
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 56: Cache: Placement
A key question: How to map chunks of the main memory address space to blocks in the cache?
  Which location in cache can a given “main memory chunk” be placed in?

## Slide 57: Three Cache Organization Methods
Direct-mapped:
  A chunk can go to only one cache block in the cache. (Another extreme)
Fully-associative:
  A chunk can go to any cache block in the cache. (One extreme)
Set-associative:
  A chunk can go to N cache blocks in the N-way set-associative cache. (Best choice)
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014

## Slide 58: Direct-Mapped Cache: Placement and Access
Direct-mapped (A block can go to only one location)
  Assume memory: 256 bytes, 8-byte blocks  32 blocks
  Assume cache: 64 bytes, 8 blocks
  Blocks with same index contend for the same cache location
    Cause conflict misses when accessing blocks in green consecutively
Tag store
Data store
Address
tag
set
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main memory:

## Slide 59: Advantage and Issue of Direct-Mapped Caches
Direct-mapped cache:
  Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time.
    One index  one entry
Main advantage of direct-mapped cache:
  Easy to implement
Main issue of direct-mapped cache:
  Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
    Assume addresses A and B have the same index bits but different tag bits
    A, B, A, B, A, B, A, B, …  conflict in the cache index
    All accesses are conflict misses

## Slide 60: Three Cache Organization Methods
Direct-mapped:
  A chunk can go to only one cache block in the cache. (Another extreme)
Fully-associative:
  A chunk can go to any cache block in the cache. (One extreme)
Set-associative:
  A chunk can go to N cache blocks in the N-way set-associative cache. (Best choice)
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014

## Slide 61: Full Associativity
Fully-associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?
Address
tag
byte in block
3 bits
5 bits

## Slide 62: Advantage and Issue of Fully-associative Caches
Fully-associative cache:
  A block can be placed in any cache block.
Main advantage of fully-associative cache:
  Highly utilization of cache blocks (global view)
Main issue of fully-associative cache:
  Can lead to extremely difficult to implement when the number of cache blocks in the cache is large.
    Number of cache blocks in modern CPU reaches 32M/64=512K.
    Choosing one out of 512K cache lines is extremely costly.

## Slide 63: Three Cache Organization Methods
Direct-mapped:
  A chunk can go to only one cache block in the cache. (Another extreme)
Fully-associative:
  A chunk can go to any cache block in the cache. (One extreme)
Set-associative:
  A chunk can go to N cache blocks in the N-way set-associative cache. (Best choice)
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014
Notes: 相连

## Slide 64: 2-way Set-Associative Cache: Structure
Set-Associative Cache
  A block can be placed in any of N blocks of N-way set-associative cache
  Example of 2-way cache:
    Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address:
tag
set
byte in block
3 bits
2 bits
3 bits
Logic
MUX
MUX
byte in block
2-way SET
Hit?

## Slide 65: 4-way Set Associativity
4-way
  + Likelihood of conflict misses even lower
  -- More tag comparators and wider data mux; larger tags
Tag store
Data store
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?
Address
tag
set
bytes
3 bits
1 b
4 bits
V
tag
V
tag
V
tag
V
tag

## Slide 66: Set-Associative Cache: Advantage and Issue
Set-Associative Cache
  Key Idea: Associative memory within the set
Advantage of Set-Associative Cache
  Accommodates conflicts better (fewer conflict misses)
    Assume addresses A and B have the same index bits but different tag bits
    A, B, A, B, A, B, A, B, …  store in the cache set
    All accesses are cache hit
Issue of Set-Associative Cache
  More complex, slower access, larger tag store
How about in Deep Learning application？

## Slide 67: Associativity (and Tradeoffs)
Degree of associativity:
  How many blocks can map to the same index (or set)?
Higher associativity
  ++ Higher hit rate
  -- Slower cache access time (hit latency and data access latency)
  -- More expensive hardware (more comparators)
Diminishing returns from higher
  associativity
associativity
hit rate

## Slide 68: Memory Roofline Model
HBM GB/s
Memory Roofline Model:
  DRAM: limited memory bandwidth;
  HBM: medium memory bandwidth;
  Cache: large memory bandwidth
9
Peak Flop/s
Throughput (Flop/s)
DRAM GB/s
Arithmetic Intensity (Flop:Byte)
      Williams, Waterman, Patterson, “Roofline: An Insightful Visual Performance Model for Multicore Architectures”, CACM, 2009
Cache GB/s
Notes: All these works rely on many different methodology's to identify memory bottlenecks in a system. Often, such methodologies are intuitively used as a indication of NDP suitability for a given application
[CLICK] However, as I will show next, none of those models are comprehensive enough to identify memory bottlenecks and NDP suitability. This happens because these models are built targeting to identify specific sources of data movement bottlenecks, and often their definitions of compute and memory bound are not enough to indicate NDP suitability.
[CLICK] For that, we will analyze two commonly used approaches: the roofline model, which correlates the arithmetic intensity of an application with performance,
[CLICK] and identifying application that has high misses-per-kilo instructions or MPKI.
[NEXT]