## Slide 1: Computer Arch. & AI Chip Lecture 9: Cache and Cache Coherence
Prof. Zeke Wang
Zhejiang University
25 April 2025

## Slide 2: Recall: Memory Roofline Model
HBM GB/s
Memory Roofline Model:
  DRAM: limited memory bandwidth;
  HBM: medium memory bandwidth;
  Cache: large memory bandwidth
9
Peak Flop/s
Throughput (Flop/s)
DRAM GB/s
Arithmetic Intensity (Flop:Byte)
      Williams, Waterman, Patterson, “Roofline: An Insightful Visual Performance Model for Multicore Architectures”, CACM, 2009
Cache GB/s
Notes: All these works rely on many different methodology's to identify memory bottlenecks in a system. Often, such methodologies are intuitively used as a indication of NDP suitability for a given application
[CLICK] However, as I will show next, none of those models are comprehensive enough to identify memory bottlenecks and NDP suitability. This happens because these models are built targeting to identify specific sources of data movement bottlenecks, and often their definitions of compute and memory bound are not enough to indicate NDP suitability.
[CLICK] For that, we will analyze two commonly used approaches: the roofline model, which correlates the arithmetic intensity of an application with performance,
[CLICK] and identifying application that has high misses-per-kilo instructions or MPKI.
[NEXT]

## Slide 3: Recall: The Problem of Memory
Bigger is slower
  SRAM, 512 Bytes, sub-nanosec
  SRAM, KByte~MByte, ~nanosec
  DRAM, Gigabyte, ~50 nanosec
  PCM-DIMM (Intel Optane DC DIMM), Gigabyte, ~200 nanosec
  PCM-SSD (Intel Optane SSD), Gigabyte, ~10 µs
  Flash memory, Gigabyte~Terabyte, ~100 µs
  Hard Disk, Terabyte, ~10 millisec
Faster is more expensive (dollars and chip area)
  SRAM, < 0.3$ per Megabyte
  DRAM, < 0.03$ per Megabyte
  PCM-DIMM (Intel Optane DC DIMM), < 0.004$ per Megabyte
  PCM-SSD, < 0.001$ per Megabyte
  Flash memory, < 0.00008$ per Megabyte
  Hard Disk, < 0.00003$ per Megabyte

## Slide 4: Recall: The Memory Hierarchy
fast
small
large but slow
move what you use here
backup
everything
here
With good locality of reference, memory appears as fast as
and as large as
faster per byte
cheaper per byte

## Slide 5: Recall: Cache Abstraction and Metrics
Cache hit rate = (# hits) / (# hits + # misses) = (# hits) / (# accesses)
Address
Tag Store
(Valid bit +
Address tag +
Replacement policy bits)
Data Store
(stores
memory
blocks)
Hit/miss?
Data
Notes: Reducing AMAT is not always beneficial for performance. The direct metric is instruction throughput, which might be orthogonal to latency.

## Slide 6: Recall: Addressing the Cache
Cache access:
  1) index into the tag and data stores with index bits in address;
  2) checks valid bit in tag store;
  3) compares tag bits in address with the stored tag in tag store;
  4) If a block is in the cache (cache hit), the stored tag should be valid and match the tag of the block, and read out data.

## Slide 7: Recall: Three Cache Organization Methods
Fully-associative:
  A chunk can go to any cache block in the cache. (One extreme)
Direct-mapped:
  A chunk can go to only one cache block in the cache. (Another extreme)
Set-associative:
  A chunk can go to N cache blocks in the N-way set-associative cache. (Best choice)
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014

## Slide 8: Direct-Mapped Cache: Placement and Access
Direct-mapped (A block can go to only one location)
  Assume memory: 256 bytes, 8-byte blocks  32 blocks
  Assume cache: 64 bytes, 8 blocks
  Blocks with same set contend for the same cache location
    Cause conflict misses when accessing blocks in green consecutively
Tag store
Data store
Address
tag
set
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main memory:

## Slide 9: Full Associativity
Fully-associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?
Address
tag
byte in block
3 bits
5 bits

## Slide 10: 2-way Set-Associative Cache: Structure
Set-Associative Cache
  A block can be placed in any of N blocks of N-way set-associative cache
  Example of 2-way cache:
    Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address:
tag
set
byte in block
3 bits
2 bits
3 bits
Logic
MUX
MUX
byte in block
2-way SET
Hit?

## Slide 11: Where Are We?

## Slide 12: Caching Basics
Cache Block (line): Unit of storage in the cache
  Memory is logically divided into blocks that map to potential locations in the cache.
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    May have to evict some other block
For high cache hit rate, important cache design decisions:
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 13: Replacement in Set-Associative Caches
Key Challenge:
  Which cache block in a set be replaced once new block comes?

## Slide 14: Cache Block Replacement Policy
Which block in the set to replace on a cache miss?
  1, Any invalid block first
  2, If all are valid, consult the replacement policy:
    Random
    FIFO
    Least recently used (how to implement?)
    Hybrid replacement policies
    Optimal replacement policy?

## Slide 15: Implementing LRU
Idea: Evict the least recently accessed block
Problem: Need to keep track of access ordering of blocks
Question: 2-way set associative cache:
  What do you need to implement LRU perfectly?
Question: 4-way (or 16-way) set associative cache:
  What do you need to implement LRU perfectly?
Extremely challenging to implement LRU in hardware.
Notes: 2-way: use one bit to indicate
4-way: 3 bit
8-way: 7-bit.
8-way: 8路
Set-associative: 组相关

## Slide 16: Approximations of LRU
Most modern processors do not implement “true LRU” (also called “perfect LRU”) in highly-associative caches
Instead, approximate LRU is chosen. Why?
  True LRU is complex
  LRU is an approximation to predict locality anyway (i.e., not the best possible cache management policy)

## Slide 17: One Implementation of LRU
Pseudo LRU for 8-way set-associated cache:
  Assume 8 blocks (L0~L7) for a set, 7 rule bits (B0~B6).
  PLRU Replacement Way Selection: choosing the suitable way (L0~L7) based on the PLRU bits.
  PLRU Bits Updating Rule: updating PLRU bits after replacing the way (L0~L7).
PLRU Replacement Way Selection:
PLRU Bits Updating Rule:

## Slide 18: Cache Replacement Policy: LRU or Random
LRU vs. Random: LRU is not always better.
  Example: 4-way cache, cyclic references to A, B, C, D, E
    0% hit rate with LRU policy
Set thrashing: When the “program working set” in a set is larger than set associativity
  Random replacement policy is better when thrashing occurs
Which one is better in practice?
  Depends on workload
  Average hit rate of LRU and Random are similar
Best of both Worlds: Hybrid of LRU and Random
  How to choose between the two?
    Intel CPU uses the hybrid approach.

## Slide 19: What Is the Optimal Replacement Policy?
Belady’s OPT (Optimal Replacement)
  Replace the block that is going to be referenced furthest in the future by the program
  Belady, “A study of replacement algorithms for a virtual-storage computer,” IBM Systems Journal, 1966.
  How do we implement this? Simulate?
    No possibility to implement in theory.
    Lots of potential in practice
Notes: Application knows…

## Slide 20: Caching Basics
Cache Block (line): Unit of storage in the cache
  Memory is logically divided into blocks that map to potential locations in the cache.
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    May have to evict some other block
For high cache hit rate, important cache design decisions:
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: write-allocate, write-back/write-through
  Instructions/data: do we treat them separately?

## Slide 21: Cache Policies: Handling Memory Write
Where should you write the result of a store? One policy for each step.
  Step 1: store insn.  cache, either policy works:
    Write-allocate policy (memory, default):
      Allocate the cache line (put it in the cache).
      Issue: Read an entire cache block from memory
    Write-no-allocate policy (PCIe/IO):
      Write it directly to memory without allocation in cache.
      Ignore cache.
  Step 2: cache  memory, either policy works:
    Write-back policy (default):
      Writes it to the cache and wait until the cache kicks the cache block out
    Write-through policy (streaming write instruction):
      Writes it to the cache and memory right away
Notes: 4 combinations…

## Slide 22: Cache: Write-back vs. Write-through
  Write-back:
    Write goes to cache; cache writes to main memory (evicted)
    + Can combine multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through:
    Write goes to memory and cache
    + Simpler
    + Evictions do not need to write to memory
    + All levels are up to date
    Consistency: Simpler cache coherence because no need to check close-to-processor caches’ tag stores for presence
    -- More memory bandwidth intensive; no combining of writes

## Slide 23: Caching Basics
Cache Block (line): Unit of storage in the cache
  Memory is logically divided into blocks that map to potential locations in the cache.
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    May have to evict some other block
For high cache hit rate, important cache design decisions:
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 24: Instruction vs. Data Caches
Core question: Separate or Unified?
Pros and Cons of Unified Cache:
  + Dynamic sharing of cache space: no overprovisioning that might happen with static partitioning (i.e., separate I and D caches)
  -- Instructions and data can thrash each other (i.e., no guaranteed space for either)
  -- I and D are accessed in different places in the pipeline. Where do we place the unified cache for fast access?
Modern CPU:
  First level caches are almost always split
  Higher level caches are almost always unified

## Slide 25: Classification of Cache Misses
Compulsory miss
  Defined as the first reference to an address (block), always resulting in a miss
Capacity miss
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
  Cause: cache is too small to hold everything needed
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss
Notes: Miss:缺失

## Slide 26: How to Reduce Each Miss Type
Compulsory miss
  Caching cannot help
  Prefetching can: Anticipate which blocks will be needed soon
Conflict miss
  More associativity
  Other ways to get more associativity without making the cache associative
    Victim cache
    Better, randomized indexing
    Software hints?
Capacity miss
  Utilize cache space better: keep blocks that will be referenced
  Software management: divide working set and computation such that each “computation phase” fits in cache

## Slide 27: Cache Performance

## Slide 28: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 29: How to Improve Cache Performance
Three fundamental goals
  Reducing miss rate
    Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
  Reducing miss latency or miss cost
  Reducing hit latency or hit cost
The above three together affect performance

## Slide 30: Cache Terminology
Capacity (C):
  the number of data bytes a cache stores
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 31: Cache Organization Recap
Main Parameters
  Capacity: C
  Block size: b
  Number of blocks in cache: B = C/b
  Number of blocks in a set: N
  Number of Sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1
31

## Slide 32: How is data found?
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by number of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks are in a single set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)

## Slide 33: Direct Mapped Cache

## Slide 34: Direct Mapped Cache Hardware

## Slide 35: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
35

## Slide 36: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15 = 20%
Temporal Locality Compulsory Misses
36

## Slide 37: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
37

## Slide 38: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10 = 100%
Conflict Misses
38

## Slide 39: N-Way Set Associative Cache

## Slide 40: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
40
Notes: N路组相关映射

## Slide 41: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces conflict misses
41

## Slide 42: Cache Size
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 43: Block Size
Block size is the data that is associated with an address tag
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and bandwidth/energy
  if spatial locality is not high
hit rate
block
size

## Slide 44: Associativity
How many blocks can be present in the same index (i.e., set)?
Larger associativity
  lower miss rate (reduced conflicts)
  higher hit latency and area cost (plus diminishing returns)
Smaller associativity
  lower hit rate
  lower cost
  lower hit latency
    Especially important for L1 caches
associativity
hit rate

## Slide 45: Cache in a Multi-Core CPU

## Slide 46: Recall: Multi-Core over Large Superscalar
Technology push
  Instruction issue queue size limits the cycle time of the superscalar, OoO processor  diminishing performance
    Quadratic increase in complexity with issue width
  Large, multi-ported register files to support large instruction windows and issue widths  more resources, reduced frequency or longer RF access, diminishing performance
Application pull
  Multiple applications run together on your CPU
Olukotun et al., “The Case for a Single-Chip Multiprocessor,” ASPLOS 1996.
Notes: What does application pull mean?

## Slide 47: Challenge from Multi-core CPU
Cache is needed to relieve the negative effect of long memory latency.
How to design cache for multiple cores?
  Cores want a consistent view of memory.
Notes: What does application pull mean?

## Slide 48: Caches in a Multi-Core System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 49: Caches in Multi-Core CPU
Cache efficiency becomes even more important in a multi-core/multi-threaded system
  Memory bandwidth is at premium
  Cache space is a limited resource across cores/threads
How do we design the caches in a multi-core system?
Many decisions:
  Shared vs. private caches
  How to preserve coherence and consistence?
Notes: Premium:

## Slide 50: Private vs. Shared Caches
Private cache:
  Cache belongs to one core (a shared block can be in multiple caches)
Shared cache:
  Cache is shared by multiple cores.
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 51: Resource Sharing Concept and Advantages
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, data shared between multiple threads can be kept in the same cache in multithreaded processors
+ Compatible with the shared memory programming model

## Slide 52: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 53: Shared Caches Between Cores
Advantages:
  High effective capacity
  Dynamic partitioning of available cache space
    No fragmentation due to static partitioning
    If one core does not utilize some space, another core can
  Easier to maintain coherence (a cache block is in a single location)
Disadvantages
  Slower access (cache not tightly coupled with the core)
  Cores incur conflict misses due to other cores’ accesses
    Misses due to inter-core interference
    Some cores can destroy the hit rate of other cores
  Guaranteeing a minimum level of service (or fairness) to each core is harder (how much space, how much bandwidth?)

## Slide 54: Caches in Multi-Core CPU
Cache efficiency becomes even more important in a multi-core/multi-threaded system
  Memory bandwidth is at premium
  Cache space is a limited resource across cores/threads
How do we design the caches in a multi-core system?
Many decisions:
  Shared vs. private caches
  How to preserve coherence and consistence?
Notes: Premium:

## Slide 55: Memory Consistency vs. Cache Coherence
Coherence is about ordering of operations from different processors to the same memory location
  Local ordering of accesses to each cache block
Consistency is about ordering of all memory operations from different processors (i.e., to different memory locations)
  Global ordering of accesses to all memory locations
Notes: Coherence;一致性
Consistency:连贯性

## Slide 56: Cache Coherence

## Slide 57: Features of Cache Coherence
Cache Coherence: Multiple cores have a consistent state of the last written value from any core to a memory address.
  Program order preservation: core C writes to the address and then reads from the same address, C gets value written.
  Coherent memory view: if C1 performs “mem[X] = 1”, after a sufficient time, C2 will read 1 from “mem[X]”.
  Write serialization: writes to the same address by different processors are seen in same order by all processors.
C
Memory
Write 1
Read 1
C1
Memory
Write 1
Read 1
C2
C1
Memory
Write 1
Write 2
C2

## Slide 58: Hardware Architecture for Cache Coherence
Hardware architecture for Cache Coherence:
  Cores, caches, interconnect, memory work together to achieve cache coherence from core’s point of view.
    Cache Tags: MESI (CPU action  Bus action, Tags)
    Cache Updating: invl./update (Bus action)
    Interconnect: Bus/Switch
Core
Interconnection Network
Main Memory
Core
Core
Cache
Interconnect
Memory
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
R: read
W:write
I: invalidate
U: update

## Slide 59: Cache Coherence: Interconnect
Cache Interconnect: cores communicate with each other.
  Bus:
    One valid at a time
    Typically used by Snooping
  Switch:
    Peer-to-peer communication
    Typically used by directory
Core
Interconnect network
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Dict.
Dict.
Notes: 大三有很多课，假如10门课，你跟你室友都选了人工智能芯片与系统专业课，这样人工智能专业课的信息大家有兴趣去了解（update比较好）；但有选修课，不是所有人都选了，这个时候update就不好，invalidate就比较好。

## Slide 60: Cache Interconnect: Bus-based Protocol
Core
Bus (One trans. a time)
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Bus-based protocol:
  1, A cache arbitrates for bus access, waiting until 2 happens
  2, A cache is granted bus access
  3, A cache places command on bus, waiting until 4 happens
  4, Other caches place responses on bus

## Slide 61: Cache Interconnect: Switch-based Protocol
Core
Switch (P2P)
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Switch-based protocol:
  Each core pair can independently communicate with each other.

## Slide 62: Cache Coherence: Cache Updating
Hardware architecture for Cache Coherence:
  Cores, caches, interconnect, memory work together to achieve cache coherence from core’s point of view.
    Cache Tags: MESI (CPU action  Bus action, Tags)
    Cache Updating: invl./update (Bus action)
    Interconnect: Bus/Switch
Core
Interconnection Network
Main Memory
Core
Core
Cache
Interconnect
Memory
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
R: read
W:write
I: invalidate
U: update

## Slide 63: Cache Coherence: Updating Policy
Cache Updating Policy: safely update replicated data in other caches.
  Update Protocol:
    Push a update command (bus action) to all copies
  Invalidate Protocol:
    Ensure only one local copy by sending out an invalidation command (bus action), then update the local copy
Core
Interconnect network
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Dict.
Dict.
Notes: 大三有很多课，假如10门课，你跟你室友都选了人工智能芯片与系统专业课，这样人工智能专业课的信息大家有兴趣去了解（update比较好）；但有选修课，不是所有人都选了，这个时候update就不好，invalidate就比较好。

## Slide 64: Bus Action: Update vs. Invalidate
Where and When: On a bus action write miss:
1, Update Protocol:
  Broadcast written data and address to cores
  Cores update the data in their caches if block is present
2, Invalidate Protocol:
  Broadcast invalidation of address to sharers
  Cores invalidate block in their caches if block is present

## Slide 65: Tradeoffs: Update vs. Invalidate
Which do we want?
  Write frequency and sharing behavior are critical
Update Protocol
  + If sharer set is constant and updates are infrequent, avoids the cost of invalidate-reacquire (broadcast update pattern)
  - If data is rewritten without intervening reads by other cores, updates would be useless
  - Write-through cache policy  bus becomes bottleneck
Invalidate Protocol
  + After invalidation broadcast, core has exclusive access rights
  + Only cores that keep reading after each write retain a copy
  - If write contention is high, leads to ping-ponging (rapid invalidation-reacquire traffic from different processors)
Notes: Invalidate Protocol is main stream.

## Slide 66: Cache Coherence: Cache Tags
Hardware architecture for Cache Coherence:
  Cores, caches, interconnect, memory work together to achieve cache coherence from core’s point of view.
    Cache Tags: MESI (CPU action  Bus action, Tags)
    Cache Updating: invl./update (Bus action)
    Interconnect: Bus/Switch
Core
Interconnection Network
Main Memory
Core
Core
Cache
Interconnect
Memory
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
R: read
W:write
I: invalidate
U: update

## Slide 67: Cache Coherence: Cache Tags
MSI Protocol: safely update replicated data in caches (goal).
  I(nvalid): block is not in cache, need to fetch from memory or other cache
  S(hared): in >=1 caches, clean, local cores can read it w/o bus action
  M(odified): in 1 cache, core can read/write it w/o bus action
Core
Bus (one trans. A time)
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Notes: 大三有很多课，假如10门课，你跟你室友都选了人工智能芯片与系统专业课，这样人工智能专业课的信息大家有兴趣去了解（update比较好）；但有选修课，不是所有人都选了，这个时候update就不好，invalidate就比较好。

## Slide 68: State Diagrams for CPU Requests
I
S
M
Core read miss
Read miss on bus
Core write miss
Write miss on bus
Core read hit
Core read hit
Core write hit
Core write hit
Invalidate on bus
Core memory read/write  Cache states, Bus action:
Miss in local cache
Hit in local cache
Bus action (Outside)  Cache states:
Invalidate
Write miss
Read miss
CPU action
Bus action
Cache blocks
Tags
Bus actions affects the overall performance of multi-core CPU.
Core
Starter

## Slide 69: State Diagrams for Bus Requests
I
S
M
Core read miss
Read miss on bus
Core write miss
Write miss on bus
Core read hit
Core read hit
Core write hit
Core write hit
Invalidate on bus
Core memory read/write  Cache states, Bus action:
Miss in local cache
Hit in local cache
Bus action (Outside)  Cache states:
Invalidate
Write miss
Read miss
I
S
M
Invalidate/Write miss
Read miss
Bus action
Cache blocks
Tags
Read miss
Cache response
Write back block to requesting cache and memory
Write miss
Write back block to requesting cache and memory
Bus actions affects the overall performance of multi-core CPU.
Cache
Starter

## Slide 70: The Problem with MSI
A block is not in cache at the beginning. On a read, the block immediately goes to the “Shared” state.
Problem: The core issues a bus action invalidate before writing the block to cache, even when only one cache copy exists.
Time | P1 op. | P2 op. | State A in P1 | State B in P2 | Bus action
t0 |  |  | I | I | 
t1 | Read A |  | S | I | Read miss A
t2 | Write A |  | M | I | Invalidate
t3 |  | Read B | M | S | Read miss B
t4 |  | Write B | M | M | Invalidate

## Slide 71: MESI Protocol
MESI Protocol: Illinois protocol (ISCA, 84)
  I(nvalid): block is not in cache, need to fetch from memory or other cache
  S(hared): in >1 caches, clean, local cores directly reads it w/o bus action
  M(odified): in 1 cache, local core can read/write it w/o bus action
  E(xclusive): in 1 cache, clean, local core reads/writes it w/o bus action
Key Differences from MSI Protocol:
  Local core reads block in state E, the state holds
  Local core writes block in state E  state M, without bus action
  Remote core reads, via read miss on bus, block in state E  state S
  Remote core writes, via write miss on bus, block in state E  state I
    Papamarcos, “A low-overhead coherence solution for multiprocessors with private cache memories,” ISCA 1984.
Notes: 大三有很多课，假如10门课，你跟你室友都选了人工智能芯片与系统专业课，这样人工智能专业课的信息大家有兴趣去了解（update比较好）；但有选修课，不是所有人都选了，这个时候update就不好，invalidate就比较好。

## Slide 72: MESI over MSI
Time | P1 op. | P2 op. | State A in P1 | State B in P2 | Bus action
t0 |  |  | I | I | 
t1 | Read A |  | S | I | Read miss A
t2 | Write A |  | M | I | Invalidate
t3 |  | Read B | M | S | Read miss B
t4 |  | Write B | M | M | Invalidate
MSI:
Time | P1 op. | P2 op. | State A in P1 | State B in P2 | Bus action
t0 |  |  | I | I | 
t1 | Read A |  | E | I | Read miss A
t2 | Write A |  | M | I | 
t3 |  | Read B | M | E | Read miss B
t4 |  | Write B | M | M | 
MESI:

## Slide 73: Sophisticated Cache Coherence Protocols
Intel i7: MESIF
  F: forward (read from remote shared instead of memory)
AMD: MOESI
  O: owned (read from remote shared instead of memory)
The protocol can be optimized with more states and prediction mechanisms to
  + Reduce unnecessary invalidates and transfers of blocks
However, more states and optimizations
  -- Are more difficult to design and verify (lead to more cases to take care of, race conditions)
  -- Provide diminishing returns
Notes: 这个方向的研究没啥意义。

## Slide 74: Cache Coherence Protocols
Core
Bus (one trans. A time)
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Cache Coherence
  Snoop: [Goodman ISCA 1983]
    Bus-based, each bus action broadcasts on the bus, one action at a time.
    Each to implement
    Single point of serialization for all memory requests.

## Slide 75: Snoop-Based Cache Coherence

## Slide 76: Cache Snoop Protocol
Core
Bus (One trans. a time)
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Snoop: [Goodman ISCA 1983]
    Single point of serialization for all memory requests
    One outstanding memory request per processor
    System interconnect is an atomic shared bus (one cache communicates at a time)

## Slide 77: Example: How Snoop/Direct Works?
C2
Interconnect
C1
C4
C3
X:
X: I
I
X: S
X: S
…
Initial states:
  X is only shared by C3 and C4
Operations:
  C1:X=888
  C3: reads X

## Slide 78: How Snoop Works? (C1: X = 888)
C1(local) Bus C3(remote) C4(remote) …
GetEx X
Invalidate X
Invalidate X
Ack
Reply X=111
C2
C1
C4
C3
X:
X: S
X: I
X: S
M, 888
I
X: I
X: I
X = 888
…
Bus (One transaction active at a time)
Notes: Bus also broadcasts to C2…

## Slide 79: How Bus Works? (C3 reads X)
GetS X
Reply X=888
C2
Bus (One transaction active at a time)
C1
C4
C3
X:
X: S
X: I
M, 888
S, 888
X: I
X: I
…
GetS X
C1(M) Bus C3(local) C4(remote)
Write X to memory
GetS X
Ack

## Slide 80: Why Needing a Bus?
Ordering
  Bus serializes requests, ordering some before others.
  However: coherence does not require ordering of requests to different address.
Communication
  Simple, fast broadcast medium
  However: coherence does not require broadcast
    Only need to communicate with sharers
    Observation: most data is not shared by every cache.

## Slide 81: Cache Coherence Protocols
Cache Coherence
  Snoop: [Goodman ISCA 1983]
    Bus-based, each bus action broadcasts on the bus, one action at a time.
    Single point of serialization for all memory requests.
  Directory:[Censier, ToC 1978]
    Cores make explicit requests for blocks
    Directory tracks which caches have each block
    Directory coordinates invalidation and updates
    Single point of serialization per block, distributed among nodes
    Long processing latency
Core
Switch (peer to peer)
Main Memory
Core
CPU action
Bus action
CPU action
Bus action
Cache blocks
Tags
Cache blocks
Tags
Dict.
Dict.

## Slide 82: Directory-Based Cache Coherence

## Slide 83: Directory Based Coherence: Goal and Idea
Goal: address the lack of scalability of snooping protocols.
  All-to-all broadcast will not scale
Idea: A logically-central directory keeps track of where the copies of each cache block reside. Caches consult this directory to ensure coherence.
  Coherence still requires single point of serialization (for write serialization)
  Serialization location can be different for every block (striped across nodes/memory-controllers)

## Slide 84: Directory: Node Definition
Cache
Regarding a cache block:
  Home Node: the node owns the corresponding directory, each cache block can have different home node.
  Local Node: the node initiates the cache read/write requests
  Remote Node: the node passively responses to the action from the home node
C2
Switch (peer to peer)
Cache
C1
Cache
C4
Cache
C3
…

## Slide 85: Directory: Basic Operations
Local node:
  On a bus read: send out getS request to directory node, after receiving the data, set the cache’s bit.
  On a bus write: send out getEx request to directory node
    invalidate all caches that have the block and reset their bits
    Have an “exclusive bit” associated with each block in each cache
Directory node:
  1, Receives getS, getEx requests from nodes
  2, Based on different cache states:
    2a, Sends Invalidate messages to sharers if needed
    2b, Forwards request to memory if needed
  3, Replies to requestor and updates sharing state
Notes: Protocol design is flexible
  Exact forwarding paths depend on implementation
  For example, do cache-to-cache transfer?

## Slide 86: Directory for Each Cache Line
Detailed directory for each cache line:
  Each cache block needs N+log2N + 2 bits for its directory, which resides at the home node.
    2-bit cache states: a block is owned by the directory unless the block is in a cache in state M. State M means a node writes to it.
    One shared bit for each cache: indicating whether the block is shared in a cache
    log2N owner bit: indicates that the cache that has the only copy of the block and can update it without notifying others
states | Owner | Sharer list (one-hot bit vector)
2-bit log2N-bit N-bit

## Slide 87: How Directory Works?
C2
Switch (peer to peer)
C1
C4
C3
X:
X: S{C3, C4}
I
X: S
X: S
…
Initial states:
  Directory stays in C2
  X is only shared by C3 and C4
Operations:
  C1:X=888
  C3: reads X

## Slide 88: How Directory Works? (C1: X = 888)
C1(local) C2(home) C3(remote) C4(remote)
GetEx X
Invalidate X
Invalidate X
Ack
Ack
Reply X=111
C2
Switch (peer to peer)
C1
C4
C3
X:
X: S
X: S{C3, C4}
X: S
M, 888
I
X: I
X: I
X: E{C1}
X = 888
…

## Slide 89: How Directory Works? (C3 reads X)
GetS X
Ack
Reply X=888
C2
Switch (peer to peer)
C1
C4
C3
X:
X: S
X: S{C1, C3}
M, 888
S, 888
X: I
X: I
X: E{C1}
…
Fwd-GetS X to C1
C1(owned) C2(home) C3(local) C4(remote)
Write X to memory